## Slide 1
Yan Xiaofei
IHEP-CC
BEIJING-LCG2 & NGI_CHINA Report

## Slide 2: OutLine
IHEP Computing Center
Grid Computing BEIJING-LCG2
Tier2 & Tier3
Internet connections & Security
Contact

## Slide 3: IHEP computing center Infrastructure
~19000 CPU cores
Water cooling
6PB tape library
Power supply system
10PB disk space
ATLAS, CMS, LHCb, BESIII, JUNO, DYB, CEPC, HEPS, LHAASO, ARGO, HXMT, …

## Slide 4: Cluster & Storage Service Topology
Lustre
9PB
DPM
735TB
dCahce
540TB
Castor 6PB
Local Cluster
15000 Cores
Grid PBS Cluster
1896 Cores
Part of the luster and gluster data have backup in Castor, usually user data, some experiment data
Cloud Cluster
2000 Cores
Gluster
350TB
Login Nodes
Local User
Grid User
Dirac
EOS
1240TB
UMD

## Slide 5: Computing Resource Usage
Resource Usage：95.8%

## Slide 6: Grid computing for LHC
WLCG is consists of 1 Tier0, 11 Tier1s, over 100 Tier2s
Raw data generated at Tier0, distributed to Tier1s
Reconstructed data generated at Tier1s, transfer back to Tier0, and distributed to Tier2
Analyzed data generated at Tier1/Tier2s, transfer back to Tier1s and Tier0

## Slide 7: BEIJING-LCG2 GRID Site Services
CNIC
VM
UI
APEL
Vobox
MyProxy
dCache
Poolnode
Poolnode
Poolnode
Poolnode
Poolnode
DPM
Poolnode
Poolnode
Poolnode
Poolnode
Poolnode
Cream CE
Torque
ArcCEs
WN
WN
WN
WN
WN
WN
WN
WN
WN
WN
WN
WN
WN
WN
WN
WN
Frontire-Squid
LFC
BDII
Worknodes
Disk nodes
10Gb Eth
1Gb Eth
Beijing_ERA_Mcore
BEIJING-TIANJIN-TH-1A_MCORE

## Slide 8: BEIJING-LCG2 Tier2 Resources
Grid Site(WLCG)
  CPU: 1896 Cores
    Intel Golden 6140: 1008 Cores (New for LHCb)
    Intel E2680V3: 696 Cores (2015)
    Intel X5650: 192 Cores(2011) Very Old
ATLAS: BEIJING-LCG2
  Total 400TB (2014)
  4TB X 24slots With Raid 6
CMS: T2_CN_BEIJING
  Total: 540TB(2014)
  4TB X 24slots With Raid 6. 8 Array box.
  3TB X 24slots With Raid 6. 1 Array box.
LHCb: LCG.BEIJING.CN
  Total 375TB (2018)
  8TBX60 slots DELL MD3860
Chart: CPU(HEP-SPEC06)
| 2008.0 | 2012.0 | 2013.0 | 2014.0 | 2015.0 | 2018.0
Pledged | 2000 | 9600 | 9600 | 9600 | 11560 | 16000
Offered | 3500 | 10640 | 10640 | 10640 | 16322 | 35600
Chart: DISK(Tbytes)
| 2008.0 | 2012.0 | 2013.0 | 2014.0 | 2015.0 | 2018.0
Pledged | 400 | 640 | 640 | 640 | 640 | 940
Offered | 400 | 640 | 640 | 800 | 940 | 1315

## Slide 9: BEIJING-LCG2 Volunteer Computing
ATLAS@home on Beijing Site
  Number of jobs : 122,383 (2018.1.1 ~ now)
  HS06 Days : 550,760 (2018.1.1 ~ now)
CEPC@home project in progress
  Experience from ATLAS@home applied
  VM wrapper is adopted
  BOINC validator & assimilator in development
Number of Jobs
HS06 resources

## Slide 10: BEIJING-LCG2 Tier2 Operations
Adding support for LHCb.
Upgrade service to Centos7
  Develop auto configuration modules for C7.
  Upgrade DPM storage element to new version.
Testing new computing element and Batch system.
  ARCCE
  HT-Condor-CE
Tier2 site auto deployment(puppet modules)
  https://github.com/yyxfei/emiconfig

## Slide 11: Tier3 Resource
IHEP-CC
ATLAS
  CPU: E5430(2008, 128), E5-2660(2012, 192),E5-2650v2(2014,256):
  576 cores
  Storage: 277TB +630TB(2018)
    4TB X 24 slots With Raid 6;
    3TB X 24 slots With Raid 6;
    10TBX84 slots DELL ME4084
CMS
  CPU: E5430(2008,128), E5-2650v2(2014,256)
  384 cores
  Storage: 493TB
    4TB X 24 slots With Raid 6;
LHCb
  CPU: GOLD 6140(2018, 72): 72 cores
  Total 375TB (2018)
  8TBX60 slots DELL MD3860(2018)
USTC-T3 (ATLAS)
CPU: 1088 cores (2176 HT on)
Storage: 2.0PB
  /lustre 621 TB
    Shared with USTC-T3 (Storage Element)
    DELL R720 + MD1200.
  /ustcfs 1300TB
    DELL R630 + SC2080

## Slide 12: Tier3 remote management
Remote Distribute Deployment
  OS and software auto installation
  Software auto configuration
  Some operations need hardware support
CentXman
Foreman
USTC
PKU
Puppet
LHAASO
BUAA
Remote Distribute Monitoring
  Auto notification with SMS
  Auto notification with WeChat
  Auto notification with email

## Slide 13: Tier2 & Tier3
Tier2 For Production users. Tier3 For local users.
Tier2
Data Disk
CPU
Tier3
Disk
CPU
For Production User
Monitored
Other Sites
DataSet
OR Files
User Disk
Grid User
Transfer Data With RUCIO or PhEDEx
RUCIO,
SRM,GFAL

## Slide 14: NGI_CHINA
National Grid Initiatives or Infrastructures
  Set up by individual countries to manage the computing resources.
  Reginal operation center of EGI
  Central of the China LHC computing.
Contributes a number of sites to the grid infrastructure.
  BEIJING-LCG2
    Only one running tier2 in china mainland
    Good Reliability for many years.
    Main gate to share data from CERN and other laboratory.
  HK-LCG2
  USTC-T3
  Others were deprecated
Support For Tier2 operations

## Slide 15: Internet Connections
IHEP-USA(Internet2)
  IHEP-CSTNet-CERNET-USA
  Bandwidth: 10Gbps
IHEP-EUR(GEANT)
  IHEP-CSTNet-CERNET-LONDON-Euro
  Bandwidth: 10Gbps
IHEP-Asia(HK & TOKYO)
  IHEP-CSTNet-HONGKONG-Asia
  Bandwidth: 10Gbps
  IHEP-*.edu.cn
  IHEP-CSTNet-CERNET-University
  Bandwidth：10Gbps
Notes: 国际国内链路；
1、（加入lhc1 qfz），进展情况；
2、中欧链路问题；

## Slide 16: LHCONE
Introduction
  Provide a collection of access locations that are effectively entry points into a network that is private to the LHC T1/2/3 sites.
The Progess
  CERNET and CSTNET joined LHCONE at Feb 2018
  IHEP joined LHCONE at Mar 2018
    Individual router equipment
    New physical link for Ipv4 and ipv6 2*10G
Problems
  Ipv6 asymmetric routing between CERN and IHEP
  More routing info ought to be learned

## Slide 17: LHCONE
LHCONE IPv6 traffic
LHCONE IPv4 traffic

## Slide 18: Security
China Cyber Security Federation For HEP(CSFHEP)
  cooperated to deal with security incident
  share threat information, technology and expertise
  help site system administrators with workshops/trainings
  communicate/cooperate with HEP security teams outside China, and security teams outside HEP community

## Slide 19: Locations of Members

## Slide 20: BEIJING-LCG2 Tier2 Issues
Lack of funding support.
  All hardware are very old except for LHCb.
  Lack of man power.
    1 for Tier2 site operations, one for each experiments.
  Need support from experiment.
Network
  Not very stabile. Lots of Internet interrupt and maintenance.
  Timeout when transfer large files.
Pressures from Experiment
  Need more resource, for atlas: 0.5% Atlas total storage. Ie 400TB today, 600TB in 2020(+15%)

## Slide 21: Contact information
Tier2 Site operations and grid service deployment
  Xiaofei Yan: yanxf@ihep.ac.cn
ATLAS
  Xiaofei Yan: yanxf@ihep.ac.cn
CMS
  Xiaomei Zhang: zhangxm@ihep.ac.cn
LHCb
  Xiaowei Jiang: jiangxw@ihep.ac.cn
  Xiaofei Yan: yanxf@ihep.ac.cn

## Slide 22: Summary
Only one running well Tier2 WLCG grid site in China mainland.
Reginal operation center of WLCG grid computing.
Atlas@home contribute more cpus to Atlas computing.
Network: Good connections to Internet, but not very stable.
Security: China Cyber Security Federation For HEP(CSFHEP).
Lake of funding support on infrastructure and manpower.

## Slide 23
Thanks