## Slide 1: R&D on thin gap RPC for ATLAS Phase-II upgrade
Yongjie Sun
State Key Laboratory of Particle detection and electronics
Department of Modern Physics,
University of Science and Technology of China (USTC)

## Slide 2
Outline
Introduction
RPC Simulation – gas amplification & signal induction
Prototype test – readout board & two-end readout method
Summary and outlook

## Slide 3: Introduction
L=7×1034cm-2s-1@14TeV
Trigger RPC @ High Luminosity LHC
Exceed their service time (10 years @ LHC)
Rate capability limited: 20 Hz/cm2
Work under lower voltage  15-35% eff. Lost
The solution
Add BI RPC layers (3 RPCs)
  Additional overall redundancy
  Additional overall lever arm
  Additional acceptance
Improved performance:
  rate, longevity, time & spatial resolution.
9 layers instead of 6
4 chambers instead of 3

## Slide 4: Requirements on RPC detector
Higher rate capability: ~ kHz/cm2
Longer longevity: 10 years of HL-LHC
Higher spatial resolution: ~ cm
Higher time resolution: ~0.5ns
Reduced gap size:
  Less charge produced per event  improve longevity, rate capability
  Less high voltage applied but higher field  better time resolution
Reduced bakelite thickness:
  Less voltage loss in bakelite  improve the rate capability
New generation FE electronic:
  Higher amplification factor and high S/N ratio to compensate the less gas amplification.
Improved readout panel and method
  Better mechanics structure, better signal transmission and better spatial resolution.
Front-End board
strips
GND
Forex-board
RPC gas gap
Gap size: 2mm1mm
Bakelite: 1.8mm1.2mm

## Slide 5: Main challenges
More sensitive, high signal-to-noise ratio, fast, low power consumption Front End Electronics.
Increasing the signal-to-noise ratio by optimizing the gas gap and readout panel structure.  impedance, cross talk, shielding, …
New materials for a thinner and more rigid chamber structure
Optimizing the detector design to maximize spatial and time resolution, for example, the two-end readout method.

## Slide 6: RPC detector simulation
Gas amplification simulation by Garfield++
Better understanding the working mechanism
Guide the detector design and optimization
Comparable results achieved to the experimental test.
experimental
simulated
5000V
5800V
5600V
5400V
Time resolution
Signal width
Signal charge distribution

## Slide 7: RPC detector simulation
Signal induction and transmission by CST PCB studio
Simulated causes relate to the “cross-talk”
Predict the high cluster size caused by the low surface resistivity of HV layer
Results have been used to optimize the BIS7/8 RPC production
simulation
1 kΩ/□
120 kΩ/□
100 kΩ/□
620 kΩ/□
Test results

## Slide 8: Readout panel design
Main considerations:
  Impedance matching: dielectric constant (εr) ↓, S ↓, d ↑,  smaller capacitor
  Light and good mechanic properties
Foam-like material: mainly air inside, εr close to 1.
But, foam board is very fragile and not stiff.
Honeycomb board
  “empty” structure inside: low εr and light
  Hard and stiff, very good mechanic performance.

## Slide 9: Honeycomb readout board
2 layers of PCB as readout strip and ground
~2 mm honeycomb plate as medium
Characteristic impedance: 18.5 ohm
Used in the two-end readout test

## Slide 10: Two-end readout method
Current structure
Two readout layers in two directions, η & φ
Single-end readout on each layer.
Spatial resolution: strip pitch
Two-end readout:
One readout layer in one direction, φ
Φ position: time difference from two ends
Save electronics channels and space.
strips
honeycomb-board
RPC gas gap

## Slide 11: Signal speed along strip
16 channels readout
Gas gap1 and readout panel1
Gas gap2 and readout panel2
8 channels
8 channels
Gap 2 and panel 2 is used to reconstruct the hit position with the fired strip.
Gap1 and panel 1, readout from two ends, the time difference (T_diff) is related to the hit position.
Very linear correlation observed between T_diff and hit channel.
The signal transmission speed achieved with the fitted slope.
1/v = [slope=2.87ns]/(2.7cm*2)
= 53 ps/cm
Correlation between the reconstructed position
RPC1
RPC2
Scintillator1
Scintillator2
Trigger area:
40cm*20cm

## Slide 12: Spatial resolution measurement
Series 3 and 4
Series 1 and 2
V1742 digitizer
RPC1
RPC2
Scintillator1
Scintillator2
Muon
Series1
Series4
Series2
Series3
Gas gap
Back End
Front End
Readout panel made by honeycomb
Two honeycomb panels on two gas gaps
with two-end readout

## Slide 13: System setup
Front End
Back End

## Slide 14: Reconstructed position
Gas gap1
Gas gap2
Position correlation between 2 gas gaps
Red line:
40 cm trigger area.

## Slide 15: Spatial resolution
NO. NAME VALUE ERROR
1 Constant 1.44985e+03 2.88736e+01
Mean 3.96725e-02 3.46177e-03
Sigma 2.15601e-01 2.56307e-03
NO. NAME VALUE ERROR
Constant 8.67033e+02 1.74151e+01
Mean 1.67119e-01 6.05049e-03
Sigma 3.58737e-01 4.55105e-03
Difference of Time_Diff (cross threshold)[ns]
Difference of Time_Diff (half_peak)[ns]
v = 18.78 cm/ns
Spatial resolution = 1.43 cm
Spatial resolution = 2.39 cm
Peak time: Spatial resolution: 1.74 cm

## Slide 16: Time resolution
NO. NAME VALUE ERROR
1 Constant 3.38852e+03 2.31866e+01
2 Mean -2.53700e-01 4.94975e-03
3 Sigma 8.18264e-01 3.82034e-03
NO. NAME VALUE ERROR
1 Constant 3.22816e+03 2.29162e+01
2 Mean -2.38151e-01 5.23308e-03
3 Sigma 8.05174e-01 3.90446e-03
Distribution of difference of leading edge between the 2 gas gaps
Distribution of difference of averaged leading edge between front end and back end
Time resolution: 0.818ns/sqrt(2)=0.578ns
Time resolution: 0.805ns/sqrt(2)=0.569ns
Time of single end
Mean Time of two ends

## Slide 17: Summary and outlook
The requirements of Phase-II RPC upgrade are clearly identified.
Simulation environment has been set up.
Honeycomb readout panel has been successfully built and it works properly.
Two-end readout method has been tested.
  Spatial resolution: 1-2 cm
  Time resolution: ~550 ps
Further optimization, test, analysis method will be performed continuously.
Thank you!

## Slide 18: Backup

## Slide 19: Compared with PCB readout panel
Efficiency plateau of PCB readout panel after applying the correction of air pressure
Efficiency of honeycomb panel @6000V: 97.68%
Time resolution of PCB readout panel.
Time resolution of honeycomb panel @6000V: ~570 ps
The characteristic impedance of PCB panel: ~14.4 ohm
The characteristic impedance of honeycomb: ~18.5 ohm
1
2
3

## Slide 20: Typical signal waveform
Front end of gap 1
Front end of gap 2
Back end of gap 1
Back end of gap 2

## Slide 21: Optimize timing in the waveform
Threshold
Point 2 in waveform
Point 1 in waveform
Y axis:
Amplitude
X axis:
Time
200 ps
Optimized leading edge
The LSB of the digitizer is 200 ps
Fit the 2 nearby points linearly: Y = a*X + b
When Y=threshold, X is the optimized time.

## Slide 22: Spatial resolution (optimized timing)
NO. NAME VALUE ERROR
1 Constant 5.53964e+03 3.71053e+01
2 Mean 3.54555e-02 9.21285e-04
3 Sigma 1.71935e-01 7.07849e-04
NO. NAME VALUE ERROR
1 Constant 3.07766e+03 2.07736e+01
2 Mean 1.37971e-01 1.69424e-03
3 Sigma 3.09449e-01 1.30087e-03
Spatial resolution = 1.14 cm
Spatial resolution = 2.05 cm