## Slide 1: LHAASO-WFCTA 进展
张寿山
中国科学院高能物理研究所
LHAASO合作组会议，西藏林芝， 2018年10月 8-12日

## Slide 2
WCDA:78,000 m2 3000 cells (25m2/cell)
WFCTA:
18 Cherenkov telescopes (1024 pixels/telescope)
LHAASO
KM2A:
5195 EDs
1171 MDs
Daochen, Sichuan (29o21’ 31” N, 100o08’15” E, 4410 m a.s.l., 600 g/cm)

## Slide 3: LHAASO science in cosmic ray measurement
0.1-10 PeV (Cherenkov mode)
  pure proton and light nuclei (P+He) spectra
  6 telescopes (30°in zenith) + ¼ WCDA
1- 100 PeV (Cherenkov mode)
  Pure iron or heavy nuclei spectra
  18 telescopes (45 °in zenith) + scintillator detectors + muon detectors array
>100 PeV (fluorescence mode)
  2nd knee
  20 telescopes + muon detectors array
  Measure individual cosmic ray spectra from 10TeV to EeV
  Multi-parameters, Multi-stages

## Slide 4: LHAASO science in cosmic ray measurement
0.1-10 PeV (Cherenkov mode)
  pure proton and light nuclei (P+He) spectra
  6 telescopes (30°in zenith) + ¼ WCDA
1- 100 PeV (Cherenkov mode)
  Pure iron or heavy nuclei spectra
  18 telescopes (45 °in zenith) + scintillator detectors + muon detectors array
>100 PeV (fluorescence mode)
  2nd knee
  20 telescopes + muon detectors array
  Measure individual cosmic ray spectra from 10TeV to EeV
  Multi-parameters, Multi-stages

## Slide 5: LHAASO science in cosmic ray measurement
0.1-10 PeV (Cherenkov mode)
  pure proton and light nuclei (P+He) spectra
  6 telescopes (30°in zenith) + ¼ WCDA
1- 100 PeV (Cherenkov mode)
  Pure iron or heavy nuclei spectra
  18 telescopes (45 °in zenith) + scintillator detectors + muon detectors array
>100 PeV (fluorescence mode)
  2nd knee
  20 telescopes + muon detectors array
  Measure individual cosmic ray spectra from 10TeV to EeV
  Multi-parameters, Multi-stages

## Slide 6: LHAASO science in cosmic ray measurement
0.1-10 PeV (Cherenkov mode)
  pure proton and light nuclei (P+He) spectra
  6 telescopes (30°in zenith) + ¼ WCDA
1- 100 PeV (Cherenkov mode)
  Pure iron or heavy nuclei spectra
  18 telescopes (45 °in zenith) + scintillator detectors + muon detectors array
>100 PeV (fluorescence mode)
  2nd knee
  20 telescopes + muon detectors array
  Measure individual cosmic ray spectra from 10TeV to EeV
  Multi-parameters, Multi-stages

## Slide 7: Wide Field of View Cherenkov Telescope (WFCTA)
5m2 spherical mirror
32×32 SiPMs array
Pixel size 0.5°
FOV: 16°× 16°
Portable design: easy to switch the array configurations
Duty cycle：>30%.
SiPM camera
A prototype of WFCTA
WFCTA:
18 Cherenkov telescopes (1024 pixels/telescope)

## Slide 8
合作任务与单位
高能所
高能所
SiPM成像探头
空间中心
合作任务
合作单位
可移动可调节镜筒
慢控制和监测系统
云南大学
  日内瓦大学
高能所
反射式球面光学
望远镜标定及大气监测
西南交大，高能所
读出电子学系统
四川大学

## Slide 9
可移动可调节镜筒进展
可移动可调节镜筒样机
镜筒内部结构示意图
主要指标
  由望远镜镜筒、可移动底盘、俯仰轴系和球面反射镜悬挂桁架组成；
  采用可移动设计，仰角0°- 90°可调，实现望远镜阵列重新布局，实现不同能区观测需求。
  已完成6台生产和测试，这个月底上稻城组装

## Slide 10
反射式球面光学系统进展
主要参数
  面积：~5m2/台；
  每台由20面六边形球面镜和5面半镜组成；
  曲率半镜：5800±10mm
  反射率：>85%@400nm
已完成6台镜子生产和测试，这个月底上稻城组装
单面反射镜
反射镜安装拼接图
拼接完整的反射镜
反射镜安装固定示意图

## Slide 12: Schematic diagram of SiPM camera assembly
AB1
AB2
DB
Cluster
SiPM camera box
SiPM camera：32×32 SiPMs
64 ×
A module has 4×4 SiPMs.
Optical filter
在云大超净室组装（葛茂茂报告）

## Slide 13
Digital Board
Analog Board
Slow control
board
Metal frame
SiPM board
Winston cone
Light concentrator (Winston cone): is to increase the effective area of the SiPM
SiPM board: 16 SiPMs, 16 temperature sensors (embedded in the SiPM chip ), and 16 pre-amplifiers
Slow control board:
  16 temperature and high voltage compensation loops;
  16 channels of high voltage power supply.
Analogue board: 16 channels of amplifier and shaping circuit
Digital board: 50 MHz FADC and FPGA
  Square SiPM：15 mm×15 mm

## Slide 14
Light concentrator (cone)：
Outlet: 15 mm×15 mm
Inlet: 25.4mm×25.4mm
Height: 25.3mm
  Square SiPM：15 mm×15mm
Pixel size: 25.4 mm × 25.4 mm
SiPM size: 15 mm × 15 mm
light concentrators (cone)
With cone/without cone
The number of photons increased by ~2.3 times

## Slide 15
64 sub-clusters have been assembled in the clean room

## Slide 16
resolution
Dynamic range
64 sub-clusters have passed the test.

## Slide 18
<40℃

## Slide 23
Filter window：AR + cutoff
To improve signal to noise ratio
Sky background light spectrum
in the moon less night
Filter
Moon less night
Moon night
NSB(without filter)/NSB（with filter）
λ （nm）
550 nm

## Slide 24
Threshold of the telescope：
~15 TeV @ moonless night，
~100 TeV @ full moon night
Proton
Helium
CNO
MgSiAl
Iron
NSB/NSB0
Full moon night

## Slide 25
N2/YAG激光器及激光转台
工艺性能
项目 | 技术指标
N2激光器 | 波长337nm，能量≥170μJ
YAG激光器 | 波长355nm，能量≥2mJ
三维旋转台 | 方位角范围：0-360° 仰角范围：0-90°角位台范围：±45° 最小转动角度：＜0.02°重复精度：<0.05°
激光升降台
工艺性能
  主要由N2激光器/YAG固体激光器、激光控制器、能量探头、功率计、水冷却系统、升降台，三维转台等部分构成；绝对刻度望远镜能量和监测站点大气质量。
主要指标
工程进度
已完成第一台激光升降台制作；2019年7月完成激光定标和大气监测系统安装和调试。
激光定标和大气监测系统 （谢宁报告）

## Slide 26: 总结
已完成6台可移动可调节镜筒和球面反射镜的生产和测试
  测试结果：性能满足要求
  镜筒正在做防腐喷漆，拆装运输
  预计月底运输到稻城组装
已完成第一台SiPM成像探头制作
  已在实验运行3天，硬件工作正常
  FPGA程序有一些bug，正在调试
  预计10月20号左右运输至稻城测试
6台望远镜制作和运行计划
  预计11月份第一台望远镜开始在稻城运行
  2019年6月份共6台望远镜在稻城运行

## Slide 27: Thank you for your attention!

## Slide 29: SiPM成像探头增益监测
Mirror
UV light 400 nm
SiPM camera
UV LED
UV-LEDs 安装在镜子中心，监测SiPM成像探头的效应
  SiPM成像探头增益的温度效应
  背景光对SiPM增益的影响
  监测电子学高低增益的比值
UV-LEDs 基本信息
  6个LED灯珠，每个光强~3000 photons/SiPM （~1000pe/SiPM）
  脉冲宽度<20 ns， 频率 1 Hz
  监测统计误差: ~0.6% /分钟 @ 无月,
  ~0.8%/分钟@100倍背景光
R3
-
+
vcc
SiPM
C1
R0
R1
OPA 846
R2
The supply voltage of the SiPM is equal to Vcc-VR0 .
LED
安装
位置
LED温度效应：0.2%/℃
恒温系统：
±3℃

## Slide 30: Trigger algorithm
First level trigger：single channel trigger
Signal to noise ratio: S/N>n
Threshold varies with the intensity of the sky background light.
Second level trigger： pattern recognition
Round-shaped
pattern
Line-shaped pattern
One of Cherenkov event
Fluorescence event
Site2
Site1
Site3
Energy threshold of the telescope: ~30 TeV @ moonless night, ~300 TeV @ half moon night.

## Slide 31
Moon trajectory
North
East
South
West
Cherenkov telescope array: 16 telescopes are aimed from north-east to north-west.

## Slide 32
4 × 4 SiPMs & Preamplifiers
Service
TCP/IP
Switch
Low voltage power supply
Slow Control Board
64 ×
DB
FPGA
50M 14 bit FADC
50M 14 bit FADC
BDB
Trigger & Data Buffer & Communication Board
Event trigger
Data
AB
Low
gain
High
gain
Synchronizing
TCP/IP
The SiPM gain (break down voltage) is sensitive to the temperature.
Slow Control Board: temperature & high voltage compensation loop.
16 ×
Temperature
High
voltage
The architecture
of SiPM camera
readout electronics
Single trigger