## Slide 1: Full Silicon Tracker
Weiming YAO (LBNL) and Chengdong FU (IHEP)
(for full silicon tracker group)

## Slide 2: Contents
Introduction
Concept design
Track performance
Future plan
Conclusion

## Slide 3: Introduction
Partial silicon tracker + TPC is designed as the tracker in the baseline detector for CepC. But other one or more tracker is still needed as the design for the potential second IP or as a backup tracker for the preferred tracker.
ILD and FCC-ee have their full silicon tracker design and have done study well.
CepC silicon study group have also studied silicon detector as partial tracker, such as vertex detector (VXD), forward detector (FTD), etc.
The study on full silicon tracker: technology, layout design and performance. The technology can benefit from the partial silicon tracker study. The full silicon tracker designs in other colliders can be referenced.

## Slide 4: Technology
Planary layers cover solid angle as much as possible.
  support layer + silicon layer:
    double side
    single side
  other support
  electronics
Silicon sensor technology (CMOS) is same as the VXD, FTD, SIT/SET in the baseline detector.
  VXD:
    Toward 16 m pitch (2.8 m single-point resolution)
  SIT/SET and FTD_STRIP:
    50m pitch
    <200m thickness
  FTD_PIXEL:
    50m
Electronics
  Same as the baseline, not yet considered in simulation

## Slide 5: Full Silicon Tracker (FST) Concept designs
Replace TPC with silicon tracker and re-design silicon parts in the baseline, same beam pipe and calorimeters
  3.0 Tesla
  14.5 mm outer radius for Be beam pipe
  Maximum 1.83 m outer radius and 4.6 m length at Z direction
Two options
  FST: expand extra SIT layers and FTD disks to fill the tracker space, and rename the parts
    Vertex detector (VXD): VXD in the baseline
    Silicon outer tracker (SOT): SIT type
    Endcap inside tracker (EIT): FTP_PIXEL type
    Endcap outside tracker (EOT): FTP_STRIP type
  FST2: expanding the SID design to full tracking volume
Double strip layer for FST and single strip layer for FST2
  FST: more expensive and high performance

## Slide 6: Layouts
Zoomed

## Slide 8: Space point

## Slide 9: Fast simulation
For track at =20 and =85 direction

## Slide 10: Layer Materials of FST
Mechanical properties have not been studied in detail
SIT(SiD-like) | silicon | peek | Carbon fiber | Rohacell 50D | epoxy | Carbon fiber | Total support
Thickness(mm) | 0.15+0.0024 | 0.1 | 0.08 | 0.9 | 0.08 | 0.08 | 1.2424
FTD_PIXEL | silicon | Carbon fiber | Rohacell50D | peek | Total support
Thickness(mm) | 0.2+0.0048 | 0.16 | 1.8 | 0.2 | 2.1648
FTD_STRIP | silicon | peek | Carbon fiber | Rohacell 50D | epoxy | Carbon fiber | silicon | Total support
Thickness(mm) | 0.15 | 0.2 | 0.16 | 1.8 | 0.175 | 0.16 | 0.15+0.0048 | 2.4998
VXD | silicon | kapton | aluminium | foam | Total support
Thickness(mm) | 0.05 | 0.05 | 0.01 | 0.94 | 1

## Slide 11: Material Budget of FST
From ~4.5% of X0 to ~8.1% (cos<0.99)

## Slide 12: Simulation and Reconstruction Tools
MokkaCa developed Mokka version @CepC
  http://cepcgit.ihep.ac.cn/cepcsoft/MokkaC
Tracking and fit
  ConformalTracking
    used as the main track pattern recognition algorithm at CLIC, and FCC-ee are also performing
    Implemented into CepC software, and ongoing
For FST2
  http://atlaswww.hep.anl.gov/hepsim/doc/doku.php?id=fcs:cepc:2017
a ZHGG event
…
…
Endcap: no VXD hit
VXD
SIT
Conformal space:
In conformal space, a track in magnetic field is a straight line
Track finding becomes straight line searching by pattern recognition (cellular automaton)

## Slide 13: Hits

## Slide 14: Tracking Efficiency of FST(Single Muon)

## Slide 15: Resolution of FST(Single Muon)

## Slide 16: Tracking Efficiency of FST(ZHGG)

## Slide 17: Mass Resolution (H)

## Slide 18: Future plan
Optimize layouts
  silicon thickness
  support structure
Electronics in simulation
If necessary, balance cost and performance
Study on physical performance
Optimize with calorimeter together

## Slide 19: Conclusion
The concepts of full silicon tracker have been implemented and seem working.
Two options have been considered, one for expensive and higher performance, close to the baseline detector, another for cheap
  Performance for more options can be estimated as between them.
Based on comparison with the baseline detector, it is expectable that the full silicon tracker can provide close performance for those particles with long life.
More optimization and study are in plan.

## Slide 20: backup
Thank you for your attention!

## Slide 21: Performance of FST2
http://atlaswww.hep.anl.gov/hepsim/doc/doku.php?id=fcs:cepc:2017