## Slide 1
650MHz Cavity Cryomodule for CEPC Accelerator
Ruixiong HAN
hanrx@ihep.ac.cn)
IHEP Cryogenics group
September 22th, 2018
7th IHEP-KEK SCRF Collaboration Meeting
Beijing, 22-23 September 2018

## Slide 2
  Outline
CEPC Cryogenic system
CEPC Cryomodule
CEPC Test Cryomodule and distribution valve box
Heat load of CEPC Cryomodule
Schedule

## Slide 3
CEPC Cryogenic System
336 650 MHz RF cavities for the Collider;
96 1.3 GHz RF cavities for the Booster;
There are 4 cryogenic station in the CEPC cryogenic system;
Each cryogenic station lies besides the RF station, which provides helium for the collider ring and the booster ring;

## Slide 4
CEPC Cryogenic System
The Cryogenic system mainly includes the refrigerators, cycle compressors, helium storage tanks, helium purification equipments, cold compressors, distribution boxes and cryomodules;
The cryomodules have two shields, a 40K~80K shield and a 5K~8K shield. A 2.2K, 1.2bar helium is supplied for the cryomodules and the 2K, 31mbar helium gas return to the cold box by the cold compressors;

## Slide 5
CEPC 650MHz-Cavity Cryomodule
Six 2-cell Cavities Cryomodule | 
Overall length(flange to flange, m) | 8.0
Diameter of Vacuum vessel ,m | 1.4
Beamline height from floor, m | 1.5
Cryo-system working temperature, K | 2
Number of cavities | 6
Number of coupler | 6
HOM absorber | 2
Number of 200-POST | 6
Cryomodule performance |  | Specification
RF gradient [MV/m] |  | 13.8(H), 9.4(W), 9.6(Z)
Dynamic heat loads at 2K (Qo=1E10) |  | 19.0(H), 8.7(W), 9.2(Z)
Static heat loads at 2K (Max. Operation) |  | 5W
Number of leakage | He →insulation | 0
 | He →beam pipe | 0
 | Insulation →coupler | 0
 | Insulation →beam pipe | 0
 | Coupler →beam pipe | 0
Alignment x/y inside (Cavities) |  | ±0.5mm
Alignment z inside |  | within 2 mm
Coupler antenna design z |  | within 2 mm

## Slide 6
CEPC 650MHz-Cavity Cryomodule

## Slide 7
CEPC Test Cryomodule & Valve Box

## Slide 8
•Vacuum vessel
– Material:316L stainless steel
–Outer diameter = 1424mm
– Length=3000mm
•Support post
–Supporting the all cold mass in the vacuum vessel
–Supporting Cavities：Diameter is 180mm
–Supporting RF-Gate Valve：Diameter is 150mm
–Number:2+2=4
–Material：FRP(G-10)
•Thermal radiation shield
–Aluminum plate ＋Muti-layer insulation of aluminum-evaporated film(Super Insulation)
–40K-70K Nitrogen gas, 5K-10K helium gas
•Strongback
–Stainless steel
–Room temperature
Two 2-cell 650 MHz superconducting cavities;
Two high power couplers
Two mechanical tuners
Two HOM absorbers
High Q0
Fast cool-down is introduced
CEPC Test Cryomodule

## Slide 9
CEPC Test Cryomodule-X-Z Section

## Slide 10
CEPC Test Cryomodule-Cavity-string

## Slide 11
Active
Follow
X,Y,Z：± 4mm
CEPC Test Cryomodule-Adjustments

## Slide 12
CEPC Test Cryomodule-X-Y Section

## Slide 13
CEPC Test Cryomodule

## Slide 14
1-2K Pipe；2- Beam Pipe ；3-cool down /warm up pipe； 4-5Kshield Ω pipe；
5- 80Kshield Ω pipe ；6-2Ktansfer line；
CEPC Test Cryomodule-cryoenic pipes

## Slide 15
1-Outer pipe，2-80K shield，3-80K pipe，4-5K pipe，5-5Kshield，6-G10 support，7-2K pipe，8-cool down pipe
CEPC Test Cryomodule-2K transfer line

## Slide 16
Tension Test
TEST
300
200
180
160
150
POST
POST
CEPC Test Cryomodule-POSTS

## Slide 17
CEPC cryomodule Assembly equipment

## Slide 18
Heat source | N | Static/W |  |  | Dynamic/W |  | 
 |  | 80K | 5K | 2K | 80K | 5K | 2K
Cavities | 6 | / | / | / | / | / | 120
Input Couplers | 6 | 36.00 | 18.00 | 2.10 | 60.00 | 36.00 | 6.00
HOM couplers | 12 | / | / | / | / | / | 6.00
200-POSTs | 6 | 44.37 | 6.81 | 2.10 | / | / | /
Instrumentation Cables | / | / | / | 0.54 | / | / | /
Radiation | / | 32.50 | 1.28 | / | / | / | /
Other | / | 1.00 | 0.30 | 0.20 |  |  | 
Summary |  | 113.87 | 26.49 | 4.94 | 60 | 36 | 132
Heat load summary of the CEPC cryomodule
Heat Load of CEPC cryomodule

## Slide 19
Distribution Valve Box

## Slide 20
Conclusion and Schedule
2017. 12 Conceptual design of CEPC Cryomodule will have been completed.
2018. 08 Mechanical design of CEPC test Cryomodule will have been completed.
2019. 04 Fabrication of CEPC test Cryomodule will have been completed.
2019. 10 Assembly of CEPC test Cryomodule will have been completed.
2020. 06 Commissioning of beam source system will have been completed.
The conceptual design of CEPC cryomodule and the mechanical design of test cryomodule have been completed.
The structure and specification of the CEPC cryomodule were introduced, and the detail design of test cryomodule was shown.
The 650MHz cavities, distribution valve box and test cryomodule will be fabricated.

## Slide 21
Thanks for your attention