## Slide 1: CEPC Accelerator Overview(CDR)
  J. Gao and Y. Zhang
  Onbehalf of CEPC Accelerator Group
  Institute of High Energy Physics
  CAS, Beijing
  CEPC Physics/Detector International Review
  Sept. 13-15 2018,IHEP, Beijing, China

## Slide 2: Accelerator from Pre-CDR to CDR
CEPC accelerator CDR completed in June 2018 (released on Spet. 2 2018)
  Executive Summary
  Introduction
  Machine Layout and Performance
  Operation Scenarios
  CEPC Collider
  CEPC Booster
  CEPC Linac
  Systems Common to the CEPC Linac, Booster
  and Collider
  8. Super Proton Proton Collider
  9. Conventional Facilities
  10. Environment, Health and Safety
  11. R&D Program
  12. Project Plan, Cost and Schedule
  Appendix 1: CEPC Parameter List
  Appendix 2: CEPC Technical Component List
  Appendix 3: CEPC Electric Power Requirement
  Appendix 4: Advanced Partial Double Ring
  Appendix 5: CEPC Injector Based on Plasma Wakefield Accelerator
  Appendix 6: Operation as a High Intensity -ray Source
  Appendix 7: Operation for e-p, e-A and Heavy Ion Collision
  Appendix 8: Opportunities for Polarization in the CEPC
  Appendix 9: International Review Report
March 2015
April 2017
Draft CDR for
Mini International
Review in Nov. 2017
CDR International Review June 28-30, 2018, final CDR (accelerator) released on Sept. 2, 2018
arXiv:1809.00285

## Slide 3
International Review of CEPC CDR
(June 28-30, 2018, IHEP)
Review Committee Members:
Brian Foster Oxford U./DESY
Eugene Levichev BINP
Katsunobu Oide (chair) CERN/KEK
Kazuro Furukawa KEK
Manuela Boscolo INFN
Marica Biagini INFN
Masakazu Yoshioka KEK/Tohoko University
Norihito Ohuchi KEK
Paolo Pierini ESS
Steinar Stapnes CERN
Yoshihiro Funakoshi KEK
Zhengtang Zhao (absent) SINAP

## Slide 4
International Review Report of CEPC CDR (June 28-30, 2018, IHEP)
The Review Committee unanimously congratulates the CEPC team on the completion of the CDR, with remarkable successes in various aspects of the design. The progress since the pre-CDR has been a major step in the project...
The Committee believes that the CDR has already reached a sufficient level of maturity to allow approval to proceed to a Technical Design Report.

## Slide 5: CDR Baseline Design
Higgs factory as first priority
Compatible with future pp collider
Maximum SR beam power 30 MW

## Slide 6: Main Parameters
 | Higgs | W | Z（3T） | Z（2T）
Number of IPs | 2 |  |  | 
Beam energy (GeV) | 120 | 80 | 45.5 | 
Circumference (km) | 100 |  |  | 
Synchrotron radiation loss/turn (GeV) | 1.73 | 0.34 | 0.036 | 
Crossing angle at IP (mrad) | 16.5×2 |  |  | 
Piwinski angle | 3.48 | 7.0 | 23.8 | 
Number of particles/bunch Ne (1010) | 15.0 | 12.0 | 8.0 | 
Bunch number (bunch spacing) | 242 (0.68s) | 1524 (0.21s) | 12000 (25ns+10%gap) | 
Beam current (mA) | 17.4 | 87.9 | 461.0 | 
Synchrotron radiation power /beam (MW) | 30 | 30 | 16.5 | 
Bending radius (km) | 10.7 |  |  | 
Momentum compact (10-5) | 1.11 |  |  | 
 function at IP x* / y* (m) | 0.36/0.0015 | 0.36/0.0015 | 0.2/0.0015 | 0.2/0.001
Emittance ex/ey (nm) | 1.21/0.0024 | 0.54/0.0016 | 0.18/0.004 | 0.18/0.0016
Beam size at IP sx /sy (m) | 20.9/0.06 | 13.9/0.049 | 6.0/0.078 | 6.0/0.04
Beam-beam parameters x/y | 0.018/0.109 | 0.013/0.123 | 0.004/0.06 | 0.004/0.079
RF voltage VRF (GV) | 2.17 | 0.47 | 0.10 | 
RF frequency f RF (MHz) (harmonic) | 650 (216816) |  |  | 
Natural bunch length z (mm) | 2.72 | 2.98 | 2.42 | 
Bunch length z (mm) | 4.4 | 5.9 | 8.5 | 
HOM power/cavity (2 cell) (kw) | 0.46 | 0.75 | 1.94 | 
Energy spread (%) | 0.134 | 0.098 | 0.080 | 
Energy acceptance requirement (%) | 1.35 | 0.90 | 0.49 | 
Energy acceptance by RF (%) | 2.06 | 1.47 | 1.7 | 
Photon number due to beamstrahlung | 0.082 | 0.050 | 0.023 | 
Beamstruhlung lifetime /quantum lifetime* (min) | 80/80 | >400 |  | 
Lifetime (hour) | 0.43 | 1.4 | 4.6 | 2.5
F (hour glass) | 0.89 | 0.94 | 0.99 | 
Luminosity/IP L (1034cm-2s-1) | 2.93 | 10.1 | 16.6 | 32.1
*include beam-beam simulation and real lattice

## Slide 7: Accelerator Chain and Systems
Three rings in the sane channel：
  CEPC & booster
  SppC
Energy Ramp
10 ->45/120GeV
1) Injector
2) Booster
3) Main Ring
Electron
Positron
10 GeV
45/120 GeV
Booster Cycle (0.1 Hz)
C=100km
The key systems of
CEPC:
1) Linac Injector
2) Booster
3) Collider ring
4) MDI
5) Civil Eng.
4) Machine Detector Interface (MDI)
C=100km
L=1.2km
5) Civil Eng.

## Slide 8: Layout
CEPC Linac injector (1.2km, 10GeV)

## Slide 9
Collider Ring
The circumference of CEPC collider ring is 100 km.
In the RF region, the RF cavities are shared by two ring for H mode.
Twin-aperture of dipoles and quadrupoles is adopt in the arc region to reduce the their power. The distance between two beams is 0.35m.
Compatible optics for H, W and Z modes
  For the W and Z mode, the optics except RF region is got by scaling down the magnet strength with energy.
  For H mode, all the cavities will be used and bunches will be filled in half ring.
  For W & Z modes, half number of cavities will be used and bunches can be filled in full ring.
Notes: 2 fold symmetry

## Slide 10
Optics of Interaction region
max deviation between two beamlines 9.7m
local chromaticity correction of both plane, asymmetric layout , crab-waist collision
L*=2.2m, C =33mrad, GQD0 =136T/m, GQF1 =111T/m, LQD0 =2.0m, LQF1 =1.48m
IP upstream of IR: Ec < 120 keV within 400m, last bend Ec = 45 keV
IP downstream of IR: Ec < 300 keV within 250m, last bend Ec = 97 keV
Nonlinearity of Interaction region is well corrected locally
Notes: to update line 3,4,5 and geometry figure
Modify 0 at IP
Lqd0=2m, MDI constraint

## Slide 11
Lattice Design of Collider Ring
  An optics fulfill requirements of the parameters list, geometry, photon background and key hardware
    FODO cell, 90/90, non-interleaved sextupole scheme, period =5cells in arc
    Get a smallest average beta function to reduce the multi-bunch instability caused by RF cavities especially for the Z mode in RF region
    The function of the straight section is phase advance tuning and injection.
Energy sawtooth is around 0.35 %. Closed orbit distortion in CEPC collider ring is around 1 mm and becomes 1um after tapering the magnet strength with beam energy
Optimized Dynamic Aperture fulfill the requirements of injection and beam lifetime
Notes: Update figures

## Slide 12: Booster & Injection Time Structure
25m separation @ IP
Mode | Higgs | W | Z
Bunch number | 242 | 1220 | 6000
Current threshold | 1 mA | 4 mA | 10 mA
Number of Cycles | 1 | 1 | 2
Injection period (sec) | 73.1 | 131 | 438
Full Injection time | 10 min | 15 min | 2.2 Hour (collide from 230mA

## Slide 13
Beam Dynamics Status
The studies on key beam dynamic issues have been finished.
Design of interaction region
Compensation of detector solenoid
Control of detector background
Lattice design
On-axis injection scheme（only for Higgs）
Optimization of dynamic aperture
Beam acceleration in the Linac and booster ring
Impedance and instabilities
Beambeam effect

## Slide 14: SRF Design Challenges
High energy, low current: high gradient, high Q, more cells, narrow bandwidth
Low energy, high current: HOM power (less cells), parasitic loss, HOM CBI, FM CBI (low voltage, large detuning)
Large ring: gap transient, dense beam spectrum
Special issues with CEPC: parking cavities for W and Z, gap transient for Higgs half-fill, transient beam loading of bunch swapping for on-axis injection
Booster cavity voltage ramp: narrow bandwidth
 | H | W | Z
Collider Ring | 650 MHz 2-cell cavity |  | 
Lumi. / IP (1034 cm-2s-1) | 2.93 | 10.1 | 16.6 / 32.1
RF voltage (GV) | 2.17 | 0.47 | 0.1
Beam current (mA) | 17.4 x 2 | 87.7 | 460
Cavity number | 240 | 108 x 2 | 60 x 2
SR power (MW) | 30 | 30 | 16.5
2 K cavity wall loss (kW) | 6.1 | 1.3 | 0.1
Booster Ring (extraction) | 1.3 GHz 9-cell cavity |  | 
RF voltage (GV) | 1.97 | 0.585 | 0.287
Beam current (mA) | 0.52 | 2.63 | 6.91
Cavity number | 96 | 64 | 32
RF input power (MW) avg. | 0.07 | 0.02 | 0.02
2 K wall loss (kW) avg. | 0.17 | 0.01 | 0.02

## Slide 15: SRF Status
CEPC CDR SRF parameters and layout have been established in view of high Higgs priority, low construction cost and upgradability.
Beam cavity interaction issues (FM and HOM CBI, parking cavities, RF transients of bunch gap and swapping, HOM power) are challenging but manageable, especially for Z-pole.
SRF key components design and R&D launched, with support of PAPS SRF facility. SRF industrialization will be synergy with SHINE and ADANES etc. in China (~ 1000 cavities in next five years).
CEPC 650 MHz 2-cell cavity by OTIC

## Slide 16: SRF Technology R&D Plan
SRF Key Technology R&D (2016-2020)
    High Q & high gradient cavity with N-doped Nb & Fe-based superconductor
    Very high power (300 kW) variable input coupler with low heat load
    High power coaxial HOM coupler (1 kW) and wideband HOM absorber (5 kW)
Cryomodule Prototyping (2019-2022)
    Collider cryomodules: 650 MHz 2 x 2-cell and full scale 6 x 2-cell (11 m)
    Booster cryomodules: 1.3 GHz 2 x 9-cell and full scale 8 x 9-cell (12 m)
    High Q operation (clean assembly, magnetic hygiene and flux expulsion)
    Beam test with DC-photocathode gun
Prepare for Mass-Production (2021-2023)
    Supported by PAPS large SRF infrastructure (start operation in early 2020)
    In the frame of CEPC Industrial Promotion Consortium (CIPC)
    In synergy with other SRF accelerator projects (LCLS-II, SHINE, ILC, etc.)

## Slide 17: Collider Magnet
Over 80% of collider ring is covered by conventional magnet.
The most important issues are Cost & Power Consumption.
  Make the magnets compact and simple.
  Use aluminum for the coils.
  Dual aperture magnets save nearly 50% power.
  Consider the combined function magnets.
  Increase the coil cross section and decrease the operating current.

## Slide 18: High efficiency klystron
CEPC Collider SRF Wall Plug Efficiency
The increase in efficiency of RF power sources is considered a high priority issue;
Development of high efficiency klystron is on going in China and other country;
The manufacture of the 1st tube will be completed this year in China and 3 schemes for the high efficiency design are ongoing based on 3 different gun design.

## Slide 19
Final Focus Magnets & Cryostat
Anti coil

## Slide 20
The accelerator components inside the detector without shielding are within a conical space with an opening angle of cosθ=0.993.
The e+e- beams collide at the IP with a horizontal angle of 33mrad and the final focusing length is 2.2m
Lumical will be installed in longitudinal 0.95~1.11m, with inner radius 28.5mm and outer radius 100mm.
The Machine Detector Interface (MDI) of CEPC double ring scheme is about 7m long from the IP
The CEPC detector superconducting solenoid with 3T magnetic field and the length of 7.6m.
With Detector solenoid
Without Detector solenoid
~cryostat in detail
MDI Layout and Parameters

## Slide 21: Beam Loss Backgrounds at IP
Beamstrahlung
IP1
IP3
Beam Lost Particles
Energy Loss > 1.5%
(energy acceptance)
Radiative Bhabha
scattering
242 bunches
Revolution frequency: 2997Hz
particles/Bunch
L:
Beam-Gas
Scattering
Beam-Thermal photon
scattering

## Slide 22
Preliminary Study for CEPC Z-pole Polarization
Longitudinal polarization of electrons
S. Nikitin

## Slide 23
01. General Layout
IP1
IP3
IP2
IP4
LSS1
LSS2
LSS3
LSS4
LINAC
BTL
L=99.67km
3.32km
3.32km
3.24km
3.24km
1.20km
1.20km
1.20km
1.20km
10.2km
Civil Engineering Design

## Slide 24
CEPC Tunnel Cross Sections, Arc and SCRF Regions
IP2 / IP4--SCRF region
Notes: IR is arranged at IP1/IP3, with the length of 3320.00m for each one. The sections from the intersections of tunnels in the IR and tunnels at the curve sections to the zones within 1532.00m of both sides of halls are linear sections with the width ranging from 6.00m~10.74m and the height of 5.00m. At these linear sections, the routing direction of tunnel will be adjusted according to booster line and transfer lines. The zones within 1532.00m of both sides of halls are divided into two tunnels respectively for arranging positive / negative electron beam and booster beam . The tunnel for arranging positive / negative electron beam is 6.00m~11.40m wide, 4.50m high and 1509.30m long (single side). The tunnel for arranging booster line is 3.50m wide, 3.50m high, and 3018.60m long. The dimension of tunnel section is determined with consideration given to local control, electrical, beam measurement, vacuum and cooling equipment as well as requirements of passage of personnel and maintenance .

## Slide 25
IP1 / IP3
3.32km
6.0~11.4x4.5
3.02km
3.5x3.5
CEPC Tunnel in Detector Region

## Slide 26
CEPC Detector Hall Area

## Slide 27: Power for Higgs and Z
266MW
149MW
Fermilab
with Tevatron
58MW
CERN-2012
LHC@3.5TeV
183MW

## Slide 28: Cost Breakdown

## Slide 29: Cost Breakdown (cont)
Magnets
Vacuum
SRF
RF Power Source
Cryogenic
LINAC
Mechanical
Instrumentation
Magnet Power Supply

## Slide 30
Conclusions
CEPC Accelerator CDR has been completed (formally released on Sept 2, 2018, after international review in June 2018) with all systems reaching the CDR design goals
CEPC MDI Design has been done in CDR with more detaied designs underway
CEPC civil engineering design has been done in CDR with detector
hall and tunnels
CEPC Z-pole polarization option has been preliminarily studied and in next years after CDR, a baseline of CEPC Accelerator Design with
Z-pole polarization will be given with the fund from MOST (II)

## Slide 31
Further reading references:
CEPC-SppC CDR http://cepc.ihep.ac.cn/preCDR/volume.html.
CEPC-SppC Progress Report http://cepc.ihep.ac.cn/Progress%20Report.pdf.
J Gao, 2016 IHEP-AC-LC 2016-002.
J Gao, 2017 2017 Int. J. Mod. Phys. A 32 1746003.
D Wang, 2017 Int. J. Mod. Phys. A 32 1746006.
Y W Wang, 2017 Int. J. Mod. Phys. A 32 1746004.
T J Bian, 2017 Int. J. Mod. Phys. A 32 1746009.
F Su, 2017 Int. J. Mod. Phys. A 32 1746005.
Y F Wang, FCC Week talk, Amsterdam, April, 2018.
J Gao, A milestone year for Higgs factories in Aisa. ILC Newsline, 2018, March 1 (http://newsline.linearcollider.org/2018/03/01/2018milestoneyearasia/)
J Gao, China’s bid for a circular electron-positron collider. CERN Courier, 2018, June 1, (http://cerncourier.com/cws/article/cern/71537)

## Slide 32
Thank you for your attention
Thanks go to
CEPC accelerator team and international collaborators

## Slide 33
Backup Slides

## Slide 34: CEPC Booster SRF Parameters
10 GeV injection | H | W | Z
Extraction beam energy [GeV] | 120 | 80 | 45.5
Bunch number | 242 | 1524 | 6000
Bunch charge [nC] | 0.72 | 0.576 | 0.384
Beam current [mA] | 0.52 | 2.63 | 6.91
Extraction RF voltage [GV] | 1.97 | 0.585 | 0.287
Extraction bunch length [mm] | 2.7 | 2.4 | 1.3
Cavity number in use (1.3 GHz TESLA 9-cell) | 96 | 64 | 32
Gradient [MV/m] | 19.8 | 8.8 | 8.6
QL | 1E7 | 6.5E6 | 1E7
Cavity bandwidth [Hz] | 130 | 200 | 130
Beam peak power / cavity [kW] | 8.3 | 12.3 | 6.9
Input peak power per cavity [kW] (with detuning) | 18.2 | 12.4 | 7.1
Input average power per cavity [kW] (with detuning) | 0.7 | 0.3 | 0.5
SSA peak power [kW] (one cavity per SSA) | 25 | 25 | 25
HOM average power per cavity [W] | 0.2 | 0.7 | 4.1
Q0 @ 2 K at operating gradient (long term) | 1E10 | 1E10 | 1E10
Total average cavity wall loss @ 2 K eq. [kW] | 0.2 | 0.01 | 0.02

## Slide 35: Main Parameters of Injector Linac
The total beam transfer efficiency from transfer line to the injection point of collider ring is higher than 90%.
The transfer efficiency can be much higher with the application of damping ring which the beam energy is 1.1GeV.
Parameter | Symbol | Unit | Designed
e- /e+ beam energy | Ee-/Ee+ | GeV | 10
Repetition rate | frep | Hz | 100
e- /e+ bunch population | Ne-/Ne+ |  | > 9.4×109 / >9.4×109
 |  | nC | > 1.5
Energy spread (e- /e+ ) | σe |  | < 2×10-3 / < 2×10-3
Emittance (e- /e+ ) | εr | nm rad | < 120
Bunch length (e- /e+ ) | σl | mm | 1 / 1
e- beam energy on Target |  | GeV | 4
e- bunch charge on Target |  | nC | 10

## Slide 36: CEPC Booster parameters @ injection (10GeV)
 |  | H | W | Z
Beam energy | GeV | 10 |  | 
Bunch number |  | 242 | 1524 | 6000
Threshold of single bunch current | A | 25.7 |  | 
Threshold of beam current (limited by coupled bunch instability) | mA | 127.5 |  | 
Bunch charge | nC | 0.78 | 0.63 | 0.45
Single bunch current | A | 2.3 | 1.8 | 1.3
Beam current | mA | 0.57 | 2.86 | 7.51
Energy spread | % | 0.0078 |  | 
Synchrotron radiation loss/turn | keV | 73.5 |  | 
Momentum compaction factor | 10-5 | 2.44 |  | 
Emittance | nm | 0.025 |  | 
Natural chromaticity | H/V | -336/-333 |  | 
RF voltage | MV | 62.7 |  | 
Betatron tune x/y/s |  | 263.2/261.2/0.1 |  | 
RF energy acceptance | % | 1.9 |  | 
Damping time | s | 90.7 |  | 
Bunch length of linac beam | mm | 1.0 |  | 
Energy spread of linac beam | % | 0.16 |  | 
Emittance of linac beam | nm | 40~120 |  | 

## Slide 37: CEPC Booster Parameters @ extraction
 |  | H |  |  | W | Z
 |  | Off axis injection | On axis injection |  | Off axis injection | Off axis injection
Beam energy | GeV | 120 |  |  | 80 | 45.5
Bunch number |  | 242 |  | 235+7 | 1524 | 6000
Maximum bunch charge | nC | 0.72 |  | 24.0 | 0.58 | 0.41
Maximum single bunch current | A | 2.1 |  | 70 | 1.7 | 1.2
Threshold of single bunch current | A | 300 |  |  |  | 
Threshold of beam current (limited by RF power) | mA | 1.0 |  |  | 4.0 | 10.0
Beam current | mA | 0.52 |  | 1.0 | 2.63 | 6.91
Injection duration for top-up (Both beams) | s | 25.8 |  | 35.4 | 45.8 | 275.2
Injection interval for top-up | s | 73.1 |  |  | 153.0 | 438.0
Current decay during injection interval |  | 3% |  |  |  | 
Energy spread | % | 0.094 |  |  | 0.062 | 0.036
Synchrotron radiation loss/turn | GeV | 1.52 |  |  | 0.3 | 0.032
Momentum compaction factor | 10-5 | 2.44 |  |  |  | 
Emittance | nm | 3.57 |  |  | 1.59 | 0.51
Natural chromaticity | H/V | -336/-333 |  |  |  | 
Betatron tune x/y |  | 263.2/261.2 |  |  |  | 
RF voltage | GV | 1.97 |  |  | 0.585 | 0.287
Longitudinal tune |  | 0.13 |  |  | 0.10 | 0.10
RF energy acceptance | % | 1.0 |  |  | 1.2 | 1.8
Damping time | ms | 52 |  |  | 177 | 963
Natural bunch length | mm | 2.8 |  |  | 2.4 | 1.3
Injection duration from empty ring | h | 0.17 |  |  | 0.25 | 2.2

## Slide 38
 | range | Peak filed in coil | Central filed gradient | Bending angle | length | Beam stay clear region | Minimal distance between two aperture | Inner diameter | Outer diameter | Critical energy (Horizontal) | Critical energy (Vertical) | SR power (Horizontal) | SR power (Vertical)
L* | 0~2.2m |  |  |  | 2.2m |  |  |  |  |  |  |  | 
Crossing angle | 33mrad |  |  |  |  |  |  |  |  |  |  |  | 
MDI length | 7m |  |  |  |  |  |  |  |  |  |  |  | 
Detector requirement of opening angle | 13.6˚ |  |  |  |  |  |  |  |  |  |  |  | 
QD0 |  | 3.2T | 136T/m |  | 2m | 19.51mm | 72.61mm | 40mm | 53mm | 1.3MeV | 527keV | 639W | 292W
QF1 |  | 3.8T | 110T/m |  | 1.48m | 26.85mm | 146.2mm | 56mm | 69mm | 1.6MeV | 299keV | 1568W | 74W
Lumical | 0.95~1.11m |  |  |  | 0.16m |  |  | 57mm | 200mm |  |  |  | 
Anti-solenoid before QD0 |  | 7.26T |  |  | 1.1m |  |  | 120mm | 390mm |  |  |  | 
Anti-solenoid QD0 |  | 2.8T |  |  | 2m |  |  | 120mm | 390mm |  |  |  | 
Anti-solenoid QF1 |  | 1.8T |  |  | 1.48m |  |  | 120mm | 390mm |  |  |  | 
Beryllium pipe |  |  |  |  | 7cm |  |  | 28mm |  |  |  |  | 
Last B upstream | 67.66~161.04m |  |  | 1.1mrad | 93.38m |  |  |  |  | 45keV |  |  | 
First B downstream | 46.06~107.04m |  |  | 1.54mrad | 60.98m |  |  |  |  | 97keV |  |  | 
Beampipe within QD0 |  |  |  |  | 2m |  |  |  |  |  |  | 2.9W | 
Beampipe within QF1 |  |  |  |  | 1.48m |  |  |  |  |  |  | 3.1W | 
Beampipe between QD0/QF1 |  |  |  |  | 0.23m |  |  |  |  |  |  | 36.2W | 
The superconducting magnet parameters are same in tt and higgs.
CEPC MDI Parameters

## Slide 39: CEPC Cost Breakdown (no detectors)
Including civil cost
Without including civil cost

## Slide 40
1)
2)
3)
4
1
2
3
4
5
6
CEPC Site Selections
1) Qinhuangdao, Hebei Province（Completed in 2014）
2) Huangling, Shanxi Province（Completed in 2017)
3) Shenshan, Guangdong Province(Completed in 2016)
4) Baoding (Xiong an), Hebei Province (Started in August 2017)
5) Huzhou, Zhejiang Province (Started in March 2018)
6) Chuangchun, Jilin Province (Started in May 2018)

## Slide 41
Item | Huangling | Shen-Shan | Funing
Project layout |  |  | 
Construction difficulty | Moderate | Relatively difficult | Relatively easy
Funing（100km）
Huangling（100km）
Shen-Shan（100km）
Notes: Huangling: The site is mainly on the loess plateau. The buried depth of the tunnel and the depth of the shafts are quite different. The construction access layout is relatively simple.
Shen-Shan: The site is mainly the low mountain area. The buried depth of the tunnel and the depth of the shafts are large, and the construction access layout is relatively complicated.
Funing: The site is generally the low hilly areas; underground burial depth is not big; the construction site conditions are better; the construction access layout is relatively simple.

## Slide 42
3 Project Layout and Preliminary Scheme
CEPC CDR Civil Enginnering Design (Funing 100km, example)

## Slide 43
CEPC Detector Hall Area-2

## Slide 44
CEPC Detector Hall Area-3

## Slide 45: IR Mechanics Assembly
RVC head
RVC tail
RVC whole layout

## Slide 46
Plan & Progress
3 design schemes for high efficiency design
  Scheme 1：optimize cavity chain by using the same gun as 1st tube;
  Scheme 2 ：with high voltage gun (110kV/9.1A), low perveance;
  Scheme 3：MBK, 54kV/20A electron gun
Parameter | Scheme1 | Scheme2 | Scheme3
Freq (MHz) | 650 | 650 | 650
Voltage (kV) | 81.5 | 110 | 54
Current (A) | 15.1 | 9.1 | 20(2.5×8)
Beam No. | 1 | 1 | 8
Perveance (µP) | 0.65 | 0.25 | 1.6(0.2×8)
Efficency (%) | >70 | >80 | >80
Power(kW) | 800 | 800 | 800(100×8)

## Slide 47
1 group 1 day can alignment 2 difficult components / 4 common components.
If 1 group 1 day alignment 3 components, it will take 1 group 17057 days to finish 51170 components alignment
The total length of tunnel control network is about 101610m.
1 group 1 day can measure 4 stations+4 stations repeat measurement, the length of 4 stations is about 24m.
It will take 1 group 4234 days to finish tunnel control network survey.
How many time spend for alignment depends on how many groups we can have.

## Slide 48: Key techniques and researches
Develop automatic observation system to improve tunnel survey efficiency
Integrates an automatic mobile platform and an vision instrument.
The automatic mobile platform mainly includes an omnidirectional mobile module, an elevating module, a self-balancing module, a power supply module and some control modules. It can be guided by a reflective stripe on the tunnel ground and provides a suitable position for vision instrument measurement.
Automatic observation system
Trace

## Slide 49
（1）Critical technical problems
Comprehensive exploration technology for long distance complicated underground engineering.
Prevention and treatment technology study for underground water.
The design and construction of long distance tunnel under complicated geographical conditions and large-span underground caverns.
The construction management of complicated underground engineering.
Integration of long distance tunnel ventilation, ventilation and air conditioning system and smoke control system.
The development, manufacturing and application of TBM.

## Slide 50
The waterproofing grade of underground caverns of the Project is Grade I.
Waterproof materials include waterproof membrane, waterproof coating, rigid waterproof material, and concrete admixture etc.
The study in the next stage will focus on new types of waterproof materials, which meet the waterproofing engineering requirements and are at lower costs.
Waterproof Study