## Slide 1: Distinguish signal and background using simple features
Long Peixun
2018.9.20

## Slide 2: Outline
Data used for machine learning
  Data for training
  Data for test
Data distribution analyze
  Distribution display
  Features will be used in machine learning
  Some abnormal events
Machine learning model
Result
  Test result
  Curves
  Background removal display
Summary

## Slide 3: Data used for training
37169 events, hits.
Signal
  round11, BBhabha
  171208, 171209, 171210, 171211
Background
  Random trigger
  Runno = 52944
Mix signal and background

## Slide 4: Data used for test
9276 events, hits.
Signal
  round11, BBhabha
  171212
Background
  Random trigger
  Runno = 52944
Mix signal and background

## Slide 5: Overall distribution

## Slide 6: Rawtime and ADC in an event
Event ID = 38238

## Slide 7: Simple features
Features will be used in machine learning
  Layer
  Rawtime
  ADC
Only 3 features?
  Use simple features as a reference for further research.

## Slide 8: Some abnormal events

## Slide 9: Machine learning model
Neural network
2 inner layers, 32 nodes per layer.
Input: 3 features (layer, rawtime, ADC)
Output: [0, 1]
Epoch = 1, batchsize = 128

## Slide 10: Test Result
Require signal reserve rate (Recall) > 99%
Threshold = 0.25
Test result:
  Test 1127273 samples, 822229 correct, 72.93965170814877 %
  label signal: 704403 true signal: 698026
  Signal reserve: 99.09469437239761 %
  label background: 422870 true background: 124203
  Background removal: 29.371438030600423 %
  TP: 698026 FN: 6377
  FP: 298667 TN: 124203

## Slide 11: P-R curve and ROC curve
P-R curve
ROC curve

## Slide 12: Background Removal – Signal Reserve

## Slide 13: Background removal display
Evend ID = 31213

## Slide 14: Background removal display
Evend ID = 40525

## Slide 15: Background removal display
Evend ID = 218346

## Slide 16: Summary
Just using simple features, the background removal effect is not good (~30%).
Next plan
  Use “clearer” training data.
  Consider more features, for example, neighbors’ features.
  Use “clustering” to get overall structure of each event.
  Cross validation.