## Slide 1: Room Temperature Surface Muon Beam line at EMuS
Luping Zhou
2018/11/21
China Spallation Neutron Source

## Slide 2: Outline
1. Overview
Current international muon beam line for μSR experiments
2. Design of baby-scheme muon beam line
  Optical design
  Multi-particle simulation without momentum spread
  Multi-particle simulation using the beam from the proton bombardment on target
3. Vertical muon beam line design(Baseline)
  Optical design
  Multi-particle simulation without momentum spread

## Slide 3: Overview

## Slide 4
Muon Beams Worldwide
 | Surface muon beamline | Magnitude of flux | Beam spot | Contamination | Momentum distribution
J-PARC, MUCE | D-line，S-line | 1.0E+07 | 30mm(H)*40mm(V) | -- | ~15%
ISIS muon facility | ISIS-Emu | 1E+06 | 10~30mm(H)*10mm(V) | e+/μ+<0.15 | 7%, centered at 27MeV/c
 | RIKEN-port2 | 1E+06 | Ø10~50,adjustable | -- | 
PSI-SμS | πE3 | 1.0E+07 | 15mm(H)*30mm(V) | e+/μ+：1%~2% | 8%,centered at 28MeV/c
 | μE4 | 1.0E+08 | 25mm(H)*35mm(V) (WSX-off) | e+/μ+：1% | 1.8%~11%
TRIUMF-CMMS | M13 | 1.0E+05 | 30mm(H)*20mm(V) | -- | 20~30MeV/c
 | M15 | 1.0E+06 | 12mm(H)*16mm(V) | -- | 19~40MeV/c
Performance of different room temperature muon beam line:
Our Goal: Limited by cost, proton beam power and space, however we still expect to have at least 1.0E+05/s rate with a proper beam spot, low contamination and high polarization

## Slide 5: Design of Baby-Scheme Muon Beam-line

## Slide 6
Beam Line Scheme
Baby-scheme muon beam line design
A simplified muon beam called ‘Baby-scheme muon’ will be located at High-energy Proton Experimental Area(HPEA)
Notes: 换图

## Slide 7
Target
According to previous research, a graphite target with a size of 10(L)*5(H)*1.5(W) was used to obtaining a higher production of surface muon
Baby-scheme target station
Surface muon yields for different target materials from a collector at 60 cm from the left lateral side of target vs. positions of the left edge of target relative to the beam axis.*
*Use a thick target to compensate for the low surface production due to low- power proton beam(5kW)
*Jing H T, Meng C, Tang J Y, et al. Production target and muon collection studies for an experimental muon source at CSNS[J]. Nuclear Inst & Methods in Physics Research A, 2012, 684(684):109-116.

## Slide 8
Primary Surface Muon Distribution
TWISS parameters of entrance are decided by the phase ellipses
Emittance ellipse decided by:
Maximum envelop: the ‘band’ width
Maximum divergence: ~120mrad
Phase map at 0.4m from the surface of target
Surface Muon (26~29.8MeV/c) | () |  | (m) | () |  | (m) | Intensity (5kW) ()
 | 5200 | -0.7 | 0.54 | 3000 | -1.55 | 0.71 | 3.2E+06
Surface Muon (26~29.8MeV/c) |  |  |  |  |  |  | 
 | 5200 | -0.7 | 0.54 | 3000 | -1.55 | 0.71 | 3.2E+06
approximately uniform distribution
Notes: 表格标题栏调大

## Slide 9
Optical Design
Using Graphic TRANSPORT to obtain approximate data of the lattice parameters of beam line

## Slide 10
Parameter Optimization
Optimized partial magnet parameters in multi-particle simulation(G4beamline), even the fringe field is included.
Resultant lattice parameters of iterative optimization.
 | Length [mm] | Inner Aperture (Width & Height) [mm] | Field | Focus direction
Q1 | 300 | Diameter=400 | 1.685kG | Vertical
Q2 |  |  | 1.498kG | Horizontal
Q3 |  |  | 1.276kG | Vertical
Q4 |  |  | 1.347kG | Horizontal
Q5 |  |  | 1.171kG | Horizontal
Q6 |  |  | 1.148kG | Vertical
Q7 |  |  | 1.200kG | Horizontal
Q8 |  |  | 1.800kG | Vertical
Q9 |  |  | 1.650kG | Horizontal
Bend Magnet (RB1&RB2) | 494.3 | W=500 H=300 | 0.978kG | 
Wien Filter |  | W=H=400 | E=2MV/m B=260G | Horizontal deflection
 | Length [mm] | Inner Aperture (Width & Height) [mm] | Field | Focus direction
Q1 | 300 | Diameter=400 | 1.685kG | Vertical
Q2 |  |  | 1.498kG | Horizontal
Q3 |  |  | 1.276kG | Vertical
Q4 |  |  | 1.347kG | Horizontal
Q5 |  |  | 1.171kG | Horizontal
Q6 |  |  | 1.148kG | Vertical
Q7 |  |  | 1.200kG | Horizontal
Q8 |  |  | 1.800kG | Vertical
Q9 |  |  | 1.650kG | Horizontal
Bend Magnet (RB1&RB2) | 494.3 | W=500 H=300 | 0.978kG | 
Wien Filter |  | W=H=400 | E=2MV/m B=260G | Horizontal deflection
A K-V distribution similar to the surface muon from target is used as a primary test beam

## Slide 11
Beam Loss
Using K-V distribution particles without momentum spread, a 88% transmission efficiency is presented

## Slide 12
Simulation Using Beam from Target
Profile of beam spot when Y=0 or X=0
Momentum spectrum
FWHM of beam spot : >60mm
FWHM of momentum distribution: <3MeV/c (relative to 28.5MeV/c, ~ 10% )
flux within FWHM larger than 1.2E+06/s(5kW)

## Slide 13
Collimation 1
Momentum Collimation
Goal: eliminate the so-called ‘cloud muon’
Method: considering the normalized dispersion function
By collimation, a fraction of 10% cloud muon in beam spot reserved
Pol-Z about -0.92

## Slide 14
Collimation 2
Removal of positrons
Goal: eliminate the positrons contaminating in the muon beam
Method: ‘Wien Filter’+ a collimator
*
However, limited by the space after the wien filter, a collimator is placed before next quadrupole to eliminate the positrons
Location of wien filter
*Prokscha T, Morenzoni E, Deiters K, et al. The new μE4 beam at PSI: A hybrid-type large acceptance channel for the generation of a high intensity surface-muon beam[J]. Nuclear Inst & Methods in Physics Research A, 2008, 595(2):317-331.

## Slide 15
Collimation 3
Shrink beam spot by slits
Goal: a smaller and adjustable spot required by experiments
Method: mainly depending on the π phase shift
The transfer matrix between two points and in the beam line could be expressed as
When (n = 0, 1, 2…), the size of envelope of would be multiple times of the size of
 | Z Position | Slit Width | Collimation Direction
Slit-1 | 3970mm | 50mm | vertical
Slit-2 | 6620mm | 80mm | horizontal
Slit-3 | 7839mm | 100mm(Horizontal) &60mm(Vertical) | horizontal &vertical
Non-effective for particles influenced by nonlinear effect

## Slide 16
Collimation 3
A possible smaller spot
FWHM for profile: 30mm
rate within FWHM-----larger than 1.2E+05/s(proton beam 5kW)
Shrink beam spot by slits
Goal: a smaller and adjustable spot required by experiments
Method: mainly depending on the π phase shift
Notes: 按collimation1改

## Slide 17: Vertical Muon Beam Line Design (Baseline)

## Slide 18
Scheme
Baseline-scheme design
Vertical conventional surface beam with a thin target
SC solenoidal muon beam line
Vertical Beam Line
Notes: 图墙删掉，看竖直的立体关系

## Slide 19
For a thin target with an equivalent thickness of 1 cm, the maximum envelop is 25mm according to the point A and B in the surface muon phase map
Phase map at 30cm from the surface of target
A K-V distributed particles with maximum envelop=25mm and maximum divergence=100mrad was used for test
Primary Surface Muon Distribution

## Slide 20
Optical Design
Limited by space, 300mm diameter of first two quadrupoles is used.
Linear optics was done by using GRAPHIC TRANSPORT
Horizontal and vertical dipoles are used to obtained a better momentum collimation

## Slide 21
Multi-particle Transmission Using K-V Distribution
The multi-particle simulation was done by using G4beamline. All the magnets and tubs are slightly adjusted for a better performance
Triplet, once used in baby-scheme muon beam
Bending on both transverse direction for a better momentum collimation
Transport efficiency:84%

## Slide 22
Results
Beam Spot
Projection of beam spot on X-axis & Y-axis
Slightly larger beam spot
Transverse Direction | Sigma(mm) | FWHM(mm)
x | 13.6 | 46.0
y | 15.8 | 38.0
X-Y
X-X’
Y-Y’

## Slide 23
Collimation
Slits for smaller spot
 | Z Position | Slit Width | Collimation Direction
Slit-1 | 8900mm | 60mm | horizontal
Slit-2 | 12900mm | slit ≤ -25 | vertical
Slit-3 | 13050mm | slit ≥ 25 | vertical
FWHM=28mm
FWHM=28mm
Notes: 跟前面一样，说明下效率等

## Slide 24
Summary
Beam Line | Reference momentum [MeV/c] | Momentum Spread | Polarization | Intensity [1E5/s] | Spot(FWHM) [mm] | Contamination
Muon Beam Line for Baby-Scheme Design | 28.5 | ~10% | -0.92 | 1.2 | 31.2(H)*32.5(V) | e+ < 1%
Vertical Beam Line for Baseline-Scheme Design | 28 | ＜8% | -0.94 | 0.6 | ~30(H)*30(V) | --

## Slide 25
Summary
Two room temperature muon beam line is designed for EMuS. One is for baby scheme design and another is for baseline scheme design
For baby-scheme design , there is a simplified muon beam line. For this beam line now it has a suitable beam spot(FWHM=30mm) , 1E+05/s flux under 5kW proton beam and polarization is high enough(-0.92), while the contamination is rather low(<1%)
For vertical beam line of baseline design, the primary result shows that the finished design could deliver about 84% of particles in emittance ellipse to the final spot. After 3 groups slits, the spot could be further minified to 30mm(FWHM). However, more detailed simulation work is required in the next step
Notes: 不要括号

## Slide 26
Thank you!