## Slide 1: Overall Design of EMuS
Yuan Ye
IHEP
20181120@CSNS
International Review on the Conceptual Design of EMuS

## Slide 2: Outline
Question and solution
Keypoints of design
Summary

## Slide 3: Question
How to make EMuS be an
attractive & cost effective
project based on 5KW proton beam?
Parameters | CSNS-I | CSNS-II
Linac Energy (MeV) | 80 | 250
RCS Energy (GeV) | 1.6 | 1.6
Power (kW) | 100 | 500
Power for EMuS (kW) | 5 | 25

## Slide 4
Conventional muon beam line
Thin target Different to spallation target
Side capture
Solution:
We can use thick target !
To improve secondary particle capture efficiency

## Slide 5: Improve capture efficiency
Put target inside solenoids

## Slide 6: Adiabatic field capture
P2T / B = C
conservation of
magnetic moment
PL-> PT

## Slide 7: Demonstrated by MUSIC @2011
A factor of 1000 achieved than conventional method
108/s for 1MW @PSI
Large acceptance, wide momentum range

## Slide 8: Projects for mu-e conversion
COMET @J-PARC:
Mu2e @ FNAL

## Slide 9: EMuS
Surface muon mode: 29MeV/c
μSR, slow muon, muonium，…
Decay muon mode: 40-150MeV/c
μSR，
High momentum muon mode: 200-450MeV/c
μ imaging, neutrino physics…
Figure of Merit
μSR: IP2=Intensity * Polarization2
Others: Intensity
Competitive & Multi-purpose muon source
A difficult design， big challenge for us

## Slide 10: Keypoints of design
Target station
Magnetic field, Geometry, Flexbility
Proton beamline
Combine with TS, Spent proton beam
Muon beamline
Large emittance, Wide momentum range,
Charge & momentum selection
Detector
Large spot, Relatively low polarization

## Slide 11: COMET & Mu2e
5T
Backward collection
Small size rod like target
Thick shield to protect Magnet

## Slide 12: Backward or Forward?
High intensity and high momentum are essential to EMuS
Forward collection is chosen
pions per p.o.t.
frontward
backward
0.222 < p (GeV/c) < 0.776

## Slide 13: Spent proton beam extract
To make all the solenoids same radius is expensive, so a 4-coils/3-steps, 15o tilt angle geometry is chosen ( see details in Hou Zhilong’s report)
The detailed size of station depend on radiation and energy deposit ( see Zhao Guang’s report)
13
Proton beam distribution
SC1 + shielding
SC2 + shielding
SC3 + shielding
SC4 + shielding
MS + shielding

## Slide 14: Flexible magnetic field
We found different magnetic field curve is needed for different run mode, especially for surface muon (see Nikos Vassilopoulos’s report)
This bring new requirements to Magnetic & proton beam design
 | μ+ with 27 < P < 29.8 MeV/c emittance = 10000 π mm mrad |  |  | 
B (T) | 1t0.5 | 2t1 | 3t1.5 | 5t3
i (x106) μ/sec | 3 | 4 | 4.8 | 8.2
<Polz> % | .75 | .45 | .25 | .22

## Slide 15: Adjustable proton beamline
Extraction hole for surface muon mode（ 2 T ）
Extraction hole for decay muon mode（ 5 T ）
Correction dipoles are needed
to make proton beam hit target correctly and extracted to beam dump safety ( see Chen Yukai’s report)

## Slide 16: Multi-mode muon beamline
Large aperture, SC solenoids for large emittance (see Bao Yu’s report)
μSR muon section
pion decay section
Decay muon section
Charge/momentum selection for pion/decay muons
2nd selection,
decay muons

## Slide 17: More consideration
Larger conical target for better μSR rate than cylindrical ones
An extra high-polarization thin target

## Slide 18: Baseline scheme: Target station
protons
protons
μ+
SC1
SC2
SC3
SC4
MS1
π+
π+
Thin target
Main target

## Slide 19: Baseline scheme: layout
Vertical beamline for thin target
Beam dump
Main target station
Proton beamline
Main muon beamline

## Slide 20: Baby scheme
Message from funding agency: EMuS may not be done in one step, a modest goal μSR project as first step
Conventional side collection solution
Reusable

## Slide 21: Parameters
 |  | Ref. momentum | High-intensity |  |  | High-polarization |  | 
 |  |  | Intensity(1E6/s) | PolZ | SpotFWHM (mm) | Intensity (1E6/s) | PolZ | SpotFWHM (mm)
Surface muon | Baseline- scheme SC surface muon | 29 | 74 | -0.51 | 96×96 | 24 | -0.74 | 72×80
 | Baby-scheme muon | 28.5 |  |  |  | 0.12 | -0.92 | 31.2*32.5
 | Baseline-scheme vertical muon |  |  |  |  | ~0.06 | -0.94 | ~30*30
Decay muon |  | 45 |  |  |  | 25 | 0.68 | 88×88
 |  | 150 | 400 | 0.53 | 60×60 | 50 | 0.73 | 60×60
High-momentum muon |  | 450 | 130 |  | 72×76 |  |  | 
Momentum spread for decay muon and high-momentum muon is ±6.7%

## Slide 22: Detector
The beam spot is large
The muon beam intensity per pulse is relatively high，
polarization is relatively low
The repetition rate is low-2.5Hz
To get good performance
Fly-past sample environment
Reducing the count rate of
positrons in usage of degrader
Small radius ring, small size scintillator,
SiPM
(see Pan Ziwen’s report)
2560Scintillator + SiPM

## Slide 23: Summary
A competitive muon source project is designed
Looking forward comments and ideas to improve
our design and finally lead to a success project
Thanks!