## Slide 1: Target System Studies Experimental Muon Source
Nikos, IHEP, CAS

## Slide 2: layout
Talk about the optimization of the 3 different targets for the Experimental Muon Source:
Baseline scheme targets:
muon and pion collection with 4-coils/3-steps Superconducting Adiabatic Solenoid
  Graphite conical target
  150 tilt angle
  capture for surface muons and pions/decay muons
  comparison between FLUKA (used as default MC) and G4
highly polarized surface muons with thin target
Baby scheme target
typical Graphite slab used in singlet, doublet or triplet configurations
Aim
produce a competitive number of muons for μSR applications
a rate of 106 – 107 for surface muons / second and higher for decay muons under certain emittance selection criteria

## Slide 3: baseline scheme: Superconducting Capture solenoid for surface and decay muons
25 m superconducting transport solenoid
“surface” muon section
pion decay section
Decay muon section
Charge/momentum selection for pion/decay muons
2nd selection,
decay muons
secondary beam operation modes (independent):
surface muon mode for μSR physics @ 1 T
  Ref. Pμ=25-29.8 MeV/c
decay muon mode @ 5 T
  Ref. Pμ = 40, 150 MeV/c for higher energy μSR physics, and muon imaging
  Captured pions ref. Pπ = 100, 260, 450 MeV/c Momentum spread: <± 10%
neutrino mode (optional) @ 5 T
  Wide energy spectra
  Ref. Pπ=260-500 MeV/c
Superconducting Capture Solenoid

## Slide 4: proton and target parameters
proton beam parameters |  | 
Ekin (GeV) | σ (cm) | Power (kW)
1.6 | ~ 0.5 at target, double Gaussian | 5
target parameters for the cylindrical shape |  |  |  | 
material | radius r1 large / r2 small (cm2) | length (cm) | Z | λI (cm)
C (1.82 gr/cm3) | 4.5 / 0.25 | 30 / 0.65 λI | 6 | 47
r1
r2
Graphite
Graphite is a common material used in neutrino and muon beams
lower neutron radiation due to low Z
30 cm length is optimized for coil radiation protection, power deposition in the Superconducting Solenoid
other material as Be or SiC have been considered and studied

## Slide 5
several adiabatic tapers are suggested for the surface and decay muon capture
1 or 2.5 -> 0.5 T for surface muon mode
5 -> 3 T for decay muon mode
z(m)
Bz(r=0) T
z(m)
Bz(r=0) T
5 -> 3 T
1 -> 0.5 T
surface muons collection
best π+ (decay muon) collection

## Slide 6
Forward spent-proton extraction, proton beam & target tilted in respect to magnetic axis, θp = 15o
4-coils/3-steps design, NbTi-Al coils, adiabatic taper
Superconducting Capture Adiabatic Solenoid Target System
150 tilt of protons/target with respect to magnetic field lines:
facilitate the extraction of spent-protons with a moderate length of 2.5 m of the CS through the Matching Solenoid and capture coils
lower tilts as 100 make the length of CS excessive due to MS shielding

## Slide 7
polarization (%)
tilt angle
1st coil study – no shielding
no emittance selection
5 -> 3 T
2.5 -> 0.5 T
1 -> 0.5 T
baseline tilt 150
polarization of surface muons
as function of tilt angle/fields
π+ rate as function of tilt angle
5 -> 3 T
  best surface muons polarization at 1 T
  tilt aids π+ capture (also for surface muons)
baseline tilt 150
π+ / s
tilt angle
r1 = 4.5 cm
Graphite
r2 = 0.25 cm

## Slide 8
μSR: surface muon collection at entrance of MS1 at 1 and 2.5 T
surface muon sources
target
shielding
shielding of MS1 act as collimator

## Slide 9
conical target
better surface muon collection
lower power deposition on the SC than the cylindrical one
μ+ with 25 ≤ P (MeV/c) ≤ 29.8
similar polarization
r1 = 4.5 cm
r2 = 0.25 cm
r1
μ+ / s
r1 (σb )
r1 (σb )
Polarization (%)
cone
cylinder
rate and polarization as function of radius r1 (in σb = 0.5 cm)
baseline
10000 π mm mrad
stat. error ~ 5%
no emittance selection
stat. error ~ 1%
10000 π mm mrad selection
no selection

## Slide 10
emittance (π mm mrad) | 10000 |  |  | 
momentum (MeV/c) | μSR - μ+ 25 < P < 29.8 |  |  | 
field | 1 -> 0.5 T |  | 2.5 -> 0.5 T | 
target material | Gr | SiC | Gr | SiC
intensity (x106) μ/sec | 7 | 7 | 18 | 22
polarization | -0.83 | -0.85 | -0.62 | -0.60
surface muon purity (%) | 86 | 85 | 68 | 65
stat. errors for both intensity and polarization < 5% |  |  |  | 
μSR: μ+ collection at MS1
1 or 2.5 -> 0.5 T
1T has the better polarization 83% @ 10000 π mm mrad
2.5 T has the better rates
r1 = 4.5 cm
r2 = 0.25 cm

## Slide 11
μSR: π+ collection for decay muons at entrance of MS1 and 5 T

## Slide 12
r1 = 4.5 cm
r2 = 0.25 cm
r1
baseline for conical
π+ / s
r1 (σb )
π+ / 2 MeV / s
P GeV/c
conical baseline
cylinder best
conical target π+ collection at MS1
slightly less (-10%) collection than cylindrical best
rate as function of radius r1 (in σb = 0.5 cm) and momentum distributions

## Slide 13
π+ / 2 MeV / s
P GeV/c
π+ entering MS1 as function
of different taper shapes at 5T
Slower taper
Baseline
Faster
~100 MeV/c
5T taper variations
5 ->3 T
different adiabatic tapers <-> different momentum selection
5T case
z(m)
Bz(r=0) T
100 MeV/c
450 MeV/c

## Slide 14
π+ / 2 MeV / s
4.5T taper variations
4.5 -> 2.5 T
π+ / 2 MeV / s
P GeV/c
4 -> 2.5 T
P GeV/c
z(m)
Bz(r=0) T
260 MeV/c
260 MeV/c
different momentum selection
4.5, 4 T cases

## Slide 15
π+ / 2 MeV / s
P GeV/c
π+ entering MS1 as function for different taper
5 , 4.5 T taper variations
π+ collection for decay muons
final 5, 4.5 T tapers used for π+ collection
Bz(r=0) T
Z in m
100 MeV/c
450 MeV/c
260 MeV/c
emittance (π mm mrad) | 100000 |  | 
P (MeV/c) ± 10% | 100 | 260 | 450
intensity π+ (x1010) μ/sec | 1 | 2.8 | 2.4
stat. error ~ 1% |  |  | 
100000 π mm mrad

## Slide 16
π+ / 2 MeV / s
P GeV/c
260 MeV/c
100000 π mm mrad
Best 4.5->2.5 T fast
coil design
4.4->2.4 T
Entrance of MS1
π+ / 2 MeV / s
P GeV/c
Exit of MS1
260 MeV/c
100000 π mm mrad
Best 4.5->2.5 T fast
coil design
4.4->2.4 T
the polynomial best field used for optimization can be reproduced with realistic coil design
π+ collection at 260 MeV/c at MS1 entrance/exit

## Slide 17
μ+, 1 T
FLUKA = 2.2x109
G4 (incl) = 2.9x109
μ+ / 2 MeV / s
P GeV/c
Ratio μ+/μ-
FL = 2
G4 = 3.6
For μSR μ+:
FLUKA ~ -30%
Both MCs could be used keeping in mind the difference
G4: Song Yingpeng
Systematics between FLUKA and G4
π+, 5 T
FLUKA = 1.7x1011
G4 (bert) = 2x1011
G4 (incl) = 2x1011
π+ / 2 MeV / s
P GeV/c
Ratio π+/π-:
FL = 1.9
G4 (bert) = 2.9
G4 (incl) = 2.2
For π+:
Total pions are similar with FLUKA and G4 (BERTINI)
FLUKA predicts a ratio π+/π- = 2

## Slide 18
Width = 0.34 cm
Turn = 450
π+
μ+
μ+
μ+
collection surface
r= 16cm
x-axis, 60 cm
protons @ z-axis
Length = 12 cm
Height = 12 cm
Graphite slab | 1 cm p -> Gr interaction |  | 
emittance (π mm mrad) | 4500 |  | 
momentum | μSR - μ+ 25 < P < 29.8 MeV/c |  | 
Target Length x Height (cm2) | 12x12 |  | 
Tilt (degree) | 20 | 30 | 45
intensity (x106) μ/sec | 1 | 0.95 | 0.8
polarization | -0.97 | -0.97 | -0.97
surface muon purity (%) | 98 | 98 | 97
statistical error | ~ 2% / 1% on intensity / polarization |  | 
tilt = 200
collected surface muon vertices at target
4500 π mm mrad selection
only a part of the target is playing a role
we can reduce the target to
Length x Height = 5 x 4 cm2
z (mm)
y (mm)
proton beam @ z-axis
thin tilted target for baseline scheme
target-proton interaction ≤ 1 cm
create highly polarized μSR beam parallel to decay muons mode
quadrupole collection
μ+

## Slide 19
“Baby” scheme, target outside collector only for surface muons
Sideway μSR collection at 900 with respect to the primary proton beam direction
Quadrupole system, low acceptance collector
Aim to maximize the μSR rate at the entrance of quadrupole using FLUKA MC for:
  singlet, singlet-tilt
  doublet (triplet)

## Slide 20
protons
π+
μ+
μ+
μ+
Best Width = 1 or 2 cm
collection surface
(z,y), r= 16cm
x-axis 60 cm
Target | Gr slab – sides : 12x12 cm2 |  |  | 
emittance (π mm mrad) | 4500 |  |  | 
momentum | μSR - μ+ 25 < P < 29.8 MeV/c |  |  | 
Target’s width (cm) | 4 | 3 | 2 | 1
intensity (x106) μ/sec | 2 | 2.4 | 2.8 | 2.9
polarization | -0.88 | -0.91 | -0.94 | -0.96
surface muon purity (%) | 92 | 94 | 96 | 97
stat. error ~ 1.5% for intensity / polarization |  |  |  | 
protons
Length = 12 cm
Height = 12 cm
singlet slab
surface muons rates and polarizations as function of target face width
proton beam peak is centered
rectangular target
length
height

## Slide 21
protons
Length = 12 cm
Height = 12 cm
protons
π+
Width = 3 or 4 cm
μ+
μ+
μ+
collection surface
(z,y), r= 16cm
x-axis, 60 cm
Target | Gr slab – sides : 12x12 cm2, width = 4 cm , σp = 0.5 cm |  |  |  | 
emittance (π mm mrad) | 4500 |  |  |  | 
momentum | μSR - μ+ 25 < P < 29.8 MeV/c |  |  |  | 
Gaussian peak from side surface (cm) | 0 | 0.5 | 1 | 1.5 | 2
intensity (x106) μ/sec | 2.4 | 3.3 | 3.1 | 2.3 | 2
polarization | -0,96 | -0.96 | -0.93 | -0.92 | -0.89
surface muon purity (%) | 97 | 97 | 95 | 94 | 92
stat. error ~ 1.5% for intensity / polarization |  |  |  |  | 
This is the best case compared to singlet-turn, also to doublet and triplet and selection of 4500 π mm mrad, see next pages
singlet slab best case
proton’s Gaussian peak is displaced by 0.5 cm = 1 σp from side (collection) surface

## Slide 22: vertices of all and selected surface muons passing through the collection surface
z (mm)
y (mm)
all surface muons
surface muon
4500 π mm mrad selection
for the given emittance selection target side surface could be reduced from 12x12 cm2
the target of Length x Height = 10x5 cm2 used is probably ok
whole target side surface is displayed, 12x12 cm2
only the first part of the target is playing a role due to emittance selection
z (mm)
y (mm)
proton beam @ z-axis
proton beam @ z-axis
protons
Length (z) = 12 cm
Height (y) = 12 cm

## Slide 23
Target | Gr slab |  |  | 
Selection | μSR - μ+ 25 < P < 29.8 MeV/c |  |  | 
target | BEST singlet with Gaussian peak 0.5 cm from side collection surface | singlet-tilt | doublet | triplet
total intensity (x106) μ/sec | 24 | 31 | 28 | 31
emittance (π mm mrad) | 4500 |  |  | 
intensity (x106) μ/sec | 3.3 | 3.2 | 2.6 | 3.2
polarization | -0,96 | -0.96 | -0.95 | -0.95
surface muon purity (%) | 97 | 96 | 97 | 96
stat. error ~ 1.5% for intensity / polarization |  |  |  | 
singlet-tilt case and doublets triplets
total proton – target interaction always at 12 cm
best cases for doublets or triplets
multiplets not shadowing the collection surface

## Slide 24: Conclusions on muon/pion collection
full scheme with 4-coils/3-steps SC solenoid / collection at MS1:
μSR physics with surface muons
1 -> 0.5 T, best for polarization
  7x106 μ+ / s, 83% polarization, 86% surface muon purity @ 10000 π mm mrad
2.5 -> 0.5 T
  1.8x107 μ+ / s, 62% polarization, 68% surface muon purity @ 10000 π mm mrad
one order more for total muon rates
decay muons, π+ collection
5 T for 100 and 450 MeV/c, and 4.5 T for 260 MeV/c
π+ / s ~ ≥ 1010 π+/s @ 100000 π mm mrad
thin target / collection at quadrupole
~ 106 μ+ / s, 97% polarization, 98% surface muon purity @ 4500 π mm mrad
baby scheme / collection at quadrupole:
3.3x106 μ+/s with 96% polarization and 97% surface muon purity @ 4500 π mm mrad
Thanks

## Slide 25: questions
concerning the capture systems
what is the minimum limit of polarization for μSR physics
what is the decay muon best momentum range ?

## Slide 26: extra

## Slide 27: thanks
MOMENT at future:
15 MW cw-proton beam
Leptonic CP-violation
DAR
CC-NSI
EMuS as R&D for MOMENT:
MW Capture system
Pion transport/decay
Charge separation
Muon transport/decay channels
EMuS innovation:
Unique SC capture solenoid (5T max.)
Forward capture & spent proton extraction
Coils will be made by Chinese industry

## Slide 28: muon yields as function of target tilt and length (exit of 1st coil, no-shield)
Total surface muons 108 / second
Polarization along beam axis ~ 80-82%
15o
For baseline target

## Slide 29
 | μ+ with 27 < P < 29.8 MeV/c – εx and εy = 10000 π mm mrad |  |  |  |  |  |  |  |  |  |  | 
 | cone, r1 = 8 cm, r2 = 4σb, σb = 10 mm (max ~ 12% / 8% / 8% error on ip2 / i / Polz) |  |  |  |  |  |  |  |  |  |  | 
B (T) | 1t0.5 |  |  | 2t1 |  |  | 3t1.5 |  |  | 5t3 |  | 
type | cub. | 1st coil | fast | cub. | 1st coil | fast | cub. | 1st coil | fast | cub. | 1st coil | fast
ip2(x106) | 1.7 | 1.8 | 1.7 | .8 | 1.8 | .9 | .3 | 1.4 | .2 | .4 | 1.4 | -
i (x106) μ/sec | 2.9 | 2.7 | 3 | 4 | 3.6 | 3.5 | 4.8 | 4.3 | 3.8 | 8.2 | 4.8 | 
<Polz> % | .76 | .81 | .75 | .45 | .71 | .51 | .25 | .57 | .23 | .22 | .54 | -
Field Study, 1 T to 5 T
μ+ with 27 < P < 29.8 MeV/c
1 T field is the best case
1st – coils are also good

## Slide 30: μSR and decay muons at matching solenoid entrance
μ+/s/2MeV
P(MeV/c)
Total muons
Only surface muons
from DAR at target
1->0.5T
Beam operation modes (independent):
Surface muon mode (baseline)
  Ref. Pμ=29 MeV/c
  Momentum spread: <±5%

## Slide 31
150 tilt of protons/target with respect to magnetic field lines
not influence the collection of the pion due to the short length of the target
facilitate the extraction of spent-protons with a moderate length of 2.5 m of the Superconducting Solenoid though the Matching Solenoid and capture coils

## Slide 32
decay muons require pion capture momentum at 100, 260 and 450 MeV/c
+ or – reflects spin direction of “forward” and “backward” muon
muon momentum MeV/c
pion momentum MeV/c
μSR muon section
pion decay section
Decay muon section
Charge/momentum selection for pion/decay muons
2nd selection,
decay muons
π+ momentum selection for decay muons

## Slide 33: π+ capture for decay muons μ+ : change the field intensity and shape in order to collect required pions
5 T taper variations
Bz(r=0) T
Z in m
5 -> 3 T
P ± 10% (MeV/c) | 128 |  |  | 225 |  | 
Taper (T) | 4f | 4.5f | 5f | 4f | 4.5f | 5f
i x 109 (π+ /sec) | 8.6 | 9.7 | 12 | 19 | 20 | 13

## Slide 34: Faster adiabatic tapers can increase the polarization, 25 ≤ P (MeV/c) ≤ 29.8 example at 2.5 T
slow
baseline
fast
1
2
3
4
5
MS1 entrance
field variations 2.5 -> 0.5 T
Field case
3% statistical error
polarization (%)
baseline
10000 π mm mrad

## Slide 35: Systematics from monte-carlos: μ+ and μ- with FLUKA and G4 (BERTINI) at MS1, 1 Τ
Same baseline 1T taper used on both
μ+, 1 T
FLUKA = 2.2x109
G4 = 2.9x109
μ-, 1 Τ
FLUKA = 1.1x109
G4 = 0.8x109
μ+ / 2 MeV / s
P GeV/c
μ- / 2 MeV / s
P GeV/c
Ratio μ+/μ-
FL = 2
G4 = 3.6
For surface muons
FLUKA -25%
FLUKA predicts again a ratio μ+/μ- = 2
Momenta distribution similar
Both codex could be used keeping in mind the difference
G4: Song Yingpeng

## Slide 36: Systematics from monte-carlos: π+ and π- with FLUKA and G4 (BERTINI, INCL) at MS1, 5 Τ
Same baseline 5T taper used on both
π+, 5 T
FLUKA = 1.7x1011
G4 (bert) = 2x1011
G4 (incl) = 2x1011
π-, 5 T
FLUKA = 0.9x1011
G4 (bert) = 0.7x1011
G4 (incl) = 0.9x1011
π+ / 2 MeV / s
P GeV/c
π- / 2 MeV / s
P GeV/c
Ratio π+/π-:
FL = 1.9
G4 (bert) = 2.9
G4 (incl) = 2.2
Total pions are similar with FLUKA and G4 (BERTINI)
G4(INCL) produces more pions
The distribution at the high momentum peak is similar
FLUKA predicts a ratio π+/π- = 2
G4 bert
G4incl
G4: Song Yingpeng

## Slide 37: FLUKA vs MARS vs HARP
FLUKA is in agreement with MARS and HARP data @ Ek = 2.2 GeV

## Slide 38: “Baby” scheme, μSR - μ+ 25 < P (MeV/c) < 29.8
p
rectangular target
p
π+
μ+
μ+
μ+
Available “good” magnetic field radius = 16 cm
Target | Slab, Height x Length = 24x24 cm2, Width = 8 σp |  |  |  |  | 
ε (π mm mrad) | 4500 |  |  |  |  | 
material | Gr | SiC | Be | Ti | Cu | W
Lt / λΙ | 0.5 | - | 0.57 | 0.86 | 1.6 | 2.4
intensity (x106) μ/sec | 3.4 | 5.4 | 4.5 | 5.5 | 9.4 | 8.5
polarization | -0.94 | -0.94 | -0.94 | -0.94 | -0.94 | -0.92
surface muon purity (%) | 96 | 96 | 96 | 96 | 97 | 96
statistical error | < 2% on intensity, < 1% on polarization |  |  |  |  | 
60 cm
Target material | Slab Gr, Width = 8 σp |  | 
ε (π mm mrad) | 4500 |  | 
Target, (Height x Length) | 6x6 | 12x12 | 24x24
intensity (x106) μ/sec | 2.9 | 3.3 | 3.4
polarization | -0.96 | -0.96 | -0.94
surface muon purity (%) | 98 | 97 | 96
statistical error | < 2% on intensity, < 1% on polarization |  | 
different target materiel performances
different Graphite target sizes performances
μSR @ 4500 π mm mrad
μ+/s: max for Cu ~ 107
polarization: 94%
12x12cm2 is similar to 24x24cm2 due to small emittance selection/ quadrupole acceptance
length
height
width
μSR beamline, Zhou Luping/IHEP

## Slide 39: turned-singlet, proton – target interaction 12 cm
best
different turn angles in respect to proton beam and widths
side-surface Length x Height from 12x12 cm2 -> 24x24 cm2 due to singlet and turn
protons @ z-axis
Best, Length x Height x Width = 24x24x2 cm3, turn = 100
μSR (25 MeV/c – 29.8 MeV/c)
  3.1 x107 μ+/s, +30%
μSR (25 MeV/c – 29.8 MeV/c), 4500 π mm mrad
  3.2 x106 μ+/s, -9%
  <p> 96%, purity 97%
Width = 6 cm
Turn = 300
Width = 4 cm
Turn = 200
Width = 2 cm
Turn = 100
Width = 1 cm
Turn = 50
π+
μ+
μ+
μ+
collection surface (z,y)
r= 16cm
x-axis, 60 cm
Schematics only
protons @ z axis

## Slide 40: zz‘ phase space on the /target beam axis z is split into two with doublet (three with triplet)
doublet underperformance:
selected μSR μ+ from only one ellipse at zz’ ez .and. ey @ 4500 π mm mrad
z‘ (mrad)
zz’ at the collection surface
zy vertex at of selected surface muons
y (mm)
proton beam @ z-axis
only surface muons from
the first target due to
the emittance selection
y‘ (mrad)
y (mm)
yy’ at the collection surface
z (mm)
z (mm)

## Slide 41: Doublet, selected μSR μ+ from two ellipses at zz’ (ez1 .or. ez2) .and. ey @ 4500 π mm mrad
z‘ (mrad)
z (mm)
zz’ at the collection surface
zy vertex at targets of selected surface muons
z (mm)
y (mm)
both targets are contributing
by selecting both ellipses
Best, Length x Height x Width = 2 x 12x12x2 cm3, turn = 400
μSR (25 MeV/c – 29.8 MeV/c), 4500 π mm mrad
  4.8 x106 μ+/s , +37%
  <p> 95%, purity 96%
proton beam @ z-axis

## Slide 42: Doublet, phase spaces zz’, yy’ at collection surface (ez1 .or. ez2) .and. ey @ 4500 π mm mrad
z‘ (mrad)
z (mm)
zz’ at the collection surface
y‘ (mrad)
y (mm)
yy’ at the collection surface

## Slide 43
protons ~52%
protons 100%
CS1 shield
thickness:
25 cm
MS1 aperture:
25-30 cm
Tungsten
MS1-shield thickness: 50 cm
π+
π+
SC1
SC2
SC3
SC4
MS1
π+
π+
π+
π+

## Slide 44
protons ~52%
protons 100%
CS1 shield
thickness:
25 cm
MS1 aperture:
25-30 cm
Tungsten
MS1-shield thickness: 50 cm
π+
μ+
π+
μ+
π+
μ+
SC1
SC2
SC3
SC4
MS1
μ+
μ+
μ+
μ+
μ+

## Slide 45: additionally highly polarized μSR beam concept short interacting ( ≤ 1 cm ) thin target upstream of capture solenoid
MS1 aperture:
25-30 cm
π+
π+
SC1
SC2
SC3
SC4
MS1
π+
π+
π+
π+
protons ~ 100%
protons ≥ 98%
protons ~ 50%