## Slide 1: Muon beam transport based on SC solenoids
International review of EMuS
Nov. 20-21, 2018, CSNS, Dongguan
Yingpeng Song, Yu Bao

## Slide 2: Outline
Beamline introduction
Beamline design
  Surface muon beamline design
  Decay muon & high-momentum muon beamline deisgn
Conclusions

## Slide 3: Beamline introduction
CSNS/RCS
Operation modes :
Surface muon
  Ref. Pμ=29MeV/c
Decay muon
  Pμ =40-150MeV/c
High-P muon
  Pμ=200-450MeV/c

## Slide 4: Challenges and possibilities
For μSR applications, users want
  High polarization
  High muon intensity
  Small beam spot
Challenges for beamline design
  Proton beam
    stand-alone
  Target thickness and geometry
    30cm,conical
  Collection method
    inner target
  Beamline
    solenoid
Detailed design in Nikos’s talk
Cloud muon contamination
Momentum selection
Spin procession
Beam spot focusing
Possible ways to
improve intensity
5kW

## Slide 5: Trunk design
 | particles | Ref. momentum | dp/p
Surface muon | + | 29 MeV/c | ±7.1%
Decay muon | +/+或/ | 40-260 MeV/c | ±10%
High-P muon | +/+或/ | 200-450 MeV/c | ±30%
Compatible for three different running modes
--- realized by adjusting currents in solenoids
Pπ =230 MeV/c case
Objective

## Slide 6: Surface muon beamline design
Ref.=29 MeV/c; dp/p=±3.5%; acceptance=30 πmmrad
  Intensity >1E6/s
  Polarization >80%
  Positron <10%
  dp/p <15% (FWHM)
  Beam spot FWHM ~30mm
Objectives:

## Slide 7: Multi-particle simulation
 | TURTLE | G4BL (ideal beam distribution) |  |  |  | G4BL (target) | 
 |  | w/o | w | w/o | w | w/o | w
distribution | Gaussian | Gaussian | Gaussian | K-V | K-V | target | target
order | 3 | full | full | full | full | full | full
transmission | 97% | 81% | 93% | 57% | 73% | 38% | 60%
Particles in R=50 mm | 73% | 57% | 71% | 22% | 31% | 20% | 26%
Equivalent field
Transmission optimizing
Optimization works for specified issues (e.g. momentum selection, positron elimination)
High-order effects make the beamline design much more complicated
we need
w and w/o means with or without fieldmap optimization

## Slide 8: Acceptance test
High-order effects reduce the acceptance
  Hollow-distributed beam adopted

## Slide 9: Positron elimination
Wien Filter is adopted for positron elimination -- Separator
The spin will precess in the magnetic field -- Spin Rotator
collimators
The procession angle is ~20°

## Slide 10: Beam spot
The focal plan is tilted for different emittance particles (Fig.1) and off-momentum particles (Fig.2).
Beam percentage in Φ100mm VS distance away from last solenoid
Fig.1
Fig.2

## Slide 11: Beamline layout and fieldmap
Layout adjustments compared with optics design:
1. B2 30°--45°
  --for momentum selection
2. Drifts 1.0 – 1.5m
  -- for positron elimination
 | placement | gepmetry
CM1 | z=15086 mm x=200 mm y=-200 mm rotation=Z45° | square a=283 mm
CM2 | z=17236 mm x=y=0 | ring R1=250 mm，R2=300 mm
CM3 | z=18486 mm x=y=0 | ring R1=160 mm，R2=300 mm
CM4 | z=18786 mm x=y=0 | ring R1=100 mm，R2=300 mm
Collimators for momentum selection and
positron elimination

## Slide 12
 | EMuS （1T） | μE4@PSI WSX-on | μE4@PSI WSX-off | ISIS | D-Line@J-PARC | H-Line@J-PARC
Proton beam power (MW) | 0.005 | 1.3 | 1.3 | 0.2 | 1.0 | 1.0
μ momentum (MeV/c) | 29.8 | 29.8 | 29.8 | 29.8 | 29.8 | 29.8
Intensity (1E6/s) | 23.7 | 420 | 21 | 1 | 10 | 100
Polarization | ~0.75 | ~0.9 | ≥0.95 | ≥0.95 | ≥0.95 | ~0.9
IP2 (1E6/s) | 13 | 340 | 20 | 0.8 | 8 | 81
dp/p (FWHM) | 15.2% | 5~9.5% | 1.8~11% | 10% | 15% | 
x (FWHM) | 72 mm | 65 mm | 24 mm | ~30 mm | ~30 mm | 
y (FWHM) | 80 mm | 26 mm | 30 mm | ~30 mm | ~40 mm | 
Surface muon parameters on different facilities

## Slide 13: Decay muon beamline design
Ways to obtain high polarized decay muon beam
Pion momentum selection ---> make decay muon IP2 maximized
Decay solenoid for pion decay ---> wide momentum acceptance
Muon momentum selection ---> make IP2 maximized
1
2
3

## Slide 14: Layout of decay muon beamline
New issue：widespectrum
Ways to improve momentum selection ability
Increase the drift length between B2 and adjacent solenoids
Set By of B2 away from the reference momentum

## Slide 15
The beamlines are optimized based three pion momentum points, 100,
260 and 445 MeV/c, the corresponding muon momentum is 45, 150, 450 MeV/c.
  Intensity >1E6/s
  Polarization >70%
  Positron <10%
  dp/p <15% (FWHM)
  Beam spot FWHM ~30mm
Objectives:
For high-momentum muon, we only need intensity requirement.

## Slide 16: Matching strategies in G4BL
S1
S2
Adjust S1 and S2 to match the beam to the straight
Matching strategies:
Initial beam distribution analyses
Choose (x, x’, y, y’) parameters that can present initial beam well
Adjust S1 and S2 to make the ideal beam get a good transmission (>85% depend on the parameters we chose)

## Slide 17: Initial pion distribution analyses
From target station (Pπ =260 MeV/c case)
260 MeV/c

## Slide 18: Acceptance of straight decay channel
Original:
  InnerRadius=150 mm
  OuterRadius=160 mm
  Current=150A/mm2
  Max field = 1.6 T
New:
  InnerRadius=150 mm
  OuterRadius=170 mm
  Current=150A/mm2
  Max field = 3.3 T
Transmission：48%
Transmission：88%
The ideal Gaussian distribution beam are chosen

## Slide 19: High polarization
S1
S2
Collimators are used for momentum selection
R
momentum
Selection performance

## Slide 20
 | EMuS | μE1@PSI | RIKEN-RAL | D-Line@J-PARC
Proton beam power (MW) | 0.005 | 1.3 | 0.16 | 1.0
μ momentum range (MeV/c) | 40-160 | 85-125 | 65-120 | 33-250
Intensity (1E6/s) | 50 | 240 | 1 | 10
Polarization | 0.73 | ~0.75 | ≥0.8 | ~0.8
IP2 (1E6/s) | 27 | 180 | 0.8 | 8
dp/p (FWHM) | 14% | 3% | 10% | 15%
x (FWHM) | 70 mm | 39 mm | ~30 mm | ~35 mm
y (FWHM) | 70 mm | 25 mm | ~30 mm | ~35 mm
Decay muon parameters on different facilities

## Slide 21: Muon beam parameter table for baseline
 | Ref. momentum | High-intensity |  |  | High-polarization |  | 
 |  | Intensity(1E6/s) | PolZ | SpotFWHM (mm) | Intensity(1E6/s) | PolZ | SpotFWHM (mm)
Surface muon | 29 | 74 | -0.51 | 96×96 | 24 | -0.74 | 72×80
Decay muon | 45 | 25 | 0.68 | 88×88 | 25 (2) | 0.68 (0.73) | 88×88
 | 150 | 400 | 0.53 | 60×60 | 50 (7) | 0.73 (0.75) | 60×60
High-P muon | 450 | 130 | - | 72×76 | - | - | -
Momentum spread for decay muon and high-momentum muon is 10~20%(FWHM)
Numbers in () are muons within beam size of Φ30mm

## Slide 22: Conclusions
With inner target nested in superconducting solenoid, we can improve muon beam intensity hugely, with about 15% polarization decrease.
Trunk can operate compatibly by tuning solenoid currents.
For decay muon mode, the high polarization can be reached by sacrificing some intensity.
Beam splitting studies is underway, a promising way to mitigate spin procession and large beam spot.

## Slide 23
BACK UP

## Slide 24: Surface mu yield from target surface
Cylinder VS slab (5*10^8 pronton)
  Cylinder (left): radius=10mm length=300mm, 1.6GeV
  Slab (right): geometry X=6mm Y=40mm Z=40mm, 585MeV

## Slide 25
Beam size
  Scraping with collimators
  Beam split
collimators

## Slide 26: Field check

## Slide 27: High-intensity
Intensity about 4E8/s, polarization about 53%

## Slide 28: High polarization
S1
S2
1
2
S1
B1
S2
S1 and S2 can be adjusted for momentum selection

## Slide 29: High polarization
Polarization can reach 75% with intensity of 5E7, muons from 140 to 160 MeV/c.

## Slide 30: High-intensity mode
Prefer broad momentum spread beam in the decay channel
High-momentum pion elimination
  Collimators
  Reduce
  Intensity >1E6/s
  Polarization >80%
  Positron <10%
  dp/p <15% (FWHM)
  Beam spot FWHM ~30mm