## Slide 1
Overview of
EMuS beamline design
Yu Bao
International Review Meeting 2018
@CSNS
2018.11.21

## Slide 2: Outlines
Layout and strategy of EMuS beamlines
Introduction of the beamlines:
  Design goals and challenges
R&D on muon moderation

## Slide 3: Staging Strategy of EMuS
CDR
Baby Scheme
Baseline Scheme
Verticle beamline
First beam for muSR
High Intensity Surface & Decay muon beam
High polarization surface muon
First funding
Second funding

## Slide 4: Baby scheme
Requirement:
  High polarization surface muon.
  Intensity reaches requirement of the 256-channel spectrometer (~105/s).
  Beam spot < 30mm
Challenge:
  Low proton power
Solution:
  Thick target 10cm

## Slide 5: What we have achieved for Baby Scheme
Intensity: 1.2E5/s
Polarization: >90%
Energy spread: <10%
Beam spot(FWHM):<30mm
e+: <1%
Talk from Luping Zhou

## Slide 6: Vertical beamline design
Requirement:
  “Useable” beam for μSR study
  NOT affect the main target station too much!
Challenge:
  Low proton power
  Thin target!
Achieved:
  Intensity: 6E4 μ+/s
  Polarization: >90%
  Beam spot: <30mm

## Slide 7: Superconducting Surface Muon Beamline
Goal: high intensity surface muon for future super muSR spectrometer
Challenge:
  Large momentum spread and emittance
  High positron containment
Approach:
  Beam matching
  Wein filter
Matching solenoids

## Slide 8: Beam matching design （1）

## Slide 9: Beam matching (2)
Beam matching increases the beam intensity and reduces the momentum spread.
Without matching
With matching

## Slide 10: Surface muon beam parameters
 | High Intensity Mode | High Polarization Mode
Intensity(1E6/s) | 74 | 24
Polarization | 50% | 75%
Beam spot (FWHM) | 96*96 mm | 72*80 mm
Momentum spread (FWHM) | <15% | <10%
e+ | <8% | <5%

## Slide 11: Decay muon beamline
Design goal:
  Flexible muon beam: tunable energy, tunable polarization and intensity
Challenges:
  Large momentum spread
  Large emittance
Solutions
  Matching and collimation

## Slide 12: Decay muon beamline parameters
 | Ref. momentum | High-intensity |  |  | High-polarization |  | 
 |  | Intensity(1E6/s) | PolZ | SpotFWHM (mm) | Intensity(1E6/s) | PolZ | SpotFWHM (mm)
Decay muon | 45 | 25 | 0.68 | 88×88 | 25(2) | 0.68(0.73) | 88×88
 | 150 | 400 | 0.53 | 60×60 | 50(7) | 0.73(0.75) | 60×60
High-momentum muon | 450 | 130 |  | 72×76 |  |  | 
*The numbers in () are muons within a spot size of 30mm, in case we have fly pass setting in the spectrometer.
Talk from Yingpeng Song

## Slide 13: Muon moderation – conventional method
Low Energy Muon (LEM) at PSI uses solid rare gas to moderate muons with an efficiency around 10-5
The large band gap means muons can not loss energy when their energy is less than tens of eV
This results in large escape length of muons in these materials

## Slide 14: Muon moderation with helium – slow muons for the future
Helium advantage:
  Largest band gap
  Low density (liquid/gas)
  No muonium formation!
Technical Challenges:
  Liquid helium hard to control in vacuum
  Electrical discharge in helium gas
    Need Demonstration !

## Slide 15: Muon Moderation Demonstration
Since we have no muons in China yet, we are going to use protons/positrons to demonstrate the methods – the low energy processes in materials are similar with muons

## Slide 16: Summary
A staging strategy has been outlined for EMuS, starting from a “baby beamline” to a superconducting scheme
We have designed flexible muon beams covering a wide range of energy for various μSR studies and high-energy applications.
We are investigating the possibility of improving the muon moderation efficiency. R&D work has been started.

## Slide 17: backups