## Slide 1
ARW 2019: Performance Tracking & Round-Table Discussion
v22
benjamin.todd@cern.ch

## Slide 2: About the session…
Performance tracking related to reliability and availability, not considering “beam performance”.
Regardless of our backgrounds, all machines consist of similar technical equipment and operators exploiting this equipment to create beams of light or particles for their final users.
lower MTTR: comes by effectively managing repairs and equipment concerned
higher MTBF: can come from designing more reliable equipment based on operation and past experience.
higher availability = a higher MTBF and shorter MTTR.
availability: is a kind of “Key Performance Indicator”

## Slide 3: Motivation…
The aim of our workshop is to share information and techniques related to reliability and availability
Despite all coming from diverse machines Equipment + Operations = Beams
We can learn from each other
We can share our lessons learned and ideas
We can swap best practices
To do this we have to understand a little bit about each others’ worlds…

## Slide 4: Format of the Session
  ≈10:35 – 11:30: introduction to cross-section of institutes ≈8 minutes each
    BNL – Gregory MARR gmarr@bnl.gov
    Australian Synchrotron – Nicholas RAE nicholas.rae@synchrotron.org.au
    GSI – Oksana GEITHNER o.geithner@gsi.de
    SOLEIL – Thomas MARION thomas.marion@synchrotron-soleil.fr
    IHEP – Weibin LIU liuwb@ihep.ac.cn
    DESY – Michael BIELER bieler@desy.de
    Institut Curie – Samuel MEYRONEINC samuel.meyroneinc@curie.fr
    CERN – Benjamin TODD benjamin.todd@cern.ch
  ≈11:30 – 12:00: round table discussion

## Slide 5: BNL Gregory MARR

## Slide 6
  C-AD (BNL): Collider-Accelerator Department (Brookhaven National Laboratory)
Accelerator Complex: LINAC/EBIS/Tandem  Synchrotrons  flagship Relativistic Heavy Ion Collider (RHIC)
  End Product: colliding particles; ions – p, d, h, Al, Cu, Ru, Zr, Au, U, polarized protons
  RHIC colliding at beam energies 3.85-100 GeV ions, 255 GeV protons
BNL

## Slide 7
BNL Collider-Accelerator Complex
Performance tracking is required for 3 programs, often concurrently:
Brookhaven Linac Isotope Producer
  66-200 MeV protons,
  150 ms cycles,
  440 us pulse,
  50 mA beam
NASA Space Radiation Laboratory
  50-1500 MeV Linac protons, Tandem protons & ions, EBIS ions
  2 sec cycles
  Up to 1x1012 ions/cycle
  Rapid switching up to 33 ion/energy combinations per exposure (1 hour)
RHIC
Other areas also require oversight – R&D, Accelerator Test Facility, Tandem beam users, other testing areas
(NSLS-II)

## Slide 8: RHIC Operational Cycle
Yearly: 20-30 weeks operation, summer shutdown
Daily: 0.25-24 hours colliding
Monthly: Scheduled Maintenance every 2 weeks, ~8-16 hours

## Slide 9: Key Performance Indicators
Chart: RHIC Availability Run 19
| physics | machine development | beam studies | machine setup | experimenter setup | failure
 | 0.31385 | 0.2811 | 0.003163 | 0.27446 | 0.015029 | 0.1124
Luminosity is the major metric for RHIC performance. Projections are estimates made prior to the year’s Run.
Isotope production depends upon the availability of the Linac.
NSRL subscribes users and reports performance to NASA; like RHIC, we track availability.
Courtesy P. Ingrassia
Chart: LINAC Availability for BLIP
| FY12 | FY13 | FY14 | FY15 | FY16 | FY17 | FY18 | FY19
 | 0.89415 | 0.93978 | 0.9589 | 0.95698 | 0.95554 | 0.95327 | 0.90934 | 0.97458
Chart: Booster Availability for NSRL Runs 18C, 19A, & 19B
| Science | Machine Setup | Machine Development | Failure | Scheduled Maintenance
 | 0.45847 | 0.39299 | 0.040722 | 0.057164 | 0.0055138

## Slide 10: Collider Availability
Chart: RHIC Run19 Availability
| FY19-week 14: | FY19-week 15: | FY19-week 16: | FY19-week 17: | FY19-week 18: | FY19-week 19: | FY19-week 20: | FY19-week 21: | FY19-week 22: | FY19-week 23: | FY19-week 24: | FY19-week 25: | FY19-week 26: | FY19-week 27: | FY19-week 28: | FY19-week 29: | FY19-week 30: | FY19-week 31: | FY19-week 32: | FY19-week 33: | FY19-week 34: | FY19-week 35: | FY19-week 36: | FY19-week 37: | FY19-week 38: | FY19-week 39: | FY19-week 40:
availability | 0.94147 | 0.91037 | 0.94725 | 0.87794 | 0.90442 | 0.84433 | 0.85157 | 0.93248 | 0.87772 | 0.84957 | 0.94415 | 0.91656 | 0.81483 | 0.8776 | 0.85296 | 0.88034 | 0.89921 | 0.89274 | 0.91025 | 0.8622 | 0.93895 | 0.93291 | 0.9029 | 0.91128 | 0.9222 | 0.79273 | 0.8823
Goal: 80% average for Run, set by US Department of Energy.
Goal is being reset up to 82.5% for upcoming years…
Courtesy P. Ingrassia
Chart: 
| Run2 | Run3 | Run4 | Run5 | Run6 | Run7 | Run8 | Run9 | Run10 | Run11 | Run12 | Run13 | Run14 | Run15 | Run16 | Run17 | Run18 | Run19
RHIC Availability by Run[%] | 0.825 | 0.779 | 0.801 | 0.847 | 0.802 | 0.698 | 0.833 | 0.803 | 0.829 | 0.763 | 0.854 | 0.837 | 0.868 | 0.879 | 0.827 | 0.86 | 0.909 | 0.887

## Slide 11: Downtime Root-Causes
Chart: RHIC Run19 Failure Hours ( > 1 hr.) by System/Group
| LEReC | RfRHIC | PS_RHIC | PPS_AGS | PS_AGS | HumanError | EBIS | PPS_RHIC | ACG_RHIC | PS_Bstr/BtA/LtB | InstRHIC | CryoRHIC | PS_Experiment | ESHQ | WaterAGS | WaterBoost/BtA | CntrlsHdRHIC | RfAGS | ES&FD_Exp | ES&FD_R | VacRHIC | InjPerformance | RadMonIntlk | Weather | RfBooster | CntrlsSftwr | WaterRHIC | PPS_Booster | QLI
% Scheduled operations | 0.035786 | 0.026679 | 0.020958 | 0.012433 | 0.0095619 | 0.0094726 | 0.0092613 | 0.0088558 | 0.0079243 | 0.0075245 | 0.006359 | 0.0056487 | 0.0046987 | 0.0045569 | 0.0045087 | 0.003909 | 0.0035177 | 0.0033348 | 0.0028669 | 0.0026031 | 0.0024755 | 0.0022288 | 0.001761 | 0.0016603 | 0.0011867 | 0.0011697 | 0.0011102 | 0.00055296 | 0.00042535
Root Cause System | Root Cause Duration [h] | % Total Scheduled Operations
Low Energy Electron Cooling | 84.1 | 3.6
RHIC RF | 62.7 | 2.7
RHIC Power Supplies | 49.3 | 2.1
AGS Fast Pulsed Power Supplies | 29.2 | 1.2
AGS Power Supplies | 22.5 | 0.9
Run19 total failure hours = 480 (all systems)
Chart: Mean Time Between Failure, Mean Time To Repair, Average Failure hours/day [cryo start to cryo end date]
| Run7 | Run8 | Run9 | Run10 | Run11 | Run12 | Run13 | Run14 | Run15 | Run16 | Run17 | Run18 | Run19
MTBF (h) | 5.25 | 6.31 | 5.51 | 5.51 | 5.69 | 6.91 | 6.55 | 8.61 | 8.09 | 6.37 | 6.75 | 9.32 | 3.86
MTTR (h) | 1.98 | 1.21 | 1.29 | 1.04 | 1.24 | 1.08 | 1.23 | 1.28 | 1.13 | 1.19 | 1.17 | 0.93 | 0.48
<Failure h/da> | 6.3 | 3.8222 | 3.4286 | 3.7704 | 4.4824 | 3.0057 | 3.4643 | 3.026 | 3.1494 | 3.5742 | 3.6507 | 2.1495 | 3.0645
Courtesy P. Ingrassia

## Slide 12: Australian Synchrotron Nicholas RAE

## Slide 13
  Australian Synchrotron - Melbourne, Australia
  3 GeV Synchrotron, 200 mA electrons, beam in top-up
  9 x-ray beamlines, 2 infrared, ODB, XDB
  8 new x-ray beamlines commissioned
  End Product: photons 5000 hours / year
Australian Synchrotron

## Slide 14
Booster
100 Mev – 3 Gev Booster
3 Cav IOT RF
Storage ring
3 GeV Storage Ring
4 RF Cavities
3 operating, 1 spare
250 kW Klystrons
LINAC
90 KeV Gun
100 MeV linac
2 Klystrons + SLED
1 Hot spare klystron

## Slide 15: Operational Cycle

## Slide 16
Operational Cycle
Maintenance
  Every 2nd Monday
  3 shutdown period per year
  Additional week for new x-ray 8 new beamline commissioning.
Machine studies
  Every Sunday
  Accelerator physics studies
  Testing and maintenance requiring beam
Stored Beam
  X-ray beamline available users
  Operators provide beamline support outside 9-5 hours
  Operate in topup mode

## Slide 17: Key Performance Indicators
Beam availability
  16 week Availability > 97 %
Mean Time Between Failure (MTBF)
  16 week MTBF > 50 Hrs
Mean downtime (time to recovery)
  16 week & 12 months < 1.5 Hrs

## Slide 18
Availability Figures

## Slide 19: Top Downtime Root-Causes
Currently:
2018: 25 beam dumps, 28.5 hours downtime
2019(8 weeks): 21 beam dumps, 30.5 hours downtime
Causes
  Plant upgrade to water cooling
  RF system
  Magnet power supplies
Past:
~2012: Implementation of UPS and diesel generator greatly reduced previous root cause: power interruptions. Blackouts, brownouts local lightening strikes etc.

## Slide 20: Top Downtime Root-Causes
1. Plant upgrade project
2. Storage ring RF issues
  End of life components
  PSS upgrade
3. Magnet power supplies
  End of life (expected ~ 10 years)
  Being replace as fast as we can source them (lead time 6-18 months)
4. Future: Disruptions from commissioning new beamlines
Thank You

## Slide 21: GSI Oksana GEITHNER

## Slide 22
  GSI: Helmholtzcenter for Heavy Ions GmbH
  End Product: Ions
GSI

## Slide 23: Facility Overview

## Slide 24: Operational Cycle
Organisation of main control room, on-call duty, communication
and meetings
Beam Time Periods (ENG RUN, PHYS RUN)
Shutdown Phases
O. Geithner, ACC Operation ARW 2019

## Slide 25: Complex Parallel Operation
O. Geithner, ACC Operation ARW 2019

## Slide 26: Availability Calculation: experiments and machines
Availability of the machines in 2 regimes:
1) availability for the local experiments
2) operation as part of the production chain
O. Geithner, ACC Operation ARW 2019

## Slide 27: Failure Statistics 2019
Failure Counts
Failure Duration [h]
RF Transmitter
Power Supply HW
Vacuum HW
Controls Frontend
Magnets
RF Cavity
Controls Apps
RF Controls
Not identified
Operating
Vacuum HW
RF Transmitter
Ion Source ECR
Power Supply HW
Power Supply Controls
Magnets
Not identified
Controls Frontend
Infrastructure Cooling Water
Ion Source South
O. Geithner, ACC Operation ARW 2019

## Slide 28
As GSI + FAIR is going to be quite large facility, automated failure tracking is a legitim requirement for the future accounting.
Such complex task cannot be achieved over night. Stepwise approach would be
a good way.
Goal: General Comments

## Slide 29: Next Steps
Increase the quality of the manually maintaned (by operators) failure data
=> establish an Availability Working Group (AWG).
Members: myself, operator and representatives of the expert groups
Goal: meet every 2 weeks, go through the failure events and complement the data.
AWG Meetings are already sheduled for the end of this year (Engineering Run 2019)
Introduce Beam Performance Factor in Availability Calculation (intensity, macri/micro spill structure, position stability, beam size, dp/p)

## Slide 30: Next Steps
Automated generation of the failure events in the E – Logbook (OLOG)
for further manuel processing by Availability Working Group (AWG)
Archiving
System
OLOG
Interlock
System
Interlocks
Buffer
ALARM
System
?
?
AWG

## Slide 31: Christmas Wish: Failure Prediction

## Slide 32: Prototype: Failure Prediction CRYRING@ESR Ion Source
Control / input variables:
anode voltage (YRT1IN1E, pulsed)
gas flow (YRT1IN1G)
cathode current (YRT1IN1K)
solenoid current (YRT1IN1M)
acceleration high voltage (YRT1IN1X)
Output observable:
pulsed ion current, measured with beam transformer, f ~ 0.3 Hz, Lpulse ~20-30 ms
Status of Application of Machine-Learning Techniques at CRYRING@ESR:
Talk by W Geithner

## Slide 33: SOLEIL Thomas MARION

## Slide 34
  Synchrotron SOLEIL
  30 km South of Paris, France
SOLEIL
  End Product: Photons

## Slide 35: Facility overview
Synchrotron light source of 3rd generation
3 accelerators
  LINAC : 0  110MeV
  BOOSTER : 0.11  2.75 GeV
  Storage ring : 2.75 GeV
Circumference : 354m
29 Beamlines
27 Undulators
5 Filling modes
Chart: Beamline and radiation tests beam time in 2018 (5049 h) repartion according to the filling modes
| Radiation tests | Low Alpha | 1 bunch | 8 bunches | uniform | Hybrid
 | 2.8958 | 10 | 11.8333 | 11.8493 | 91.6431 | 82.1639
Hybrid : 445 +5mA
Uniform : 500mA
1 bunch : 16mA
8 bunches : 100mA
Low alpha : 18mA

## Slide 36: Operational Cycle
In 2019 :
5 RUNs
5 Shutdown periods
35 weeks for users
5100 h of beam for users
1200 h of beam for accelerators
A typical week:
Machine session Monday 7am to Tuesday 7am
1h or more dedicated for maintenance on Mondays (in 2018 – 280 interventions)
144h of beam given to users (6 days - 24h/24)
Every RUN:
5/6 days scheduled to restart & check machine
In case of failure in User session :
The operator reinjects the beam as soon as possible (after diagnostics and analysis)
If the failure needs emergency fix, in each group there is a person on call
24/7 operation
Shutdown
Machine session

## Slide 37: Key Performance Indicators
  Objectives:
    5000h of beam delivered to the user every year
    99% Beam availability
    MTBF 100h
    Beam stable in flux and brilliance
      Beam stable in intensity
      Beam stable in position
      Beam stable in size (10 µm in vertical plane, sub-micrometric stability at 2%)
  No Beam failure:
  Beam loss
  All Front-End closed
  Top-Up failure:
  Current < 99,9% of Nominal
  If Current < Nominal – 30mA (for 500mA)
  close the frontend to reinject  No Beam
Top-Up failure
Front-End closing for reinjection
No Beam Failure
499,5mA
470mA
Inom = 500mA
  Beam Line failure:
  If beam position and size > 10% of nominal size
  All incident blocking photon use for one or more beamlines (Frontend or undulator)
KPI: Availability, MTBF, MTTR
For No Beam and Top-Up

## Slide 38: Availability Figures
Chart: Origin of the 59 hours BEAM TIME LOST in 2018
| RF | Power supply | Linac | Magnet & insertions | Electronic Control | Informatic Control | Vacuum | Control Room | EP | Diagnostics | PSS | Cryo | Beamline | Utilites | Power outage | Others | FBT | Human
TOTAL | 0.14792 | 0.20347 | 0.0041667 | 0.1 | 0.10208 | 0.013194 | 0.18681 | 0.0125 | 0.11528 | 0.059722 | 0 | 0 | 0.27847 | 0.37569 | 0 | 0.17222 | 0.35208 | 0.020139 | 0.31458
Chart: Efficiency by week and integrated in 2018 In 35 weeks; 20 are > 99% (10 at 100%)
| Sem 04 - 18 | Sem 05 - 18 | Sem 06 - 18 | Sem 07 - 18 | Sem 08 - 18 | Sem 11 - 18 | Sem 12 - 18 | Sem 13 - 18 | Sem 14 - 18 | Sem 15 - 18 | Sem 16 - 18 | Sem 20 - 18 | Sem 21 - 18 | Sem 22 - 18 | Sem 23 - 18 | Sem 24 - 18 | Sem 25 - 18 | Sem 26 - 18 | Sem 27 - 18 | Sem 28 - 18 | Sem 29 - 18 | Sem 30 - 18 | Sem 36 - 18 | Sem 37 - 18 | Sem 38 - 18 | Sem 39 - 18 | Sem 40 - 18 | Sem 41 - 18 | Sem 44 - 18 | Sem 45 - 18 | Sem 46 - 18 | Sem 47 - 18 | Sem 48 - 18 | Sem 49 - 18 | Sem 50 - 18
Efficacité par semaine | 1 | 1 | 0.99498 | 1 | 0.98831 | 0.90493 | 0.99755 | 0.98333 | 0.97662 | 0.99489 | 0.99468 | 1 | 0.97002 | 0.98059 | 0.98565 | 1 | 0.98438 | 0.97569 | 0.98426 | 0.99769 | 0.98947 | 0.99352 | 0.99495 | 0.98021 | 0.98738 | 1 | 1 | 1 | 1 | 0.99491 | 0.99144 | 1 | 0.9787 | 0.98194 | 0.99002
Efficacité cumulée en 2018 | 1 | 1 | 0.99828 | 0.99871 | 0.99664 | 0.98159 | 0.98385 | 0.98379 | 0.98299 | 0.98423 | 0.98517 | 0.98639 | 0.98513 | 0.9848 | 0.98485 | 0.98572 | 0.98564 | 0.98509 | 0.98504 | 0.98567 | 0.98586 | 0.98621 | 0.98659 | 0.98632 | 0.98636 | 0.9869 | 0.98741 | 0.98779 | 0.9882 | 0.98843 | 0.98852 | 0.98888 | 0.98857 | 0.98838 | 0.98845
Chart: Quality of Top-Up: Stored current > 99,9% of the nominal MTBF (34h) and availability (99,76%) of the Top-Up, during user session, in 2018
| 23/01 au 26/02 | 13/03 au 23/04 | 15/05 au 30/07 | 04/09 au 15/10 | 30/10 au 20/12
MTBF-Top-Up | 3.3012 | 1.0579 | 0.81016 | 3.1311 | 3.1731
Disponibilité Top-Up | 0.99974 | 0.99387 | 0.99832 | 0.99889 | 0.99708

## Slide 39: Top Downtime Root-Causes
Fluid (7 failures - 9h01): Flowmeter default -> clogged filters, bad setting
      Cleaning of all the Magnets & powersupply filter
Others (16 failures - 8h27): Beam blow-up (collective effect) due to a bad local vacuum, after installation of new vacuum chamber.
Human (6 failures - 7h33) : involuntary stop of fluid and forced openning of beamline hutch
Beamlines (8 failures - 6h41) : Electronics of the Personal Safety System
59h of Downtime in 2018

## Slide 40: IHEP Weibin LIU

## Slide 41
IHEP
  IHEP: Institute of High Energy Physics
  Accelerator complex of BEPCII: LINAC  flagship Beijing Electron Positron Collider
  End product: colliding particles, photons

## Slide 42
BEPCII Complex
BEPCII — An upgrade project of Beijing Electron Positron Collider (2008)
— A double-ring factory-like machine (1×1033 cm-2s-1 @1.89 GeV)
— Deliver beams to both HEP (1.0 GeV — 2.3 GeV e+, e-)
& SR (2.5 GeV e-, 250 mA)
Linac
BESIII
Storage Ring
BSRF
e+
e-

## Slide 43
BEPCII Operational Schedule 2018/19
Superconducting 3W1
Beam energy upgrade
Top-up upgrade
9 energy points
Data taking @ Ebeam>2GeV
{
1200 pb-1
3800 pb-1

## Slide 44
Luminosity of BEPCII 2018/19
The luminosity is the major metric of BEPCII.
Peak Luminosity:
7.666×1032cm-2s-1 @ 617mA*627mA
(Mar. 10, 86 bunches, @XYZ)
4.674×1032cm-2s-1 @ 707mA*723mA
(Jan. 14, 112 bunches, @J/psi)
Chart: 
| *1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31 | *32
周积分亮度 | 3.22 | 54.73 | 46.98 | 86.43 | 125.78 | 118.45 | 119.33 | 133.07 | 131.92 | 122.13 | 127.85 | 136.92 | 139.78 | 111.76 | 196.34 | 229.03 | 257.23 | 203.74 | 231.47 | 232.36 | 230.93 | 229.04 | 230.86 | 223.12 | 234.55 | 177.89 | 207.02 | 207.16 | 181.91 | 194.9 | 164.07 | 97.32
Availability | 98.7847 | 89.7123 | 74.0278 | 98.631 | 94.4742 | 92.6488 | 95.6052 | 97.8274 | 91.6369 | 88.0456 | 98.0258 | 98.7202 | 98.8591 | 93.8988 | 98.1548 | 97.5893 | 99.0079 | 95.119 | 98.2937 | 97.3512 | 97.629 | 98.7798 | 94.4742 | 97.9762 | 96.2996 | 88.5813 | 96.0714 | 94.3948 | 92.8373 | 94.7817 | 93.9484 | 95.816
Physics Achieved [pb-1]
Availability [%]
94.94%

## Slide 45
BEPCII Status of Collision Operation 2018/19
Machine statistics
Accelerator failure: 267.68 hrs., 422 times
The faults of kicker power supply were a little more than before. Kicker power supply faults: 7 times, 18.41 hrs.
The failure of the air conditioner in the equipment room caused the feedback system to work in an unstable state.

## Slide 46
Top-up Upgrade Testing of Collision Operation
Chart: Integral Luminosity by Shift (pb-1)
| Mon. Day | Mon. Night | Tues. Day | Tues. Night | Wed. Day | Wed. Night | Thurs. Day | Thurs. Night | Fri. Day | Fri. Night | Sat. Day | Sat. Night | Sun. Day | Sun. Night | Mon. Day | Mon. Night | Tues. Day | Tues. Night | Wed. Day | Wed. Night
Luminosity(pb^-1) | 14.71 | 14.5 | 3.6 | 15.12 | 11.52 | 15.08 | 10.45 | 15.31 | 7.05 | 12.86 | 6.47 | 10.69 | 12.21 | 14.5 | 14.58 | 18.88 | 0.3 | 15.77 | 18.75 | 17.38
Continuous Top-up operation
from Jun. 17 to Jun. 20, 2019
Fully automatic, works well, stable enough.
Average integral luminosity increased by 25%.
e+: 510 — 525mA, e-: 470 — 535mA

## Slide 47
BEPCII Availability of SR Operation 2018/19
Availability: 99.54%, MTBF: 129.77 hrs., MDT: 0.6 hrs.
Availability
Top-up @2.5 GeV, 250 mA
A photon absorber was misaligned in the installation direction. Which caused one beam line (4B9) to fail to see light.
When solving the control problem of wiggler 4W2, an incorrect magnet gap was set. This leaded to the decrease of beam life time.
Thank you!
MTBF
MDT

## Slide 48: DESY Michael BIELER

## Slide 49
  DESY: Deutsches Elektronen Synchrotron
  Accelerator Complex: Flagships PETRA III, FLASH, European XFEL
  End product: Photons
DESY

## Slide 50: DESY’s Accelerators
Linac II 1970 450 MeV e+/e-
PIA 1970 450 MeV e+/e-
DESY II 1990 7 GeV e+/e-
PETRA III 2009 6 GeV e+/e-
FLASH 2003 1.2 GeV e-
XFEL 2016 17.5 GeV e-

## Slide 51: PETRA III Operational Cycle
  Winter Shutdown
  Summer Break
  4800 User hours per year
  Machine development on Wednesdays
  Top Up operation for the rest of the week

## Slide 52: PETRA III Key Performance Indicators
Definition:
Fault: Every beam loss of more than 25%
KPI: Availability =
scheduled beam time
delivered beam time
  PETRA III delivers the brightest high energy electron beam: 1.2 nm rad x 12 pm rad @ 6 GeV

## Slide 53: PETRA III Availability 2019
Summer
Break
2018:
96,37 %
98,44 %
Service Week
Power Glitch
as of Oct. 13

## Slide 54: Top Downtime Root-Causes
as of Oct. 13
  Main causes of downtime in 2019:
  Power Glitches
  Kicker Magnets
  Magnet Power Supplies

## Slide 55: Institut Curie - Protonthérapie Samuel MEYRONEINC

## Slide 56
  Institut Curie –Centre de Protonthérapie d’Orsay
  Accelerator Complex: 1 cyclotron for 3 treatments rooms
  End product: Protons
PARIS

## Slide 57
Centre de Protonthérapie d’Orsay
Cyclotron
230 Mev
(IBA)
Gantry Room:
All tumors
(IBA)
Y1 Room: Intracranial tumors
(Home made)
Y2 Room: Ophthalmic Tumors
(Home made)
1957 Research physical center
----------------------------------------
1990: Creation of CPO (network)
1991: 1st Ocular treatment
1 Room – Fix. Line
1993: 1st intracranial treatment
2 Rooms – Fix. Lines
2004: Integration
into the Institut Curie
2006 1st General Anesthesia
2010 New cyclotron + 1 Gantry
2011 1Gantry +2 rooms (Horiz line)
2019 11 000 fractions/year - %PBS

## Slide 58
Centre de Protonthérapie d’Orsay
Gantry room

## Slide 59: CPO Operational
Typical day
6h30 - 7h30 technical startup and warm-up
2 days per week with 30 minutes of maintenances
7h30 - 8h30 Beam checks (by users)
8h30 – 19h15 – use for clinics (treatment or Quality Control) -11 hours of operations
after 19h15 several options
Extra-time to finish the clinical activity (if case of large activity or delays during the days)
evening session for Periodic Tests
evening session for experimentations (physics, or mainly radiobiology in vitro or in vivo)
Typical week
  5 days of operation
  Some saturday morning or week-end of maintenance
Typical year
  52 weeks of treatment
  Only 4 fridays + week-end for large quarterly maintenance sessions

## Slide 60: General Key Performances Indicators (CPO)
Branding
external
Analysis
internal
Happy Users
internal
- number of sessions of treatment done
- medical publications (local control, survival rate)
- Annual green light from authorities (Medical/ Nuclear Safety / Quality Assurance)
- patient satisfactions (formular filled)

## Slide 61: 3 Technical Key Performances Indicators (CPO)
% patient treated the day scheduled
Detailed Uptime:
sum of downtimes/
Normal time of operations
Feedback from medical users:
are you OK ? List of top-problems
1
2
3
Branding
external
Analysis
internal
Happy Users
internal
Prioritar target: avoiding events with TTR >2h >>> 0,5day >>> 1 day

## Slide 62: CPO Latest Availability informations
Treatments session done and % done the D Day
Years
nb sessions
report 3 rooms
% Done the D Day

## Slide 63: Top Downtime sources (for accelerator)
Branding
external
Analysis
internal
Happy Users
internal
1. Regular Ions source problems
2. long duration events on the deflector
3. General capacity of diagnosis for some systems

## Slide 64: CERN Benjamin TODD

## Slide 65
  CERN: European Organisation for Nuclear Research
  Accelerator Complex: LINAC  Synchrotrons  flagship Large Hadron Collider
  End Product: colliding particles, hadrons or ions
CERN

## Slide 67
  LS = Long Shutdowns for Upgrades
  Run = Production Period
  White = Shutdown
  Green = Production
  Blue = Development
  Production Fault recover and refilling

## Slide 68
Key Performance Indicators

## Slide 69
2018: Availability Figures

## Slide 70
2018: Top Downtime Sources

## Slide 71
2018: Top Downtime Sources
Root Cause System | Root Cause Duration [h] | % of Total Duration
Injector Complex | 237.9 | 23.7
Cryogenics | 187.3 | 18.6
Power Converters | 101.0 | 10.1
Quench Protection | 75.2 | 7.5
Radio Frequency | 49.2 | 4.9
= 650.6 hours
= 64.7%

## Slide 72: Round Table

## Slide 73: Questions
  How are operations and faults managed? Together / separately?
  What level of integration has equipment with operations?
  What authorities manage faults and fault information?
  Who ensures that the faults which are recorded are consistent?
  Who is using the fault information, and what for?
  How are dependencies figured out between faults?
  What examples are there of reliability driven improvements?
  Are people making use of predictive models based on fault data–
  e.g. identifying hidden sequences / dependencies forewarning larger issues…