## Slide 1: CSNS Accelerator Operation Status and Reliability Improvement
Yuliang Zhang
On behalf of the CSNS accelerator team
ARW'2019.Guangzhou

## Slide 2: Outline
2
Brief Introduction of CSNS
1
3
4
Accelerator Operation Status
Reliability Assurance and Improvements
Summary

## Slide 3: Brief Introduction of CSNS
25Hz,1.6GeV
80Mev H- LINAC
1.6GeV
25Hz
100kW
Tungsten target
3 beam lines/20
in phase-I

## Slide 4: Brief Introduction of CSNS
Linac Design
 | Ion Source | RFQ | DTL
Input Energy（MeV) |  | 0.05 | 3.0
Output Energy(MeV) | 0.05 | 3.0 | 80
Pulse Current (mA) | 20/40 | 15/30 | 15/30
RF frequency (MHz) |  | 324 | 324
Chop rate (%) |  | 50 | 50
Duty factor (%) | 1.3 | 1.05 | 1.05
Repetition rate (Hz) | 25 | 25 | 25
Electrostatic chopper in LEBT

## Slide 5: Brief Introduction of CSNS
Lattice of 4-fold symmetry, triplet.
227.92m circumference.
Four long straight sections for injection, acceleration, collimation and extraction.
24 main dipoles with one power supply.
48 main quadrupoles with 5 power supplies.
Ceramic vacuum chambers for the AC&pulsed magnets.
8 RF ferrite loaded cavities to provide 165 kV.
RCS Design

## Slide 6: Brief Introduction of CSNS
10kW
30kW
40kW
50kW
20kW
Spark of RFQ cavity
Summer shutdown
50kW machine study
80kW machine study
Problem of RFQ power source
August 2017, first proton beam delivered to target and first neutron beam generated.
August 2018, the whole project passed the national acceptance.
CSNS commissioning and operation overview(2017.11~2019.10)
80kW
Summer shutdown & 80kW machine study

## Slide 7: CSNS Accelerator Operation Status
First round(2018.9.30-2019.6.26) open run of user experiments completed.
Beam power increased from 25kW to 50kW step by step.

## Slide 8: CSNS Accelerator Operation Status
Chart: 
| Startup | Target | Accelerator Study | Maintenance | Failure | Other
 | 62 | 4055 | 1901 | 265 | 361 | 68
First round operation statistics(in hour)
Beam availability was 91.8% in the first round of open run of user experiments
Scheduled beam time on target is 4000 hours, completed 4055 hours
Availability=

## Slide 9: CSNS Accelerator Operation Status
Second round operation statistics(in hour) until now
Second open run of user experiments until now, availability is nearly 95%
Chart: 
| Startup | Target | Accelerator Study | Maintenance | Failure | Other
 | 53 | 769 | 19 | 78 | 38 | 0

## Slide 10: CSNS Accelerator Operation Status
Beam power increases from 10kW to 80kW and beam availability is also increased.
Knowledge of operating a high intensity proton machine and skills of operators are promoted a lot in the past year.
Chart: Beam Availability
| 18.1-18.7 | 18.9-18.12 | 19.1-19.6 | 19.9-19.10
 | 0.6856 | 0.89955 | 0.92643 | 0.94883
25kW
50kW
80kW
10-25kW

## Slide 11: CSNS Accelerator Operation Status
Chart: 
| Lianc RF | Ion Source | Power Supply | DTL | Other | Ring RF | RFQ | Vacuum | Beam Instrument | Magnet | Control
 | 134.95 | 93.95 | 42.42 | 36.85 | 18.03 | 14.25 | 2.53 | 2.12 | 1.83 | 1.47 | 1.18
Downtime statistics in hours by system during user experiments(Sep. 2018 to Oct. 2019)
Chart: 
| Lianc RF | Ion Source | Power Supply | DTL | Other | Ring RF | RFQ | Vacuum | Beam Instrument | Magnet | Control
 | 134.95 | 93.95 | 42.42 | 36.85 | 18.03 | 14.25 | 2.53 | 2.12 | 1.83 | 1.47 | 1.18

## Slide 12: CSNS Accelerator Operation Status
Linac RF: crowbar, HV modulator、spark of klystron、4616 tetrode, LLRF.
Ion source: discharge chamber, instability of extracted beam
Power supply: RCS injection，extraction and RTBT power supplies
RFQ&DTL：cavity arc, VSWR
Ring RF：LLRF, bias power supply, cavity arc, amplifier, etc.
Vacuum：Valve gate interlock caused by small leak
Magnet：high voltage discharge, mis-trigger by temperature sensors
Other：Thunder and lightning, beam loss interlock, etc.
Main failures by system:

## Slide 13
Reliability Assurance and Improvements

## Slide 14: Machine Protection System
Beam Off
/RST
Beam Off
/RST
MPS A
MPS B
FPS
IS HV
RMS
Interlock
Interlock
PPS
Stop Beam
Fault
Fault
Interlock
Interlock
RFQ LLRF
IS Timing
Stop Beam
RST
Machine protection system consists of Normal MPS and Fast MPS, NMPS consists of two independent systems(MPS-A and MPS-B).
Both NMPS and FPS use independent cable route to stop beam.
Relations among the CSNS protection systems

## Slide 15: Machine Protection System
Beam stop and recovery process
IS
RFQ
4616
RFQ LLRF
FPS
Fault
Timing
50kV HV
1
2
3
5
6
RFQ RF power off
~150nsec
After IS 50kV HV drop down to <5kV
RF power to RFQ again
drop IS 50kV HV
~4 sec
Turn off IS Ext timing
4
Major fault beam stop procedure(Manual recover)
MPS
LRF LLRFs
Block LRF beam gate timing

## Slide 16: Machine Protection System
IS
RFQ
Kly
RFQ LLRF
FPS
Fault
Timing
50kV HV
1
2
3
4
RFQ RF power off
~150nsec
RF power to RFQ again next cycle
LRF LLRFs
Block LRF beam gate timing
Beam stop and recovery process
Major fault beam stop procedure(Auto recover next or few cycles)

## Slide 17: Beam Loss and Control
Injection area
Collimator downstream area
Beam loss control is one of the key tasks to operation the high intensity proton machine
Regular residual dose measurement every week and the residual dose database has been built
Accumulate big data to establish the relation between beam loss and residual dose and to optimize the operation.
Beam loss
Residual dose

## Slide 18: Moving Monitoring System in Linac Tunnel
18
A moving monitoring system was mounted on the crane of the Linac tunnel, with a NaI detector to monitor gamma dose, a gamma imager and a temperature safety monitoring camera.
Gamma imaging
Temperature monitoring
Gamma dose monitored at DTL2 by the NaI detector.
Shut down

## Slide 19: RCS Dry running
A week per time, 2 times, many problems occurred and solved:
Water leakage was found in one cavity.
Cooling tubes of two AC magnets were burned.
17 chokes had strong vibration and had been returned to the manufacture factory to repair.
Ceramic vacuum chamber cracked
Arc of extraction kicker
……

## Slide 20: Solve the Problem of RFQ Spark
The chopped beam lost in the vane of RFQ, is confirmed to be the reason of RFQ spark
By rotating the chopper 45 degrees, most of the chopped beam passed through the slit between to adjacent vanes.
2018.06 open RFQ cavity
RFQ cavity before beam

## Slide 21: Solve the Problem of RFQ Spark
Chart: 
| 43215 | 43216 | 43217 | 43219 | 43220 | 43221 | 43222 | 43223 | 43224 | 43225 | 43226 | 43227 | 43228 | 43243 | 43244 | 43245 | 43246 | 43247 | 43274 | 43275 | 43276 | 43277 | 43278 | 43279 | 43280 | 43281 | 43282 | 43283 | 43284 | 43285 | 43286 | 43287 | 43288 | 43289
 | 0.5 | 0.3 | 4.3 | 13 | 6 | 6 | 10.5 | 14.5 | 5.5 | 9.5 | 13 | 7.5 | 8 | 0.75 | 0.8 | 10 | 10 | 11 | 0.33333 | 0.016667 | 0.033333 | 0.58333 | 0.1 | 0.25 | 0.11667 | 0.25 | 0.15 | 0.13333 | 0.1 | 0.016667 | 0.016667 | 0.083333 | 0.05 | 0.033333
Number of RFQ cavity spark per day

## Slide 22: Upgrade the RF Power Source of RFQ
The stability of the RFQ 4616 tetrode is one of the main cause of failure.
The lifetime and price of 4616 tetrode.
The retired klystron from DTL, can be used for RFQ, zero cost.
LLRF
CPI klystron
Magic T
Arch waveguide
RFQ
Circulator
Dummy Load

## Slide 23
High voltage discharging has caused insulation failures of RCS-272Q quadrupole magnets due to several reasons.
Corresponding measures had been carried out to enhance the insulation.
Insulation Enhancement for RCS Quadrupole
U-type fixture problem
Discharge between water tube and magnet
Coil abrading due to vibration
Notes: Nce

## Slide 24
All the U-type fixtures of the quadrupole magnets were replaced by the special ones with increased insulation distance.
Insulation for 8 sets of 6kV 272Q magnets was improved this September.
Insulation Enhancement for RCS Quadrupole
Rectangle reshaped to round rectangle of 272Q magnet core
Newly designed U-type fixture

## Slide 25: Reliability Improvement of Ion Source
To keep the consistency of each discharge chamber, strict fabrication and checking procedure was determined.
To ensure that at least one ion discharge chamber has been tested at the test stand as the hot standby spare.
Adopting the novel dual high voltage output extraction power supply to reduce the cesium deposition on the surface of anode, so as to decrease the arcing.
Developed the auto adjusting application to suppress the long period fluctuation.
Beam power auto adjusting

## Slide 26: Improvement of RCS Extration Power Supply
Building the online monitoring system，key signals of each extraction power supply are monitored
Improving the grounding of the extraction hall
Changing timing signal link from cable to fiber to eliminate signal transition interfering
Minimize the pulse width of high voltage charging for thyratron anode
Chart: Breakdown comparison by year
| Downtime(h) | No. of breakdown | No. of mis-trigger
2017.6~2018.7 | 66 | 311 | 293
2018.10~2019.6 | 22.5 | 151 | 142

## Slide 27: Grounding Improvement for Timing System
Original
grounding
Point
New
grounding
point
CSNS is located in south china, thunder and lightning occurs frequently every summer, so well-grounding is one of the key issues for high reliability operation.
Reference line
signal shift
Lightning
conductor

## Slide 28: Summary and Future Plan
CSNS accelerator has entered the stage of user experiments operation since Sep. 2018. After then, the beam power was ramped from 25kW to 80kW step by step.
The overall accelerator reached high reliability availability in the first round of CSNS user operation, while accelerator machine study and demands of user experiments operation need to find a balance .
Still needs further work to keep high reliability operation, and also the high availability will be a challenging task as the devices aging year by year.
Collaboration with other labs are welcomed.

## Slide 29
Thank you for your attention!