## Slide 1
?
Longitudinal Crystal segmentation
readout (Dual ?)
PFA CAPATIBLE
1 channel
(25 X0)
(5 X0)
(20X0)
(2x5 X0)
(20X0)
2 channel
7 channel
BGO
or
PWO
Crystal ECal
Computability?

## Slide 2
How thin the solenoid coil can be made?
Where the solenoid coil should be?
Effects of solenoid coil to calorimeter performance?
Inside or outside solenoid coil?
Readout

## Slide 3
W/Si
Best PFA performance ECal?
Low EM resolution
High cost
Heat and cooling
W/Si ECal
Computability?

## Slide 4
More traditional approach
Need to optimize:
segmentation size/absorber thickness
scint. shape
SiPM size (WLS fiber or direct acctach)
Improve light yield
W/Scint stip/tile ECal
Computability?

## Slide 5
Glass RPC Based DHCal
Scintillating strips/tiles
Which one to use if we have to choose?
Who to make decision to move to engineering design stage?
PFA Hadron Calorimeter

## Slide 6
Lead or copper?
Can more improvements be made?
Dual Readout Hadron Calorimeter

## Slide 7
Tianchi Zhao
March, 2018
Some thoughts about dual readout hadron calorimeter

## Slide 8
A Projective Tower of Dual Readout Calorimeter
~10 
Short fibers
Full length fibers
Total area to be covered by PMT determined by OD and barrel length of calorimeter
Assuming: OD = 7 m, L = 6 m
Total area = 190 m2
Barrel = 130 m2
End caps = 2 x 30 m2
2（ 6 x 6 ）SiPMs or MCP-PMT
5 cm
Total PMTs = 2 x 400 x 190 = 152000

## Slide 9
Ternary Readout
Scintillating light
Cherenkov light
Shower time profile
plastic scintillator plate/light guide
Fast PMTs
(S-fibers)
Fast PMTs
(C-fiber)
Cu-lead/Fiber module
Correct light attenuation
Correct sampling ratio change
Correct e/h change
PFA friendly?
plastic scintillator plate/light guide
An Alternative Readout Scheme
All full length fiber
Sampling ratio changes

## Slide 10
0 50 100 150 200 250
24
18
12
6
0
Depth in calorimeter tower (cm)
Scintillation light arrival time (ns)
Forward particle speed ~ 30 cm/ns
light speed in fibers ~ 17 cm/ns
Light to front PMT (ns)
Scintillation light start time (ns)
23 ns
Scintillation light arrival time
Effective light speed ~ 11 cm/ns
Signal time profile
e//h ID
Attenuation correction
T = 0
8.3 ns
Sc fiber readout from front face

## Slide 11
1 mm
1.5 mm
2.0 mm
1.5 mm
1 mm
2.0 mm
A possible Cu unit
average
X0 ~ 20 mm
~ 20 cm
Front
Rear
RD52 coper module (2012)
1 mm
1.5 mm
X0 ~ 24 mm
lint ~ 25 cm
Cu~60%, d ~ 5 g/cm3
Fiber~35%, Air~5%
1.5 mm

## Slide 12
Another RD 52 Dual Readout Calorimeter Cell
1.0 mm
1.0 mm
2.0 mm
Front
1.5 mm
1.0 mm
3.0 mm
Back

## Slide 13
sPHENIX Ecal at EIC
 < 20 cm

## Slide 15
calorimeter ~ 8
~1.6 m
~1.8 m
~4 m
Scaled SID tracker
TPC also possible
Projection in  and 

## Slide 16
Projection in  configuration

## Slide 17
Inner surface area of the calorimeter barrel and two end caps
Readout segmentation
Area to be Covered Determine by
Crude estimation：2 x (65 m2 + 2 x 12.5 m2) = 180 m2
Take
Rin = 2 m
Barrel Length = 5 m
Barrel area
End cap area
2.5 cm x 2.5 cm  288,000 PMTs
5 cm x 5 cm  72,000 PMTs