## Slide 1: CEPC项目组TDR讨论会及所创新基金总结汇报会 -直线注入器
张敬如
2018.12.26

## Slide 2: 主要内容
直线加速器介绍
需要解决的技术问题，本系统在TDR阶段需要解决的关键技术
TDR研究阶段各系统时间安排

## Slide 3: 直线加速器简介
The baseline design of the linac
  Electron linac
    Gun and Bunching System (BS) : 50 MeV && 3nC for electron
    LINAC-1: Electron beam @ 4 GeV && 3 nC
    Electron Bypass Transport Line (EBTL): Electron beam @ 4 GeV && 3 nC
    LINAC-3: Electron beam to 10 GeV && 3 nC
  Positron linac
    Positron Source and Pre-Accelerating Section: Positron beam larger than 200 MeV
    LINAC-2: Positron beam to 4 GeV. A 1.1 GeV damping Ring (DR) with circumference of 75.4 m
    LINAC-3: Positron beam to 10 GeV && 3 nC
EBTL
4GeV
Gun
Section-1
DR
Section-3
50MeV
1.1GeV
4GeV
10GeV
200MeV
Section-2
BS
(3nC/10nC)
(3nC/10nC)
(3nC/3nC)
(3nC)

## Slide 4: 直线加速器简介

## Slide 5: 需要解决的技术问题
List of events to be completed Issues
  Accelerating structure
  Positron source
  Electron gun
  SHB1
  SHB2
  Buncher
  Big hole accelerating structure
  Pulse compressor
  650MHz RF cavity
  ……

## Slide 6: 需要解决的技术问题
Thermionic electron gun
  Pulser System
  High Voltage System
Parameters | Values
Type | Triode
Maximum Beam Current(A) | 10
Anode High Voltage(kV) | 120~200
Filament voltage(V) | 6~8
Filament current(A) | 5~7.5
Grid bias voltage(V) | 0~200
Pulse width (ns) | 1
Pulse rate (pps) | 100
Beam trajectory of the injector electron gun
EIMAC-Y796 cathode-grid assembly
Cathode grid assemble
Current situation: EIMAC(USA) monopoly, price increase year by year and embargo at any time.

## Slide 7: 需要解决的技术问题
SHB1
  It is successfully used at BEPCII
  The frequency is deferent
  Need re-design
First sub-harmonic pre-buncher |  | 
Type | Re-entrant | 
Frequency | MHz | 143
Unloaded Q |  | 8175
Shunt impedance | M | 1.4
Esurface, max/Egap, max |  | 2.53
SHB1 assembly
SHB1 cut view

## Slide 8: 需要解决的技术问题
SHB2
  It is successfully used at BEPCII
  The frequency is deferent
  Need re-design
Second sub-harmonic pre-buncher |  | 
Frequency | MHz | 572
Unloaded Q |  | 13000
Shunt impedance | M | 3.7
Esurface, max/Egap, max |  | 2.44

## Slide 9: 需要解决的技术问题
Buncher
  It is successfully used at BEPCII
  The frequency is deferent
  Need re-design
parameters | value | unit
frequency | 2860 | MHz
mode | 2π/3 | -
Cell number | 6 | -
vp | 0.75 | -
a | 24 | mm
vg | 0.0193 | -
τ | 0.147 | Np/m
Shunt impedance | 33.2 | MΩ/m
Q | 11083 | -
VSWR | ≤1.1 | -
Input power | 2.5 | MW
type | 行波等阻抗 | -

## Slide 10: 需要解决的技术问题
S-band accelerating structure design
    Mechanical design
    High power test bench
      The power source is available at IHEP
      The high power test will begin recently

## Slide 11: 需要解决的技术问题
Big hole accelerating structure
  Constant impedance
  Processing technology is similar as the regular 3m long accelerating structure
  Preliminary design parameters
Parameters | value | Unit
Operating frequency | 2860 | MHz
Operating temperature | 30.0  0.1 | oC
Number of cells | 55 +2 coupler cells | 
Section length | 2 | m
Phase advance per cell | 2/3 - mode | 
Cell length | 34.966 | mm
Disk thickness (t) | 5.5 | mm
Iris diameter (2a) | 25 | mm
Cell diameter (2b) | 89.475 | mm
Shunt impedance (r0) | 60.8 | M/m
Q factor | 15448 | 
Group velocity (vg/c) | 0.019 | 
Filling time | 336 | ns
Attenuation factor | 0.195 | Neper

## Slide 12: 需要解决的技术问题
Pulse compressor
  According to the performance of the accelerating tube, determine the parameters of the pulse compressor
  The spherical cavity is a new type of design in recent years
  Advantages:
    Low temperature stability requirements
    Almost no radiation
Parameters | value
frequency | 2860MHz
VSWR | ≤1.1
Tuning range | ≥±500kHz
Peak power | ≥80MW
Repetition frequency | 100Hz
Pulse length | ~4µs
Output pulse length | ~0.8µs
Work temperature | 30±0.1oC
Vacuum leakage rate | ≤ 2×10-10 Torr.L/Sec
Spherical cavity
Two cavities

## Slide 13: 需要解决的技术问题
DR V2.0 | Unit | Value
Energy | GeV | 1.1
Circumference | m | 75.4
Storage time | ms | 20
Bending radius | M | 3.565
Dipole strength B0 | T | 1.03
U0 | keV | 36.3
Damping time x/y/z | ms | 15.2/15.2/7.6
0 | % | 0.05
0 | mm.mrad | 376.7
z，inj | mm | 5.0
Nature z | mm | 7.5
inj | mm.mrad | 2500
ext x/y | mm.mrad | 530/180
inj /ext | % | 0.2/0.05
Energy acceptance by RF | % | 1.0
fRF | MHz | 650
VRF | MV | 2.0
D, Wang
Damping ring

## Slide 14: 需要解决的技术问题
  Frequency: 499.7MHz
  Accelerating voltage: 1.09MV
  Accelerating gradient: 0.73MV/m
  Length: 1800mm
  Without HOM damper
DatenblattVers.2.0,500MHz,5-cellCavity HERA-Type, 2010
DESY 500MHz, 5-cell cavity

## Slide 15: 需要解决的技术问题
  Frequency: 508.9MHz
  Accelerating voltage: 2MV(total)
  Accelerating gradient: 2.7MV/m
  Length: 1100mm
  With HOM damper
1. RF Cavities for SuperKEKB MRs and DR, 2014
2. PHYSICAL REVIEW ACCELERATORS AND BEAMS 19, 102001 (2016)
SuperKEKB DR 509MHz RF cavity

## Slide 16: 需要解决的技术问题
Australian synchrotron 500MHz RF cavity
  Made by Toshiba
  Frequency: 499.7MHz
  Accelerating voltage: 750kV
  Accelerating gradient: 0.75MV/m
  Length: <1m
  With HOM damper
1. Nuclear Instruments and Methods in Physics Research A 592 (2008) 224– 229
2. HIGHER ORDER MODE (HOM) DAMPER OF 500MHZ DAMPED CAVITY FOR ASP STORAGE RING, EPAC 2006

## Slide 17: 需要解决的技术问题
SLC DR 714MHz RF cavity
  2 cell RF cavity
  Frequency: 714MHz
  Accelerating voltage: 800kV
  Number of cavities: 2
DAMPING RING RF SYSTEM FOR SLC IEEE Transactions on Nuclear Science, Vol, NS-30, No. 4, August 1983

## Slide 18: TDR阶段各系统时间表
Time: 2019.1-2022.12
  Accelerating structure
    Based on the high power test, optimize the accelerating structure continuously
    Complete the TDR
  Electron gun & SHB1 & SHB2 & buncher & Big hole accelerating structure
    Finish the RF simulation, physical design, thermal analysis and mechanical design
    Complete the TDR
  pulse compressor
    Finish the RF simulation and physical design and mechanical design
    Complete the processing of one prototype cavity
    Complete high power test
    Complete the TDR
  650 MHz RF cavity
    Physical design
    Finish the RF simulation and physical design and mechanical design
    Complete the processing of one prototype cavity
    Complete high power test ？
    Complete the TDR

## Slide 19
谢谢！