## Slide 1
Physics case,
status
and perspectives
NICA
Volga
river
MPD-ITS PROJECT
Yuri Murin, VBLHEP JINR
murin@jinr.ru
NICA
Yangtze
Volga
Notes: Good afternoon! First of all I would like to express my gratitude to organizers for the opportunity to give a short presentations on the NICA project and related physics

## Slide 2
NICA (Nuclotron based Ion Colider fAcility)
Main targets:
study of hot and dense baryonic matter
at the energy range of max net baryonic density
investigation of nucleon spin structure, polarization phenomena
modernization of existing accelerator facility
construction of Collider to collide
  relativistic ions from p to Au at energy range √SNN= 4 - 11 GeV
  polarized p and d at energy up to √S =27 GeV (p)
Notes: NICA is a Nuclotron … The main targets of the project are: ..
That has required a development of accelerator facility and construction of

## Slide 3
I.C. Arsene at al., Phys. Rev. C75 (2007) 24902.
5 r0
FAIR SIS-100
8 r0
NICA
Net Baryonic density to be reached
in Au + Au collisions
Notes: Net baryonic density to be reached in Au+Au collisions according various models is 5 and 8 standard densities at FAIR and NICA energies correspondingly

## Slide 4
maximum in the net baryon density – density frontier;
maximum in K+/p+ ratio;
maximum in L/p ratio;
maximum yield of hypernuclei
transition from a Baryon dominated system
to a Meson dominated one;
maximum of the L polarization;
1-st order transition & mixed phase creation;
Critical Endpoint ?
Mixed phase matter at the NICA energies:

## Slide 5
STAR F.T.
HADES
CBM
Interaction rate [Hz]
Collision energy √S [GeV]
NN
NICA/BM@N II
Current and future experiments on CBM
NA-61/SHINE
2022 – 2025: SIS-100 FAIR
energy region of max.
baryonic density
NICA/MPD
STAR BES II
Notes: Concerning fixed target experiments –there are several ones including NICA/BMN. CBM/FAIR will provide extremely high interaction rate.

## Slide 6: Current limitations of eхperimental data on D meson
Abdel Nasser TAWFIK† and Ehab ABBAS
Thermal Description of Particle Production in Au-Au Collisions at STAR Energies
Physics of Particles and Nuclei Letters. November 2013
Identificaion achieved
Thermal generator: D meson’s pt - spectrum

## Slide 7: ITS pointing resolution within STAR-ALICE toy model
ALICE
MPD
New ITS
Old ITS
Ø = 40 mm
Ø = 50 mm
Ø = 60 mm
Pions
Pions

## Slide 8
basic facility
SPD
MPD
Center NICA
Nuclotron ring (c=251,5 m)
Collider ring (c=503 m)
2 major milestones in 2018
BM@N
the first
physics run
Booster commissioning
Notes: This is a view of major NICA facilities. The Nuclotron – supercoducting synchrotron with circumference of 250 meters was put in operation 24 years ago. The beams from Nuclotron are extracted to the experimental hall, where the first experiment of NICA program BM@N is located. The plan is to put in operation a booster in 2019, and collider - in 2020 simultaneously with the MPD.

## Slide 9
Ecool
RF
Booster
PS
Assemblies | # | tested / ready %
dipoles | 40 | 100/30
qdr doublets | 24 | 80/5
BPM stations | 24 | 80/0
magn.joint kits | 45 | 100/50
bypass for coolant liquid | 2 | 60/0
warm sect. | 4 | 70/50
refererence magnet sec. | 2 | 90/50
feed box | 2 | 10/0
vac. station (cryostat) | 26 | 50/50
vac. station (beam pipe) | 24 | 90/30
ref. mag. sec.
milestone II: Booster status

## Slide 10
The Collider
45 T*m, 4.5 GeV/u for Au79+
Double aperture magnets:
dipole & quadrupole
prototypes
MPD
SPD
Ring circumference, m | 503,04
Number of bunches | 22
r.m.s. bunch length, m | 0,6
b, m | 0,35
max. int. Energy, Gev/u | 11,0
r.m.s. Dp/p, 10-3 | 1,6
IBS growth time, s | 1800
Luminosity, cm-2 s-1 | 1x1027
Notes: The lattice design and prototyping of most collider elements are completed. The ring circumference is twice as one of the Nuclotron. For the gold beam a Luminosity at the energy above 10 GeV per nucleon will be 10 to the 27

## Slide 11
MPD
Hall
SPD
Hall
Western
semiring
readiness for equipment installation in the MPD Hall - 2019
September 2018
Civil Construction, bld17

## Slide 12
Control Dewar,
pipe lines
Cryostat
SC coil
Trim Coil
superconducting Solenoid
ASG superconductors,
(Genova) general responsibility:
Cold Mass + Cryostat
Trim Coils
Vacuum System
Control System + PS +…
TPC region
weight ~ 900 t
B0=0.5 T
high level (~ 3x10-4) of magnetic
field homogeneity
HM Vitkovice, Czech Republic:
fabrication of yoke & supports
Rated current: 1790 A
Stored energy: 14.6 MJ
MF measurement in 8×103 points: cooperation with CERN
Notes: The major part of MPD is SC solenoiodal magnet. It is a challenging project due to very high requirement for the magnetic field homogeneity – better that a permill.
After long negotiations a contract is signed with the ASG sc company – the one which produced a big solenoid for CMS. The ASG is responsible for production of coils, cryostat control system etc. In addition the company takes responsibility for the overall supervision and final characteristics.

## Slide 13
Stage I: TPC, TOF, ECAL, ZDC, FFD + ITS(OB)
MPD-ITS (OB) is now recognized at Stage I
Stage I: overall commissioning
starts in 2022 (t.b.c.)
Stage II : ITS(IB) + EndCap (CPC, Straw, TOF, ECAL)
FHCal
FFD
Transfer of High Tech Instrumentation
Know-How from CERN to NICA-MPD
Notes: The MPD will be put in operation at two stages. At the first one the barrel part will be equipped with major tracking detector TPC, TOF end ECAL. FHC and FD will be operational as well.
At the second stage the detector will be supplemented with IT and end cap subdetectors.

## Slide 14
CERN will procure, test and deliver to NICA
19’000 ALPIDE Monolithic Active Pixel Sensors for the MPD ITS
4’500 SAMPA electronic circuits for the TPC readout
5’000 FEAST DC/DC converters for the ECAL MPD
Jigs and fixtures for module and supermodule assembly for the MPD ITS
Training of personal for assembly and QA certification modules and supermodules of the MPD ITS
Provision of complete technical and commercial information on parts of the
new ALICE Inner Tracking System, including drawings, internal technical reports, quotes, etc.
Items to be shipped from CERN formulated in Addendums to the Protocol

## Slide 15: MPD ITS based on the ALPIDE MAPS CERN technology
Layer | Number of staves | Number of ALPIDEs per a stave | Rmin, mm | Rmax, mm | Ladder active length, mm
1 | 12 | 12 | 22.4 | 26.7 | 360
2 | 22 | 23 | 40.7 | 45.9 | 608
3 | 32 | 37 | 59.8 | 65.1 | 708
4 | 18 | 196 | 144.5 | 147.9 | 1190
5 | 24 | 196 | 194.4 | 197.6 | 1468
Beam pipe Ø = 38 mm
Notes: The MPD TPC bore of 500 mm diameter allows installation of 5-layer system based on ALPIDE MAPS of size 15х30 mm2
ALPIDE has 512х1024 active pixels (524’288 pixels!) of 50 um (Inner barrel) and 100 um(Outer) thickness
The active area of ITS is 4,17 m2 (IB=0,76 ;OB=3,41) with 10 416 sensors (IB=1184; OB=8232) to placed in space with
аccuracy better 0,5 mm !
The OB will be built out existing technology developed by ALICE ITS Upgrade team (L.Musa et al)
The IB is a subject of joint R@D will be based on the idea of ALICE for the Supper ITS involving stiching technolodgy
For long super-ALPIDES sensors
OB is to be build and commissioned by the end of 2022
IB is to be installed together with the beampipe of reduced diameter later 2025 (?)

## Slide 16: ITS Monte-Carlo simulation scheme within MpdRoot
At the reconstruction stage the main simulation tasks include:
generation of detector responses (Hit Producer);
reconstruction of particle tracks using generated hits (Track Finder) ;
reconstruction of the primary and secondary interaction vertices (Track Analysis).
Particle MC transport
through ITS: GEANT3
Hit generation
Vertices reconstruction
Track finding: KF
Event MC generator:
LAQGSM
MC generator

## Slide 17: Selection criteria
D0 selection parameters:
distances of closest approach to the collision vertex DCAπ,K ,
two-track separation DCAD ,
decay path λD,
pointing angle θD.
Selection criteria:
DCAπ > С1 && DCAK > С2 && DCAD < С3 && λD > С4 && θD < С5
The parameters of the corresponding selections are optimized by maximizing
the signal significance :
where S and B are the estimated numbers of the signal and background events.
Do → K- + π+

## Slide 18: D0 reconstruction – cut selection
dcaK>0.01 сm & dcaPi>0.01 сm & distPiK < 0.02 cm & path(D0) > 0.025 сm & angle(D0) < 0.2 rad

## Slide 19: D0 reconstruction – invariant mass spectrum for ITS#1
D0→ K‒ + π +
ITS – option#1:
t1=t2=t3=50μ
t4=t5=700μ

## Slide 20: D0 reconstruction – invariant mass spectrum for ITS #1
D0→ K‒ + π +
t1=t2=t3=50μ
t4=t5=700μ

## Slide 21: D0 reconstruction – TMVA selection
IT – option#2:
t1=t2=t3=200μ (IB ITS2)
t4=t5=700μ (OB ITS2)
DCA(π, K,D0), path(D0),angle(D0) cuts
BDTD cut
IT – option#1:
t1=t2=t3=50μ (IB ITS3)
t4=t5=700μ (ОВ ITS2)

## Slide 22: D0 reconstruction – invariant mass spectrum
D+→ K‒ + π + + π +
ITS – option#1:
t1=t2=t3=50μ (IB ITS3)
t4=t5=700μ (OB ITS2)
ITS – option#2:
t1=t2=t3=200μ (IB ITS2)
t4=t5=700μ (OB ITS2)
Preliminary results of TMVA-BDTD simulations of 10M 9 GeV central Au-Au central collisions (V. Kondratiev)

## Slide 23: D+ reconstruction – TMVA selection
ITS – option#1:
t1=t2=t3=50μ (IB ITS3)
t4=t5=700μ (OB ITS2)
IT – option#2:
t1=t2=t3=200μ(IB ITS2)
t4=t5=700μ (OB ITS2)
DCA(π, K,D+), path(D+),angle(D+) cuts
BDTD cut

## Slide 24: D+ reconstruction – invariant mass spectrum
D+→ K‒ + π + + π +
ITS – option#1:
t1=t2=t3=50μ (IB ITS3)
t4=t5=700μ (OB ITS2)
ITS – option#2:
t1=t2=t3=200μ (IB ITS2)
t4=t5=700μ (OB ITS2)
Preliminary results of TMVA-BDTD simulations of 10M 9 GeV central Au-Au central collisions (V. Kondratiev)

## Slide 25
Particle | D0 |  | D+ | 
Decay channel | D0→ K- + π + |  | D+→ K- + π + + π + | 
Multiplicity (HSD | 10-2 |  | 10-2 | 
BR,% | 3.9 |  | 9.1 | 
IT option | #1 | #2 | #1 | #2
S/B(2σ) | 0.43 | 0.10 | 0.65 | 0.27
Significance | 15.1 | 2.2 | 28.5 | 7.6
Efficiency,% | 1.9 | 0.13 | 2.3 | 0.3
D-meson parameters in 10М central Au+Au collisions at = 9 ГэВ

## Slide 26: MC and reconstructed pt-spectra of D0-mesons and their decay products
D0 mesons
Pions
Kaons
Yu.Murin. 4-th CBM-China Meeting

## Slide 27: MC and reconstructed pt-spectra of D+-mesons and they decay products
D+ mesons
Pions
Kaons

## Slide 28
Stage I: Installation of OB (2022)
~ 9 500
ALPIDE MAPS
in 5 cylinders of 2 barrels
D+
K-
π+
π+
tentative assembly
layout
ITS realization in two Steps (OB first) due to BP sequence
4,9۰109 pixels, active area 3,9 m2.
MPD beam pipe
Stage I: 64 mm in diameter
Stage II:
38 mm in diameter
Stage II: OB+IB (2022+3) ?

## Slide 29
Task 1: Assembly of HICs and OB Staves (60 pcs incl.)
JINR & CCNU
Truss length is 1540 mm. Modules (HICs) are are located on two cooling plates .
OB stave carriers 196 sensors.
The MPD ITS need is 42 OB staves.

## Slide 30
Task 2 . FC trusses (60), cooling plates (120)
JINR &SPbSU

## Slide 31
Task 3 . Mechanics for integration with the TPC - JINR

## Slide 32: solving of the “GBTx problem”
Task 4. Updating the readout electronics
Task 5. Assembly the System and bench and in-beam
tests of the parts
Task 6. Writing the TDR

## Slide 33
Task 7. R@D for the IB as part ALICE ITS3 upgrade plan
(under supervision of CERN)

## Slide 34
3 pillars of assembling process:
Infrastructure
Trained stuff
Custom designed fixtures
Planar EM-4370
iBond5000
SuperDry SD-702-02
Memmert UFP-800
VB LHEP existing Infrastructure: Two Clean Rooms (ISO-7 and ISO-8) equipped for assembling modules and of the MPD ITS

## Slide 35
Conclusions
and summary
Yu.Murin. 4-th CBM-China Meeting
Notes: Few words on the NICA …

## Slide 36: major milestones of the MPD ITS project (tentavily!)
2018 – paper work and infrastructure
2018 –2019 – simulations and start of delivery of parts from CERN
2019 – organization of the Russian-Chinese Consortium
2019 – Writing TDR ( Version 1)
2019 – Production of first HICs at VBLHEP
2020 –2021 – Mechanics including parts for integration
2020 –2021 – updating the readout chain
2020 –2022 – R@D effort on IB together with ALICE
2020 –2022 – Production HICs, assembly of OB staves
2022 (?) – ITS-OB assembly, bench testing, commissioning
2025( ?) – ITS-OB+IB commissioning (Stage I)

## Slide 37
summary
The MPD-ITS project is both scientific- and time-wise well justified
The project has a solid reason to be accomplished in two stages
The MPD-ITS(OB) (stage 1) one is now recognized and approved for financing at JINR
The MPD-ITS(IB) (stage 2) contains R@D proposed to be performed under the supervision of ALICE Collaboration (ITS3)
The project effort due to its technical complexity cannot be undertaken by JINR alone and calls for organization of a Consortium of Institutes from Russia and China functioning at least till 2025

## Slide 38
Thank you