## Slide 1
Status of high rate MRPC for CBM-TOF
  Wang Yi
  Department of Engineering Physics, Tsinghua University

## Slide 2
  Introduction on FAIR and CBM-TOF
Development of low resistive glass
High rate MRPC for CBM-TOF
Status of STAR-eTOF and mCBM
Conclusions
Outline

## Slide 3
The phase diagram of strongly interacting matter

## Slide 4
Facility for Antiproton &Ion Research: FAIR

## Slide 5
Layout of CBM detector

## Slide 6
The structure of CBM-TOF wall
CBM-ToF Requirements
Full system time resolution sT ~ 80 ps
Efficiency > 95 %
Rate capability  30 kHz/cm2
Polar angular range 2.5°– 25°
Occupancy < 5 %
Low power electronics
(~100.000 channels)
Free streaming data acquisition
Au+Au, Center, 10AGeV
Simulated with CBM ROOT

## Slide 7
MRPC
2
3
Optic (~50m)
CBM CLK (40MHz)
ToF CLK (160MHz)
MRPC
MRPC
MRPC
ToF SYNC Signal
Counting-Room
CAVE
Example for 192 Channel
Electronics & Readout chain

## Slide 8
Padi8
GET4
FPGA - TDC
TOF electronics

## Slide 9
Precision between two channels
PADI X & GET4 V1.23
below 30ps
below 30ps
below 30ps
Pulser test of PADIX & GET4

## Slide 10
The voltage drop in the gas gap:
Two main ways to improve rate capability:
Reducing bulky resistivity of electrode glass (CBM)
Reducing the avalanche charge (ATLAS)
The smaller the voltage drop, the higher efficiency and higher rate capability!
How to increase rate of MRPC

## Slide 11
Development of low resistive glass
Performance of the glass
Glass mass production
Yield >100m2/month
Aging test with X-ray source
Online test system. The efficiency and time resolution can be obtained by cosmic ray while irradiated by X-rays. 0.1C/cm2 charge is accumulated in 35 days.

## Slide 12
Continuous melting
Continuous pouring
Continuous annealing
Technology of R&D
Glass R&D and mass production

## Slide 13
Rate: 70kHz/cm2
Time resolution: 40 ps
Rate capability of high rate MRPC
Even though the rate is 70kHz/cm2, the efficiency is still higher than 90% and the time resolution is about 80ps.
Test results at Nuclotron, Dubna

## Slide 14
Prototype design for CBM-TOF
Strip-MRPC
Inner zone-MRPC

## Slide 15
15
15
Design of strip-MRPC for high rate region
Glass: low resistive glass
0.7mm thick, 33cm x 27.6cm
Strip: 27cm x 0.7cm, 0.3cm interval, 32 strips
Gas gap: 8 x 0.25mm, two stacks
Honey
PCB
Mylar
Graphite
Fish line
Glass
Upper stack
lower stack

## Slide 16
16
High rate test in February 2015 at SPS CERN
13 GeV Ar beam
Flux rate around 1kHz/cm2
Buc-2013
THU-Pad
Buc-Ref
PMT
HD-Ref
THU-Strip
HD-P2
Experimental Setup:
USTC
Up setting
Down setting
Beam test @ SPS Feb 2015

## Slide 17
SPS Nov 2015 THU-DU results
Results of each run
Time resolution from tracking method
Performance of the prototype

## Slide 18
The efficiency curve with STAR gas is shifted 300 V behind compared to CBM gas.
CBM-TOF: 90% C2H2F4+5% i-C4H10+5% SF6
STAR-eTOF: 95% C2H2F4+5% i-C4H10
STAR gas, ±5200 V
Time Res: 113.8 ps
CBM gas, ±5600 V
Time Res: 92.9 ps
Performance in different working gas

## Slide 19
The dark current and cluster size increases a little without SF6 in the gas mixture because of the expanded avalanche. At the working point, the performances still satisfy the requirements.
Performance in different working gas

## Slide 20
Two-dimensional code of MRPC
Producttion website:
http://hepd.ep.tsinghua.edu.cn/CBM_TOF/
Mass production of high rate MRPC

## Slide 21
The automatic boundary recognition method makes the measurement more accurate.
1 cm
Visual check of gas gap

## Slide 22
Each spot reprsents the efficiency and time resolution of one produced counter.
All the points are in the qualified region, and most of the counters show a stable performance of 70 ps time resolution and 98% efficiency.
Test results of 33 MRPC

## Slide 24
Picture of STAR-eTOF

## Slide 25
25
green IT cube
Schedule | 
10/2017 | HTD cave & beam line: preparation of construction, start of procurement
11/2017 | HTD cave & beam line: start of construction
11/2017 | mDAQ test stand @ Heidelberg operational
11/2017 | installation of detector subsystems: mechanical design freeze
03/2018 | HTD cave construction completed
04/2018 | mFLES cluster @ Green IT Cube installed
05/2018 | installation of detector stations
06/2018 | start commissioning w/o beam
09/2018 | start commissioning with beam
mCBM@SIS18

## Slide 26
Production of modules for eTOF and mCBM

## Slide 27
Time resolution of STAR-eTOF
eTOF was included in the calibration production for Au+Au at 27GeV
  ~ 2M events available in total
  ~ 600k events with good timing eTOF information after firmware fix
Choose π (0.8-1.2 Gev/c)
System time resolution is 85ps
The time resolution of MRPC is around 60ps

## Slide 28
PID of STAR-eTOF
The (,k)/p separation can reach 2.5~3Gev/c

## Slide 29
Summary
Low resistive glass (~1010 .cm) was developed
The rate capability of high rate MRPC can reach 70kHz/cm2
The construction of CBM-TOF goes smoothly
STAR-eTOF is successful
time resolution<100ps
(,k)/P separation: 3GeV/c
mCBM is ready and run soon…

## Slide 30
Thanks for your attention !