## Slide 1: Calibration system & 20 inch MCP-PMT of WCDA
Bo Gao
20190415

## Slide 2: Outline
Time calibration system
design & test
assembly & installation
calibration method
some results
Work on 20 inch MCP-PMT
WCDA requirements
what have we done
now and next ...

## Slide 3: Calibration system

## Slide 4: Design & Test
Hardware
  wide angle LED (468nm / 120°)
  PMMA fiber bundle （41 fiber/ 40m length / 50 bundles）
  LED driver （based on FPGA, 5 ns width）
Test
  output uniformity
  fiber time offsets

## Slide 5: Assembly & Installation
waterproof
fiber intalled

## Slide 6: Calibration method
“cross calibration”
  2 fiber bundle for 1 cluster
  1 for inside calibration
  2 for neighbour cluster calibration
calculation
  basic concept : A-C = (A-B)+(B-C)
  Tci_chi - Tc0_ch0
    = (TINci_chi-TINci_chx)-(TCRci_chx-TCRc0_ch0)
    ci_chi : test cluster & channel
    c0_ch0: ref cluster & channel
    ci_chx: the “pedal” channel
    TIN: inside fiber calibration result
    TCR: cross fiber calibration result

## Slide 7
the data
  LED signal selection
    LED triggered seperatly
    event mode (nhit > 900)
    LED charge & time
  Q-T recorrection
    T(q) = 20.*pow(q,-1.2)+10.*pow(q,-0.8)
    normalized to 30 PE
cr fiber
in fiber
infiber
Charge
crossfiber
Charge
crossfiber
Time
infiber
Time

## Slide 8: some results - to USTC data

## Slide 9: some results - to offline calibration
hardware
iteration
offline
iteration

## Slide 11
the results
  calibration system : PMT & FEE
  ustc calibration : PMT only
  offline calibration : detector cells (PMT & position & water & FEE)
most of WCDA channel calibration result matchs USTC calibration data and offline calibration result；
some channels are still in check.

## Slide 12: Work on 20 inch MCP-PMT

## Slide 13: WCDA requirements
2# 3# pool, 2220 PMTs are needed
Special design for WCDA
Test
  SPE
  tts / cttd
  linearity
  afterpulse
  dark rate
  etc ...
HV divider
Potting

## Slide 14: what have we done - special design
普通聚焦极
扩张型莲花座聚焦极
NNVT optimized the focus electrode design for WCDA, considering both collection efficiency and TTS (< 7 ns).

## Slide 15
PMT test
  SPE @ Gain = 5×106
  Dark rate (1/3 PE, cooling after 16 hours)
  TTS (LED ratio < 10%)
  Risetime (10GHz scope)
  Afterpulse (500ns - 20μs)
  non-linearity (A-B method)
Np
NV
Pedestal
A
B
C=A+B

## Slide 16: HV divider
Final design （2019.02）
  HV / signal seperated
  special drill drawing for potting glue and cable fasten
  reduce number of welding point to 12

## Slide 17: Potting & FEE debug
Potting based on JUNO potting technique
  2019.01 - sample tube potting
  2019.02-2019.03 - potting production line are setup
FEE debug @ 2019.04
  FEE debug with 3 potting PMTs
  1st batch (15 PMTs) finished and retested
PMT channel | FEE LSB | NNVT qdc | risetime | falltime | amplitude
18 | 42.85 | 5.15E6 | 3.2 ns | 17.6 ns | 6 mV
19 | 41.4 | 4.90E6 | 3.4 ns | 17.2 ns | 6 mV
20 | 42.5 | 5.24E6 | 3.4 ns | 16.8 ns | 6 mV

## Slide 18: now and next - PMT production
PMT procudtion
  about 800 good PMTs are produced in NNVT， ready to potting， all 2270 PMTs will produced in 2019；

## Slide 19: now and next - potting & installation
Potting plan
  252 PMTs / month，> 1500 PMTs delivery in 2019
  batch test platform setup on HZS
    water pressure test
    parameter test platform
installation
  structure
  installation procedure
  protection in delivery
  more ...

## Slide 20: Conclusion
LHAASO-WCDA is the first ground-based cosmic ray & gamma ray detector to use 20 inch MCP-PMT in whole world, and the PMTs are made in China !
We work with pressure and proud !

## Slide 21
二、稳定性研究
Chart: 
| PC1710-2 | PC1710-6 | PC1710-7B | PC1710-8 | PC1711-1 | PC1711-2 | PC1711-3 | PC1711-6 | PC1711-7 | PC1711-8
PeakToValley | 3.007 | 4.438 | 6.515 | 2.57 | 3.596 | 3.773 | 5.829 | 2.621 | 5.275 | 3.666
Chart: 
| PC1710-2 | PC1710-6 | PC1710-7B | PC1710-8 | PC1711-1 | PC1711-2 | PC1711-3 | PC1711-6 | PC1711-7 | PC1711-8
DarkRate(kHz@22℃) | 14.92 | 8.77 | 12.81 | 12.93 | 9.98 | 13.83 | 14.74 | 16.2 | 9.94 | 3.98
Chart: 
| PC1710-2 | PC1710-6 | PC1710-7B | PC1710-8 | PC1711-1 | PC1711-2 | PC1711-3 | PC1711-6 | PC1711-7 | PC1711-8
QE(%) | 30.46 | 23.85 | 28.45 | 30.4 | 28.02 | 27.96 | 30.05 | 26.91 | 22.46 | 29.19
1. 性能一致性
Chart: 
| PC1710-2 | PC1710-6 | PC1710-7B | PC1710-8 | PC1711-1 | PC1711-2 | PC1711-3 | PC1711-6 | PC1711-7 | PC1711-8
TTS(ns) | 6.39 | 6.29 | 6.31 | 6.12 | 6.68 | 6.68 | 6.21 | 6.11 | 5.3 | 5.93

## Slide 22
Chart: 
| PC1710-2 | PC1710-6 | PC1710-7B | PC1710-8 | PC1711-1 | PC1711-2 | PC1711-3 | PC1711-6 | PC1711-7 | PC1711-8
RiseTime(ns) | 1.83 | 1.87 | 1.48 | 1.83 | 1.34 | 1.45 | 1.29 | 1.21 | 1.87 | 1.82
1. 性能一致性
Chart: 
| PC1710-2 | PC1710-6 | PC1710-7B | PC1710-8 | PC1711-1 | PC1711-2 | PC1711-3 | PC1711-6 | PC1711-7 | PC1711-8
AfterPulseRate(%) | 0.16 | 0.15 | 0.19 | 0.19 | 0.22 | 0.18 | 0.19 | 0.24 | 0.33 | 0.31
Chart: 
| PC1710-2 | PC1710-6 | PC1710-7B | PC1710-8 | PC1711-1 | PC1711-2 | PC1711-3 | PC1711-6 | PC1711-7 | PC1711-8
TestVoltage | 1711.5 | 1841.5 | 1781.5 | 1791 | 1801.5 | 1821 | 1822 | 1761 | 1841 | 1791
Chart: 
| PC1710-2 | PC1710-6 | PC1710-7B | PC1710-8 | PC1711-1 | PC1711-2 | PC1711-3 | PC1711-6 | PC1711-7 | PC1711-8
趋势10%线性 | 2710 | 1310 | 1610 | 1480 | 2120 | 1730 | 1205 | 2950 | 2150
二、稳定性研究

## Slide 23
二、稳定性研究
3. 增益稳定性
Chart: 电荷量/C
| 0.432 | 0.864 | 1.296 | 1.728 | 2.16 | 2.592 | 3.024 | 3.456 | 3.888 | 4.32 | 4.752 | 5.184 | 5.616 | 6.048 | 6.48 | 6.912 | 7.344 | 7.776 | 9.504 | 9.936 | 10.8 | 11.232 | 11.664 | 12.096 | 12.528 | 12.96 | 13.392 | 13.824 | 14.256 | 14.688 | 15.12 | 15.984 | 16.416 | 16.848 | 17.28 | 17.712 | 18.144 | 19.008 | 19.872 | 20.304 | 20.736 | 21.168 | 21.6 | 22.032 | 22.464 | 22.896 | 23.328 | 24.192 | 25.056 | 25.92
样管1 | 10700000 | 10900000 | 10600000 | 11100000 | 11800000 | 12300000 | 12500000 | 11400000 | 11500000 | 12600000 | 12200000 | 12500000 | 13100000 | 12300000 | 12100000 | 12500000 | 11700000 | 11900000 | 11700000 | 11100000 | 11900000 | 10700000 | 11000000 | 10900000 | 11200000 | 10600000 | 11500000 | 11600000 | 11000000 | 10600000 | 10600000 | 10100000 | 10400000 | 10900000 | 10400000 | 10900000 | 10100000 | 10100000 | 9870000 | 10700000 | 9820000 | 10300000 | 9680000 | 9209000 | 10210000 | 9835000 | 9918000 | 10240000 | 8970000
样管2 | 10500000 | 11000000 | 11500000 | 12200000 | 11700000 | 12200000 | 11400000 | 12100000 | 12700000 | 11000000 | 13700000 | 13400000 | 11700000 | 11300000 | 11200000
Chart: 
| 0.432 | 0.864 | 1.296 | 1.728 | 2.16 | 2.592 | 3.024 | 3.456 | 3.888 | 4.32 | 4.752 | 5.184 | 5.616 | 6.048 | 6.48 | 6.912 | 7.344 | 7.776 | 9.504 | 9.936 | 10.8 | 11.232 | 11.664 | 12.096 | 12.528 | 12.96 | 13.392 | 13.824 | 14.256 | 14.688 | 15.12 | 15.984 | 16.416 | 16.848 | 17.28 | 17.712 | 18.144 | 19.008 | 19.872 | 20.304 | 20.736 | 21.168 | 21.6 | 22.032 | 22.464 | 22.896 | 23.328 | 24.192 | 25.056 | 25.92
暗计数 | 6170 | 8830 | 7420 | 8830 | 13600 | 11900 | 14200 | 15800 | 22100 | 16800 | 7580 | 9580 | 9580 | 13400 | 21800 | 13500 | 13400 | 10400 | 14300 | 7580 | 6420 | 7750 | 7420 | 7080 | 7170 | 7830 | 15400 | 8670 | 10300 | 10800 | 7500 | 5170 | 15200 | 5833 | 4833 | 6333 | 9250 | 3667 | 4583 | 5917
暗计数率
下降14%
下降32%

## Slide 24
10只样管性能测试
莲花座聚焦极
@22℃ @Gain = 5×106
管号 | 工作电压（V） | 峰谷比 | 量子效率(%) | 暗计数率 (kHz) | TTS (ns) | 上升时间 (ns) | 后脉冲比例(%) | 趋势10%线性
PC1710-2 | 1711.5 | 3.0 | 30.46 | 14.92 | 6.39 | 1.83 | 0.16 | 2710
PC1710-6 | 1841.5 | 4.4 | 23.85 | 8.77 | 6.29 | 1.87 | 0.15 | /
PC1710-7B | 1781.5 | 6.5 | 28.45 | 12.81 | 6.31 | 1.48 | 0.19 | 1310
PC1710-8 | 1791 | 2.6 | 30.41 | 12.93 | 6.12 | 1.83 | 0.19 | 1610
PC1711-1 | 1801.5 | 3.6 | 28.02 | 9.98 | 6.68 | 1.34 | 0.22 | 1480
PC1711-2 | 1821 | 3.8 | 27.96 | 13.83 | 6.68 | 1.45 | 0.18 | 2120
PC1711-3 | 1822 | 5.8 | 30.05 | 14.74 | 6.21 | 1.29 | 0.19 | 1730
PC1711-6 | 1761 | 2.6 | 26.91 | 16.20 | 6.11 | 1.21 | 0.24 | 1205
PC1711-7 | 1841 | 5.3 | 22.46 | 9.94 | 5.3 | 1.87 | 0.33 | 2950
PC1711-8 | 1791 | 3.7 | 31.45 | 3.98 | 5.93 | 1.82 | 0.31 | 2150

## Slide 25
光电倍增管与分压器指标要求 | 
光阴极尺寸 | 直径为20英寸，椭球面
外形尺寸公差 | 玻壳在垂直轴线的平面里的投影直径公差 ≤ 2mm，高度差 ≤ 10mm
光阴极大小 | 在垂直轴线的平面里的投影直径与玻壳投影直径之比大于90%
玻壳气泡 | 光阴极表面玻壳气泡：没有大于等于5 mm直径的，直径[2 mm, 5 mm)的不超过5个。其它玻璃部分：没有直径大于5 mm的，直径[2 mm, 5 mm)的不超过10个
玻壳耐压 | ＞ 3 atm，典型值为10 atm
正常工作高压值 | 在5×106增益下，工作电压小于2000 V，每批次最大偏差在平均值的±120 V之内
工作电流 | 小于300 µA
单光电子峰谷比 | ＞ 2 @ 5×106
频谱响应曲线 | 300 nm - 650 nm
量子效率 | 在频谱响应曲线的最高点＞ 22%
上升时间 | ＜ 3 ns @ 5×106，典型值为1.4ns
渡越时间分散 | ＜ 7 ns @ 5×106
CTTD | ＜ 4 ns @ 5×106
暗噪声计数率 | ＜ 25 kHz @ 5×106，阈值为1/3 个光电子，环境温度22±3摄氏度
后脉冲比率 | ＜ 2%
稳定性 | 在加上工作高压3小时后到12个小时期间，增益变化小于5%，暗噪声率变化小于10%
抗振稳定性 | 经过振幅1 mm、频率25 Hz正弦波，持续时间30 s振动后，无机械损伤，且产品性能满足远距离运输要求
寿命 | 累计阳极输出电荷75库仑时增益降低程度小于20%
阳极电荷非线性 | ≥ 1800光电子（±10%）@ 5×106，均值大于2000光电子，输入脉冲光源脉宽≤30 ns
元器件与电路板 | 选用精度好于1%和额定功率大于等于1/4 W的金属膜电阻，电容选用耐压3千伏以上的陶瓷电容

## Slide 26: 计算结果-时间差传递
以某一单元（igcell = 3）为例，阵列参考单元igcell=440（cluster12，cell8）
  传递路径1：(0,3)->(5,8)->(10,8)->(11,8)->(12,8)

## Slide 27
以某一单元（igcell = 3）为例，阵列参考单元igcell=440（cluster12，cell8）
  传递路径2：(0,3)->(5,8)->(6,8)->(7,8)->(12,8)

## Slide 28
以某一单元（igcell = 3）为例，阵列参考单元igcell=440（cluster12，cell8）
  传递路径3：(0,3)->(1,8)->(2,8)->(7,8)->(12,8)

## Slide 29
以某一单元（igcell = 3）为例，阵列参考单元igcell=440（cluster12，cell8）
  传递路径4：(0,3)->(1,8)->(6,8)->(11,8)->(12,8)