## Slide 1: Progress of LHAASO-WFCTA
Shoushan Zhang
Institute of High Energy Physics
LHAASO collaboration meeting，Nanjing， 2019/4/13-15

## Slide 2
WCDA:78,000 m2 3000 cells (25m2/cell)
WFCTA:
18 Cherenkov telescopes (1024 pixels/telescope)
LHAASO
KM2A:
5195 EDs
1171 MDs
Daochen, Sichuan (29o21’ 31” N, 100o08’15” E, 4410 m a.s.l., 600 g/cm)

## Slide 3: LHAASO science in cosmic ray measurement
0.1-10 PeV (Cherenkov mode)
  pure proton and light nuclei (P+He) spectra
  6 telescopes (30°in zenith) + ¼ WCDA
1- 100 PeV (Cherenkov mode)
  Pure iron or heavy nuclei spectra
  18 telescopes (45 °in zenith) + scintillator detectors + muon detectors array
>100 PeV (fluorescence mode)
  2nd knee
  20 telescopes + muon detectors array
  Measure individual cosmic ray spectra from 10TeV to EeV
  Multi-parameters, Multi-stages

## Slide 4: Wide Field of View Cherenkov Telescope (WFCTA)
5m2 spherical mirror
32×32 SiPMs array
Pixel size 0.5°
FOV: 16°× 16°
Portable design: easy to switch the array configurations
SiPM camera
A prototype of WFCTA

## Slide 6
Six movable/adjustable containers, and spherical mirrors have been installed at LHAASO site.

## Slide 7: Schematic diagram of SiPM camera assembly
AB1
AB2
DB
Cluster
SiPM camera box
SiPM camera：32×32 SiPMs
64 ×
A module has 4×4 SiPMs.
Optical filter
In the cleaning room (Yunnan university lab)

## Slide 8
Digital Board
Analog Board
V&T compensation loop board
Metal frame
SiPM board
Winston cone
Light concentrator (Winston cone): is to increase the effective area of the SiPM
SiPM board: 16 SiPMs, 16 temperature sensors (embedded in the SiPM chip ), and 16 pre-amplifiers
Voltage and temperature compensation loop:
  16 temperature and high voltage compensation loops;
  16 channels of high voltage power supply.
Analogue board: 16 channels of amplifier and shaping circuit
Digital board: 50 MHz FADC and FPGA
  Square SiPM：15 mm×15 mm

## Slide 9
resolution
Dynamic range

## Slide 10
Telescope pointing： zenith angle 0 °;
Running time：from 2019-01-29.
A coincidence event of WFCTA and WCDA

## Slide 11
Event Rate with time: 50Hz – 100 Hz
Total size distribution
Delta time between two arriving events
log10(total Npe)
3 3.5 4 4.5 5 5.5
Exponential fitting
2019/04/06
Trigger condition: single pixel threshold = 30pe & pattern=3 adjacent pixels

## Slide 12
Air in
℃
20℃
15℃
10℃
5℃
0℃
Air out
Temperature distribution
℃
20℃
15℃
10℃
5℃
0℃
Night
Day
8.9℃
-1.1℃
Air in
Air out

## Slide 13
Gain instability is within ±1% in the whole night
Gain ununiform is less than ±2% in the camera
Mirror
UV light 400 nm
SiPM camera
UV LED
UV-LEDs are mounted at the center of the mirror to monitor and calibrate the gain of the SiPM camera.
Gain instability is within ±1% in the whole night after the temperature and high voltage compensation loops.
The temperature distribution on camera is within the adjustable range of high voltage and temperature compensation loops.

## Slide 14
The telescope can be run in the moon night
Stars passing through the field of view of the telescope
See Dr. Lingling Ma’s talk in 15 April
Stars can be used to calibration the direction of the telescope and study the spot shape etc.

## Slide 15
Filter window：AR + cutoff
To improve signal to noise ratio
Sky background light spectrum
in the moon less night
Filter
Moon less night
Moon night
NSB(without filter)/NSB（with filter）
λ （nm）
550 nm

## Slide 17
Device | Parameters
N2 laser | Wave length=337nm Energy≥170μJ
YAG laser | Wave length=337nm Energy≥2mJ
3-D Rotary Platform
Calibration and Atmosphere Monitoring
See Dr. Fengrong Zhu’s talk in 15 April

## Slide 18
Conclusion and future plan
First Cherenkov telescope has been successfully run in January 2019.
Six movable/adjustable containers, and spherical mirrors have been installed at LHAASO site.
More stable version online FPGA program would be finished in May 2019.
Dynamic threshold and more function FPGA program would be finished in July. (see Prof. Guoqiang Zeng’s talk in tomorrow)
  Single pixel threshold: using signal to noise ratio (S/N>n), threshold varies with the intensity of the sky background light.
  More functions: e.g. recording more longer pulse width for laser event
Second camera will be installed at LHAASO site before 26 April.
Total 6 cameras will be installed at LHAASO site in August.
Total 10 telescopes will be installed at LHAASO site in the end of 2019.

## Slide 19: Thank you for your attention!

## Slide 21
Task and collaboration of WFCTA
Institute of High Energy Physics
Institute of High Energy Physics
SiPM camera
Task
Collaboration
Movable and adjustable container
Yunnan University
  Geneva University
Institute of High Energy Physics
Spherical mirror
Calibration system
Southwest Jiaotong University
Readout electronic system
Sichuan University
National Space Science Center
Slow control system