## Slide 1: Application controlled by MicroTCA at DESY
Holger Schlarb, Group Leader MSK/DESY
IHEP, Beijing, 23. June 2019

## Slide 2: DESY on a glance

## Slide 3
NanoLab
Synchrotron radiation source (highest brilliance)
VUV & soft-x-ray free-electron laser
MPI-SD
FLASH
PETRA III
+
X-Ray Free-Electron Laser
atomic structure & fs dynamics
of complex matter
DESY activities : birds view …
AMTF
SINBAD
REGAE
CMTB
DESY II
LINAC II
PIA
PETRA ext. Nord
PETRA
ext. East

## Slide 4: European EuXFEL
North of Germany: between Hamburg Bahrenfeld and Schenefeld
Super conducting accelerator with up to 17.5 GeV electron beam energy.
Three undulator beamlines in two branches (north and south).
In total 6 experiments, 4 for hard X-rays and 2 for soft X-rays.
Experimental hall in Schenefeld
Undulators/Photon beamlines
Start on the DESY campus
Accelerator
1.9 km/ 17.5 GeV
Electron beam
distribution
Notes: Before you start editing the slides of your talk change to the Master Slide view: Menu button “View”, Master, Slide Master:
Edit the following 2 items in the 1st slide: 1) 1st row in the violet header: Delete the existent text and write the title of your talk into this text field 2) The 2 rows in the footer area: Delete the text and write the information regarding your talk (same as on the Title Slide) into this text field.
If you want to use more partner logos position them left beside the DESY logo in the footer area Close Master View

## Slide 5: FLASH = Free electron LASer at Hamurg
TESLA type superconducting accelerating modules 1.3 GHz
FLASH1 fixed gap undulators
3rd harmonic sc module 3.9 GHz
FLASH1 Experimental Hall
Extraction to FLASH2
FLASH2 variable gap undulators
315 m
5 MeV
150 MeV
1250 MeV
Bunch Compressors
450 MeV
Accelerating Structures
RF Stations
Lasers
RF Gun
Soft X-ray Undulators
sFLASH
FEL Experiments
Photon Diagnostics
Beam Dump
THz
FLASH1
FLASH2
FLASH2 Experimental Hall
Albert Einstein
Kai Siegbahn
FLASH.
Free-Electron Laser
in Hamburg
| Application controlled by MicroTCA at DESY | Holger Schlarb | MTCA/ATCA Workshop for Research and Industry | IHEP 23.06.2019
Normal conducting 1.3 GHz RF gun
Ce2Te cathode
Two Nd:YLF based ps photocathode lasers

## Slide 6: Motivation & History

## Slide 7: Main motivation …
+ MOSA = Modular Open System Approach
 no vendor lock-in situation!!!! Any company can step in!
reduce development expense, design cycle time, and manufacturing costs
Access to hardware/software/firmware (to provide functionalities we need)
Performance
+
Functions
+
Availability
7
Notes: Before you start editing the slides of your talk change to the Master Slide view: Menu button “View”, Master, Slide Master:
Edit the following 2 items in the 1st slide: 1) 1st row in the violet header: Delete the existent text and write the title of your talk into this text field 2) The 2 rows in the footer area: Delete the text and write the information regarding your talk (same as on the Title Slide) into this text field.
If you want to use more partner logos position them left beside the DESY logo in the footer area Close Master View

## Slide 8: History of MicroTCA@DESY
Nov. 2005: Reliability Workshop in Grömitz, Germany
  Joint meeting with ILC (intern. linear collider, 33km, 500GeV)
Dec. 2007: European XFEL Crate-Standard Workshop
  MicroTCA and ATCA was defined to be used
Mar. 2009: First PICMG Meeting “xTCA for Physics”
  Hardware group: rear I/O and timing
  Software group: standardization of interfaces for FPGAs…OPsys
Oct. 2011: Official announcement of PICMG Specification
  “MTCA.4 Enhancements for Rear I/O and Precision Timing“
Jul. 2012: Start of Helmholtz Validation Funds till Dec. 2014
  „MicroTCA.4 for Industry“
Jan. 2014: Reestablish HW/SW PICMG working groups
  „MicroTCA.4.1 release: 01.Nov 2016“
Oct. 2016: Start of MicroTCA TechLab
Jan. 2017: Commissioning European XFEL …
31km
ILC
8
Notes: Before you start editing the slides of your talk change to the Master Slide view: Menu button “View”, Master, Slide Master:
Edit the following 2 items in the 1st slide: 1) 1st row in the violet header: Delete the existent text and write the title of your talk into this text field 2) The 2 rows in the footer area: Delete the text and write the information regarding your talk (same as on the Title Slide) into this text field.
If you want to use more partner logos position them left beside the DESY logo in the footer area Close Master View

## Slide 9: Start: small … medium … large scale …
Equipping of facilities …
2012 REGAE ~ 1 crate
2013 FLASH II ~ 20 crates
2018 Refurbish ~ 50 crates
2015/16 European XFEL ~ 250 crates
RF controls
History of MicroTCA at DESY
2024 PETRAIV …
Notes: Before you start editing the slides of your talk change to the Master Slide view: Menu button “View”, Master, Slide Master:
Edit the following 2 items in the 1st slide: 1) 1st row in the violet header: Delete the existent text and write the title of your talk into this text field 2) The 2 rows in the footer area: Delete the text and write the information regarding your talk (same as on the Title Slide) into this text field.
If you want to use more partner logos position them left beside the DESY logo in the footer area Close Master View

## Slide 10: MicroTCA@Accelerators

## Slide 11: European XFEL Linac
Systems using MicroTCA in EuXFEL Accelerator Tunnel
| Application controlled by MicroTCA at DESY | Holger Schlarb | MTCA/ATCA Workshop for Research and Industry | IHEP 23.06.2019

## Slide 12: European XFEL Linac
Systems using MicroTCA in EuXFEL Accelerator Tunnel
| Application controlled by MicroTCA at DESY | Holger Schlarb | MTCA/ATCA Workshop for Research and Industry | IHEP 23.06.2019

## Slide 13: Standard set of MicroTCA modules …
Standard set of MicroTCA modules used in the European XFEL accelerator control system
MTCA.4 Backplane
Ethernet
MCH
Trigger
Clock
Timing
From central timing
CPU
Clock
Interlock
Machine
Protection
System
Common Modules
Application Modules
Trigger
Interlock
Clock
ADC
Digital I/O
Controller
Electron Beam Diagnostics
Laser Controls
Kicker Controls
Special Diagnostics
  Arrival time monitors
  Kalypso
  CRISP
LLRF
RF Coupler Interlocks
Magnet and Vacuum Controls
Photon Beam Diagnostics
  Gas Monitor Detector
  Imagers
  …
Courtesy K. Rehlich
| Application controlled by MicroTCA at DESY | Holger Schlarb | MTCA/ATCA Workshop for Research and Industry | IHEP 23.06.2019

## Slide 14: Timing & Clock systems
Timing System @ EuXFEL
Star topology with master timing system synchronized to 1.3 GHz reference from master oscillator
Timing Master distributes encoded data with events for trigger, bunch pattern table, clocks to all receivers across the accelerator subsystems as well as shot or train ID for tagging data
Data Word
Data Word
Master Transmitter
Receiver
delay
Data Word
1
delay
Machine Protection
Limitation of bunches
&
delay
Trigger out
Qualified
Trigger out
Bunch Pattern
Trigger #
Timestamp
Macropulse ID
Bunch Pattern Table:
Number of bunches with source and destination
Data
Data
Clock
÷
Clock out
Master
Clock
Local Trigger Mask
1
1.3 GHz
Drift Compen-sation
Up to 4km optical link
Courtesy K. Rehlich
| Application controlled by MicroTCA at DESY | Holger Schlarb | MTCA/ATCA Workshop for Research and Industry | IHEP 23.06.2019

## Slide 15: Timing & Clock systems
Timing System Workhorse – NAMC-psTimer AMC
Transmitter
Daughter Board
IN OUT OUT OUT
2 x Trigger out
1 x Clock out
RJ45
LVDS
2 x Trigger out
1 x Clock out
4 x General I/O
Three optional RTM variants:
9 lemo outputs, SFP outputs, optical outputs with more trigger or clock signals
MicroTCA backplane
Clocks: TCLKA and TCLKB,
Trigger: 8 x M-LVDS
Fiber Optics
SFP
2 x Trigger out
1 x Clock out
Courtesy K. Rehlich
NAMC-psTimer AMC
Tutorial on MicroTCA.4
Timing System
Kay Rehlich
length compensated
10 ps jitter
| Application controlled by MicroTCA at DESY | Holger Schlarb | MTCA/ATCA Workshop for Research and Industry | IHEP 23.06.2019

## Slide 16: Machine Protection System (MPS)
Machine protect to prevent acc. & photon sub-system damages
Tight connection timing & MPS
160 collectors boards
~ 4000 different signals (magnets/BLMs/toroids/vacuum/ diagnostic/couplers/waveguides/..)
Beam destination & Beam Modes
 up 500kW electron beam power
 damages within ~ few us possible
3.5 km
Laser Pulse Controller
Timing Master
MPS Master
| Application controlled by MicroTCA at DESY | Holger Schlarb | MTCA/ATCA Workshop for Research and Industry | IHEP 23.06.2019
Courtesy: J. Jäger et. al

## Slide 17: Machine Protection System (MPS)
MPS Hardware
DRTM-MPS
DAMC2
45 digital inputs (RS422)
7 digital outputs (RS422)
3 input lines from backplane
2 output lines to backplane
3 digital inputs from FMC-card
I2C-bus to FMC-card
PCIe-bus to all FPGA-registers
4 double-fibred bi-directional optical links (SFPs)
IPMI and JTAG for firmware updates
RS422 in
RS422 out
FMC
PCIe
BP
SFPs
Safety & availability & timeliness
  all machine safety-relevant functions are realized within FPGA logic (~100 ns latency)
  to be independent from the availability of network, operating system, DOOCS-servers, PCIe-device drivers …
Maintainability & scalability
  MPS architecture can be extended by utilizing the cascaded communication topology
  same firmware on every board, same DOOCS-server on every crate
  all alarm-responses can be configured through DOOCS/JDDD even during machine run
  boards and RTMs are hot-swappable
| Application controlled by MicroTCA at DESY | Holger Schlarb | MTCA/ATCA Workshop for Research and Industry | IHEP 23.06.2019
Courtesy: J. Jäger et. al

## Slide 18: Technical InterLock (TIL) for Power coupler & Cavity
Superconducting cavity & coupler protection system EuXFEL/FLASH
Sensors per coupler / cavity ( = 32 x 6 = 192 inputs)
  3x e- antenna (free electrons)
  1x spark (light)
  2x temperature
Sensors per RF-Station (32 cavities)
  6x vacuum
  2x cryogenic (He level, He presure)
DRTM-TIL
DAMC02
MPS/Kly/LLRF
Courtesy: D. Tischhauser
see MTCAWS2018
| Application controlled by MicroTCA at DESY | Holger Schlarb | MTCA/ATCA Workshop for Research and Industry | IHEP 23.06.2019

## Slide 19: Technical InterLock (TIL) for Power coupler & Cavity
Superconducting cavity & coupler protection system EuXFEL/FLASH
Courtesy: D. Tischhauser
Ref: MTCAWS2018
| Application controlled by MicroTCA at DESY | Holger Schlarb | MTCA/ATCA Workshop for Research and Industry | IHEP 23.06.2019

## Slide 20
System overview
HF-Oscillator
Local RF (uLOG)
Field detectors (uDWC)
DAQ (SIS8300L)
Controller (TCK7)
Clocks
Vector
Modulator
HPA
Waveguide
FPGA
ADC
ADC
DAC
DAC
ADC
LO
for
ref
probe
Cavities
ZF
HF
FPGA
HF
FB Feedback
loop
AMC
uLOG
RTM
AMC
RTM
RTM
eRTM
X 8
Low Level RF System
| Application controlled by MicroTCA at DESY | Holger Schlarb | MTCA/ATCA Workshop for Research and Industry | IHEP 23.06.2019

## Slide 21: Low Level RF System
HF-Oscillator
Local RF (uLOG)
Field detectors (uDWC)
DAQ (SIS8300L)
Controller (TCK7)
Clocks
Vector
Modulator
Klystron
Waveguide
FPGA
ADC
ADC
DAC
DAC
ADC
LO
for
ref
probe
Cavities
ZF
HF
FPGA
HF
FB Feedback
loop
AMC
uLOG
RTM
AMC
RTM
RTM
eRTM
X 16
System overview
| Application controlled by MicroTCA at DESY | Holger Schlarb | MTCA/ATCA Workshop for Research and Industry | IHEP 23.06.2019

## Slide 22: EuXFEL RF station
KLYSTRON
CM1 (8 cav.)
CM2 (8 cav.)
CM3 (8 cav.)
CM4 (8cav.)
LLRF master
LLRF slave
Drift compensation
Reference synchr. + distr.
Clocks + local oscillator
Main controller crate (MicroTCA)
Piezo*
Power supplies
* not installed yet
| Application controlled by MicroTCA at DESY | Holger Schlarb | MTCA/ATCA Workshop for Research and Industry | IHEP 23.06.2019
More than 3000 RF channels
Requirements: <0.01deg and <0.01%

## Slide 23: LLRF for EuXFEL: crate occupation
Front
Rear
| Application controlled by MicroTCA at DESY | Holger Schlarb | MTCA/ATCA Workshop for Research and Industry | IHEP 23.06.2019

## Slide 24: Diagnostics: Beam position monitor
110 BPMs installed at FLASH
Ref: B Lorbeer et al 2018 J. Phys.: Conf. Ser.1067 072011
AMC: SIS8300L Digitizer
RTM: RF front-end
Double Peak detector electronics
4 input channels
Test pulse generator
Test output connectors
Vrf_pk_min = 5mV
B3dB ~ 600MHz (~-6dB@ 1GHz)
N.F.=3.3dB(maximum gain)
RF-Gain ~40dB
1um
Delay-Line:1/2”, ~26m, ~100ns
RF front-end
50pC
| Application controlled by MicroTCA at DESY | Holger Schlarb | MTCA/ATCA Workshop for Research and Industry | IHEP 23.06.2019

## Slide 25: Diagnostics: Toroid readout system
Used charge measurement & beam transmission based Interlock
First beam in XTL
1 pC
Charge measurement with ~0.2pC resolution RMS
36 Toroids along EuXFEL
Integrated test pulser functionality
Machine Protection:
  Fast Protection: transmission of adjacent Toroids
  Slow Protection: consecutive alarms block further bunchtrains
Self Trigger: beam detection on pC level
SIS8300L2
RTM Toroids
Ref: M. Werner MTCAWS2016
| Application controlled by MicroTCA at DESY | Holger Schlarb | MTCA/ATCA Workshop for Research and Industry | IHEP 23.06.2019

## Slide 26: Beam Loss Monitors
474 BLMs along the EuXFEL for protection
Plastic scintillators and quartz rods (Cherenkov radiation)
DAMC02 + RTM-BLM
  Analog alarm path, independent from digital electronics and timing
Machine Protection:
  Fast Protection: single, multibunch and integral alarms cutting within current bunchtrain
  Slow Protection: consecutive alarms block further bunchtrains until user acknowledgement
  Integrated tests: LED and software alarm
Courtesy: T. Wamsat IBIC2018, WEOB03
| Application controlled by MicroTCA at DESY | Holger Schlarb | MTCA/ATCA Workshop for Research and Industry | IHEP 23.06.2019

## Slide 27: Special Diagnostics: THz spectrometer
Special Diagnostics – CRISP THz Spectroscopy with MHz readout
RTM: TAMC532-TM AMC TEWS TAMC532
4 pyroelectric detector board with 30 channels
Parallel readout of all 120 channels by 4 TAMC532 each with 32 ADCS and TAMC532-TM shaper RTM
Channel 1
Channel 120
...
Diffraction
Radiation
Detector Board
Courtesy C. Gerth/B. Schmidt/ N. Lockmann
absorber
Electron bunch length characterization
32 ch.
shaper
+
14bit
50 MSPS
ADC
| Application controlled by MicroTCA at DESY | Holger Schlarb | MTCA/ATCA Workshop for Research and Industry | IHEP 23.06.2019

## Slide 28: Special Diagnostics: EO Sampling/ XUV Spectrometer / …
Special Diagnostics – KALYPSO Line Detector with MHz readout
A. Mielczarek et al., IEEE Transactions on Nuclear Science, in print, 2018.
KALYPSO mezzanine card + FPGA Carrier
Parameters for current version 2.1
  256 pixels, 50 µm pitch
  14 bit ADC, 2.7 Mfps
Synchronisation to clock of timing system
Continuous, low-latency data stream out
AIES MFMC (Artix 7)
CAENels SFP2+ 2-ch. Transceiver (FMC20)
Multimode Fibre
(< 500 m, 6.4GB/s)
X2Timer
12V DC
MTCA.4 Crate
KALYPSO
mezzanine card
Courtesy C. Gerth
After machine tuning:
FEL spectra more uniform over pulse train
Start up of FEL tuning:
Instabilities at the end of pulse train
0th order
to experiment
6nm
60nm
1st order
variable line spacing
grating (VLS)
FEL beam
G. Brenner et al.,
Nucl. Instr. and Meth A 635, 99–103 (2011).
KALYPSO detector
CeYAG scintillator screen converts X-ray laser pulses to visible pulses
Soft X-ray Spectrometer
| Application controlled by MicroTCA at DESY | Holger Schlarb | MTCA/ATCA Workshop for Research and Industry | IHEP 23.06.2019
KALYPSO ASIC / 1-D array

## Slide 29: Femtosecond synchronization system
Laser oscillator Locking & Optical fiber links stabilization
Detection
Feedback/
Actuators
Readout/ controls
Balanced
photodetector
DRTM-DWC10
Struck SIS8300L2
Realized by modified LLRF boards
e.g. XFEL Injector Laser …
Photodiode based lock (~ 30 laser osc. at DESY)
Optical synchr. fiber stabilisation ~ 40
Talk on femtosecond Synchr. System
M. Felber
| Application controlled by MicroTCA at DESY | Holger Schlarb | MTCA/ATCA Workshop for Research and Industry | IHEP 23.06.2019

## Slide 30: Misc. MicroTCA Application
“Slow” MTCA.4 Applications
ESD 4-Fold CANbus AMC
Vacuum And Magnet Controls
Magnet Controls connected to P/S controls via CANbus
Vacuum Controls connected via CANbus to vacuum electronics
Large, distributed Dosimetry System
  Using FMC on MPS DAMC2 w/ external DOSIMON Boxes connected via ring line (RS488 telegrams)
RADMON
| Application controlled by MicroTCA at DESY | Holger Schlarb | MTCA/ATCA Workshop for Research and Industry | IHEP 23.06.2019

## Slide 31: XFEL Accelerator Controls
MicroTCA.4-based components used as standard hardware platform (LLRF, Diagnostics, Vacuum, HPRF, Magnets, Timing, ….)
About 250 crates installed, serving more than 10.000.000 control parameters, 700000 DAQ channels & 30 TB/day
Operational from day 1 of deployment
Key benefits:
  Fully automated and standardized installation procedure allows rapid deployment and recovery
  Enhanced remote management via IPMI and Ethernet allow for simplified maintenance
  Extended monitoring and management of module ensure reliable crate operation
  No major hick-ups during commissioning and operation
  Significant benefits due to remote controls of MicroTCA components
| Application controlled by MicroTCA at DESY | Holger Schlarb | MTCA/ATCA Workshop for Research and Industry | IHEP 23.06.2019

## Slide 32: Photon Science Diagnostics & Experiments

## Slide 33: Photon diagnostics/Experiments EuXFEL
Used MicroTCA board portfolio in photon science EuXFEL
Courtesy: P. Gessler see MTCAWS2017
Talk Photon Diagnostics M. Tolkiehn
| Application controlled by MicroTCA at DESY | Holger Schlarb | MTCA/ATCA Workshop for Research and Industry | IHEP 23.06.2019
MicroTCA Crates
Large 12 slot 9U and small 6 slot 2U
(including MCH, Power Supply and CPU)
X2Timer
XFEL Timing System module for synchronization (clocks and triggers) and pulse parameters from NAT
SIS8300
Fast 125MSPS ADC with 10 channels and 16bit resolution for diagnostics and detectors from Struck Innovative Systeme
ADQ412/ADQ14/ADQ7
High-speed digitizers from 1.8GSPS to 10GSPS with 12 to 14 bit resolution from Teledyne SP Devices
DAMC2
Required for Clock & Control system for fast 2D detectors, VETO System, Machine Protection System and photon beam loss monitors from DESY

## Slide 34: Photon diagnostics XFEL
34
Courtesy: P. Gessler
see MTCAWS2017
Notes: Before you start editing the slides of your talk change to the Master Slide view: Menu button “View”, Master, Slide Master:
Edit the following 2 items in the 1st slide: 1) 1st row in the violet header: Delete the existent text and write the title of your talk into this text field 2) The 2 rows in the footer area: Delete the text and write the information regarding your talk (same as on the Title Slide) into this text field.
If you want to use more partner logos position them left beside the DESY logo in the footer area Close Master View

## Slide 35: Photon diagnostics/Experiments EuXFEL
Used MicroTCA board portfolio in photon science EuXFEL
Courtesy: P. Gessler see MTCAWS2017
| Application controlled by MicroTCA at DESY | Holger Schlarb | MTCA/ATCA Workshop for Research and Industry | IHEP 23.06.2019
Aggregation of 16 electron Time-of-Flight tubes
Electrons hitting the detector generate electrical pulses
All 16 channels are digitized with MicroTCA Digitizer
  8 x SP Devices ADQ412-4G Module
  16 Channels @ 2/4GSPS @ 12bit
Possible measurements:
  Angle resolved energy spectrum
  Polarization
Courtesy: Photon Diagnostics Group (XPD) and collaborators

## Slide 36: Photon diagnostics FLASH
36
MicroTCA@FLASH I
MicroTCA@FLASH II
Applications:
Gas Monitor Detector (GMD)
OPIS XUV Spectrometer
Online Spectrometer  Kalypso (256 pixel array MHz readout)
ToF‘s for diverses beam lines and experiements (as local readout system)
Diverse fast photodetectors
Boards: Primarily SP Device (1-7 GSPS) or Struck ADC 125MSPS
Notes: Before you start editing the slides of your talk change to the Master Slide view: Menu button “View”, Master, Slide Master:
Edit the following 2 items in the 1st slide: 1) 1st row in the violet header: Delete the existent text and write the title of your talk into this text field 2) The 2 rows in the footer area: Delete the text and write the information regarding your talk (same as on the Title Slide) into this text field.
If you want to use more partner logos position them left beside the DESY logo in the footer area Close Master View

## Slide 37: Thanks for your attention