## Slide 1: Online monitor for ATLAS Phase I RPC cosmic ray test
Xiangyu Xie (USTC)

## Slide 2: About the cosmic ray (CR) test
Motivation:
  To qualify RPC gas gaps and FEE after assembled in BB5, CERN. (QC)
Prior CR test workflow
  Singlet DAQ
  Go to offline analysis to check the performance
  Fix the problems if exist
  Re-DAQ to check if fixed
  Triplet HV-efficiency scan
    ~13 HV points (from 4600 – 5800V)
    8 areas/Chamber, due to the limitation of TDC channels
    ~ 100 runs are required
    Each run needs ~2 mins to initialize
Setup of DAQ system
η
φ
Area 1
Area 2
Area 3
Area 4
Area 5
Area 6
Area 8
Area 7
Chamber division

## Slide 3: The online monitor
Motivation
  Get the primary results while DAQing
  One-step workflow
  Speed up the test
Features:
  GUI instead of terminal
  Control the VME&TDC
  Reconstruct & display in real time
  Quick analysis report
  Support offline re-analysis
Screenshot of the monitor

## Slide 4: Hardware & software setup
TDC: CAEN V1190a
VME controller: CAEN V1718
Server: CentOS 7.6, GCC 4.8
Developing environment:
  Qt (GCC 4.8)
  Root 6.14.06
  3rd plot library
The DAQ part based on the GIF_DAQ developed by Alexis Fagot
Source code of the monitor is fully available on my Gitlab

## Slide 5: Workflow of the monitor
Config files import:
  Mapping file
  TDC inifile
Data taking / data re-analysis
  Read from TDC / import from disk
  Reconstruct & refresh
Prepare for next DAQ
  Save the raw data
  Clear the TDC buffer & plots
Mapping file
DAQ/Import modes

## Slide 6: Demo of the latest version

## Slide 7: Plots: efficiency curves
Trigger efficiency (for Eta, Phi, Eta&&Phi)
  Definition: P(triggered | scintillators triggered)
  Motivation: to show the RPC acceptance comparing to the scintillators
Reference trigger efficiency (For Eta, Phi , Eta&&Phi, Eta||Phi)
  Definition: P(triggered | reference singlet triggered)
  Motivation: reflects the real efficiency of the chamber / gas gap
  |delta ch| <= 2,
  |delta LE| <=10.0 ns

## Slide 8: Plots: efficiency of channels
Hits distribution (for Eta, Phi)
  Definition: each entry  one hit
  Motivation: To give a quick look if there are broken / noisy FEE channels.
Channel efficiency bar (for Eta, Phi)
  Definition: bin height  reference efficiency of one channel
  Motivation: reflects the efficiency of separate channel
  |delta ch| <= 2
  |delta LE| <=10.0 ns

## Slide 9: Plots: CS & LE histograms
Cluster size
  Definition: the number of strips fired by one hit.
  Motivation：to check out the CS distribution
Leading edge
  Motivation: to confirm the time window
  Distribution width dominated by scintillators

## Slide 10: Plots: 2D plots
2D hit distribution
  Definition:
    One grid  One Eta strip && one Phi strip
    Whole plot  One singlet
    Temperature  Hits number
  Motivation:
    The overall hits distribution
    Easy to find the false welding channels / noisy channels
2D noise distribution
  Definition: as above, but only hits outside the LE window
  Motivation: to check out the noisy points of gap
Noise map
Hit map, a typical example with Phi Ch1&2 disconnected

## Slide 11: Plots: TOT (time over threshold)
TOT 1D distribution (for Eta, Phi)
  Definition:
    The bin height  the average TOT of the channel
    The error  one standard deviation
  Motivation: to check the uniformity of amplifiers
TOT 2D distribution
  Definition:
    temperature  average TOT of eta and phi signals
  Motivation:
    To check the uniformity of amplifiers and gas gaps

## Slide 12: Plots: Time resolution
Use three singlets
  When three singlets triggered
  All channels are utilized
  Definition:
  Time resolution = 0.58 ns
Use two singlets
  When two singlets triggered
  Definition:
  Time resolution = 0.67 ns
Only primary results provided
  The time of walk not calibrated

## Slide 13: Quick analysis report
A pdf-version quick analysis report
  Automatically generated
  Printed all plots

## Slide 14: Extra: tracks broadcasting for AR
Reconstruct tracks from hits of all chambers
  Linear reconstruction:
  In mm unit
Broadcast via TCP/IP
  The event number
  ,, to be sent
Received by an AR program
  A project proposed by Giulio
  For outreach
  May help detector maintaining
  A demo program developed
Serer config

## Slide 15: Demo of the AR program

## Slide 16: Summary
An online monitor for RPC cosmic ray test developed
  Simplify the workflow
  Speed up the test
  Provide various plots
    To check gap/chamber efficiency
    To check gap status
    To check FEE status
  Quick analysis report
Potential in Phase II RPC mass production in China sites
Potential for outreach and detector maintaining