## Slide 1: Beam background simulation in CgemBoss
Influence of different levels of beam background on track reconstruction efficiencies

## Slide 2: Beam background simulation
Simulate additional (random) background clusters
Probability of background clusters per event
Beam background rate per layer
  Details: CGem CDR
  Estimation based on beam background measurement of current chamber
  Nominal estimate for 1th layer: kHz/x-strip
  Conservative estimate for 1th layer: kHz/x-strip
Time window
  Time resolution of CGEM
  Intrinsic time spread of primary ionisation
  Nominal:
  Conservative:
Layer 1
Layer 2
Layer 3
Beam background rate estimate
CGEM CDR
Per event ~1-2 additional
clusters on the 1th layer
Giulio
preliminary + uncalibrated
Neglect beam background in layer2+3

## Slide 3: Effect on reconstruction efficiency
Sample reaction
  tracks
  Same momentum distribution
nTrk | noBkg | Nominal | Consv. | Consv2. | Huge | w/o layer1
--------------------------------------------------------------
1 0.954 0.954 0.955 0.955 0.953 0.954
2 0.969 0.969 0.969 0.969 0.959 0.964
3 0.962 0.961 0.961 0.96 0.927 0.953
4 0.953 0.953 0.951 0.95 0.784 0.939
5 0.943 0.943 0.94 0.939 0.302 0.93
6 0.926 0.925 0.92 0.915 0.017 0.917

## Slide 4: Implementation details
New algorithm CgemBeamBkg
  Available in CVS, part of the next CgemBoss release
Add clusters random in (z,ϕ) to RecCgemClusterCol
Run after CgemClusterCreate, before MdcHoughFinder
Cross-check
  Huge background
  Homogeneously distributed in (z,ϕ)
π track
EventDisplay
#include "$CGEMCLUSTERCREATEROOT/share/CgemClusterCreateOption.txt"
#include "$CGEMBEAMBKGROOT/share/jobOptions_CgemBeamBkg.txt" CgemBeamBkg.ProbLayer1=0.001995; //p1 default value
CgemBeamBkg.ProbLayer2=0.; //p2 default value
CgemBeamBkg.ProbLayer3=0.; //p3 default value
#include "$MDCHOUGHFINDERROOT/share/jobOptions_MdcHoughFinder.txt"

## Slide 5: Summary
Nominal beam background expectation 1th layer : kHz/x-strip,
Neglect layer 2 and 3
New algorithm CgemBeamBkg
Effect on reconstruction efficiency is negligible for low multiplicity events
and small for high multiplicity events