## Slide 1: Longitudinal Beam Polarization@ CEPC-Z
Zhe Duan
On behalf of CEPC Beam Polarization Working Group
2019. 07. 05
This work is supported as a sub-task in CEPC MOST Grant 2018.

## Slide 2: Requirements of longitudinal beam polarization
Figure of merit: Luminosity * f( Pe+, Pe- )
Typically, longitudinal beam polarization > 50% @IPs is required
Not interesting if luminosity loss is too high

## Slide 3: Self polarization @ CEPC
Beam energy (GeV) | 45.5 | 80 | 120
Polarization build-up time (hr) | 256 | 15.2 | 2
Beam lifetime for colliding bunches (hr) | 3.2 | 1.2 | 0.22
Expected equilibrium beam polarization | >50% | < 50% | ~ 0
Beam energy (GeV) | 45.5 | 80 | 120
 | 256 | 15.2 | 2
 | 3.2 | 1.2 | 0.22
 | >50% | < 50% | ~ 0
E. Gianfelice-Wendt, PRAB, 19, 101005 (2016)
Rassmann, et al., AIP Conf. Proc, 570, 169-178, 2001
Increasing energy spread leads to enhancement of synchrotron sideband resonances, and faster reduction of beam polarization with energy.
Beam polarization evolution in an electron storage ring between injections
  , ,

## Slide 4: Beam polarization in CEPC Collider Rings
Top-up injection (continuous injection) is baseline to maintain a high average luminosity
Average beam polarization for continuous injection during physics runs
Self-polarization: equilibrium beam polarization in the ring
Injected beam polarization
Competition between beam decay/injection
and polarization build-up in the ring
@CEPC-Z: > 50%, > 100 hour, ,
The first term is by default negligibly low.

## Slide 5: How to achieve a high average beam polarization ?
Scenario 1: self-polarization + unpolarized injected beam
Mandatory to make
  can be reduced down to ~ 10 hours, with asymmetric wiggler, limited by allowed energy spread increase
  is dominated by radiative Bhabha & beamstrahlung, increase in -> loss in luminosity
Significant loss in luminosity makes this scenario uninteresting, according to FCC-ee CDR
A. Blondel, talk on FCC Week 2017

## Slide 6: How to achieve a high average beam polarization ?
Scenario 2: polarized injected beam
, given that
A high average beam polarization is not in direct contradiction to a high luminosity!
Tasks:
  Preparation of polarized beam in the injector (AGS, RHIC)
  Design of spin rotators in the collider rings (LEP, HERA, SuperB, SuperT-C, RHIC)
  Ensure via spin matching (LEP, HERA)
This scenario is not considered in FCC-ee CDR, and we can make a difference @ CEPC

## Slide 7: Longitudinal polarized e- beam preparation in CEPC
Longitudinal polarization in source & linac
Siberian snake is necessary in the booster to maintain a decent polarization
Spin rotators are necessary in the collider ring to make the polarization along longitudinal direction @ IPs.
Siberian snake
Spin rotators
Polarized electron source is a matured technology, polarization ~ 90% and nC-level bunch charge is achievable

## Slide 8: Key R&D items
At the moment, we’ll focus on the accelerator physics study & design of polarized colliding beams, to give parameter specs. for harewares
  Siberian snake in the booster
  Spin rotators in the storage ring
Additional hardwares
  Polarized electron gun
  Longitudinal polarimeter

## Slide 9: Questions
Physics motivation for longitudinal polarized beams @ CEPC-Z?
  Single beam polarization or both beam polarization is needed?
  At least what level of polarization is required?
  What are the strongest physics cases?

## Slide 10
Thanks!

## Slide 11
Backup
  What about higher CM energy?
    More challenging to maintain beam polarization in the booster: stronger spin resonances, longer snakes
    More challenging to ensure as depolarization is more severe at higher energy