## Slide 1: MOST2 PLL Weekly Report
Xiaoting Li
IHEP
April 8, 2019

## Slide 2: IO definition
IO Name | Description | IO Name | Description
BSEL | Loop bandwidth Configuration | AVDD/AGND | Analog power
ISEL0 | Charging Current Configuration | DVDD/DGND | Digital power
ISEL1 |  | REF | Reference clock input (CMOS), 40MHz
CKESEL | Clock delay selection | DOUT/_DOUT | Serial-data outputs (CML)
NSEL | Divisor selection: “0” for 64, 2.56GHz; “1” for 32, 1.28GHz | TCK | Low-speed test clock of PLL (CMOS), 40MHz
DSEL | Input data selection: “0” for pixel array data; “1” for PRBS data | TCKH/_TCKH | High-speed test clock of PLL (CML)
TMOD | Trigger mode selection: “0” for trigger mode, 160MHz for Serializer “1” for triggerless mode, 2.56/1.28GHz for Ser |  | 
PSET | PRBS initial setting, a high-pulse signal |  | 
TVC | Control voltage test port |  | 
Total | 9 | 8+ | 
Internal in-IO | Description | Internal out-IO | Description
D<0:31> | Data from pixel array 5Mbps for trigger mode , 160Mbps for triggerless mode | CK160M | A 160MHz clock for periphery circuit
SCK160M | Sampling clock from periphery together with data 5MHz for trigger mode , 160MHz for triggerless mode |  | 

## Slide 3: Operating Mode （NSEL & TMOD）
PLL
40MHz
1.28GHz
2.56GHz
1
0
×32
×64
÷2
640MHz
1.28GHz
NSEL
÷4
÷2
÷2
÷2
320MHz 160MHz 80MHz 40MHz
40 MHz
1
160MHz 80MHz 40MHz
Ref
Div
÷2
Serializer
1
TMOD
80MHz
0
1
0
NSEL
NSEL
0
160MHz
Data SCK
32
DOUT
TMOD-NSEL | Operating Mode | Central F of PLL (Hz) | DR of data source (bps) | F of Sampling Clock (Hz) | Highest F of Ser (Hz) | DR of serial data (bps)
00 | Trigger, ×64 | 2.56G | 5M | 5M | 80M | 160M
01 | Trigger, ×32 | 1.28G |  |  |  | 
10 | Triggerless, ×64 | 2.56G | 160M | 160M | 2.56G | 5.12G
11 | Triggerless, ×32 | 1.28G |  |  | 1.28G | 2.56G
CK160M