## Slide 1: Imperfection and correction for CEPC
Yuanyuan Wei, Bin Wang, Yiwei Wang, Chenghui Yu, Yuan Zhang
The Institute of High Energy Physics, Beijing
CEPC workshop 18 Nov 2019, IHEP

## Slide 2
The sensitivity of CEPC lattice
The correction scheme
The correction results
  50mm FF quadupole misalignment
  30mm FF quadupole misalignment
Outline

## Slide 3: Lattice
E=120GeV
=363.11
=365.22
= 0.36m
= 0.0015m
=599m
=4023m
= 1.21nm

## Slide 4
Orbit amplification factor
<Δyrms> = 4.69mm
Orbit amplification factor = 4.69/50e-3 = 94
Turn off sextupoles and FF is left perfectly aligned.

## Slide 5
Quadrupole jitter sensitivity
The RMS vertical orbit distortion caused by 0.15μm quadrupole jitter is equal to beam size at 2.4pm vertical emittance.
Turn off sextupoles and FF is left perfectly aligned.

## Slide 6: Quadrupoles and sextupoles tilt sensitivity
FF is left perfectly aligned.

## Slide 7: Misalignment sensitivity
The alignments are included in the calculation now.
 | Super B LER | Super B HER | ILC DRs | KEK ATF | CEPC
Vertical emittance (pm) | 4 | 4 | 2 | 4.5 | 2.4 (0.2%couplig)
Orbit amplification factor | 46 | 44 | 32 | 21 | 94
Quadrupole jitter sensitivity (nm) | 209 | 217 | 221 | 227 | 150
Sextupole alignment sensitivity (μm) | 95 | 87 | 70 | 50 | 16
Quadrupole tilt sensitivity (μrad) | 166 | 183 | 79 | 800 | 100 (sextupoles included)

## Slide 8: Correction scheme
COD correction with sextupoles off
Turn on the sextupoles and perform COD correction again.
Dispersion correction (DFS)
Beta beating correction (LOCO)
Coupling and vertical dispersion correction (Local coupling parameter correction）.

## Slide 9: COD correction
BPMs placed at quadrupoles (~1500, 4 per betatron wave)
Horizontal correctors placed beside focusing quadrupoles（~1500）
Vertical correctors placed beside defocusing quadrupoles（~1500）
Orbit correction is applied using orbit response matrix and SVD method.

## Slide 10: Dispersion correction
Dispersion free steering principle (DFS): orbit manipulation by knob correctors.
M
rbit vector
vector
: Weight factor
A: Orbit response matrix
B: Dispersion response matrix

## Slide 11
Beta-beating correction
Correct the beta functions with sextupoles on.
Based on AT LOCO: model based correction
  Establish lattice model Mmod, multi-parameter fit to the orbit response matrix Mmeas to obtain calibrated model:
  Parameters fitted: K, KS …
  Use calibrated model to perform correction and apply to machine.
  Application to correct beta-beating, dispersion and coupled response matrix.

## Slide 12: Coupling correction
Neglecting beam-beam effects
Local coupling parameter matching was developed for BEPCII.
Both coupling and vertical dispersion are controlled.
Using the trim coils of the sextupoles (~1000), which providing skew-quadrupole field, to perform emittance tuning for CEPC.
The vertical orbit distortion due to a horizontal deflection at a BPM is:
++
, ：only related to the decoupled linear optics
: local coupling parameters
: response matrix
: skew-quadrupole vector

## Slide 13: Correction results (FF=30mm)
Component | Field error
Dipole | 0.01%
Arc Quadrupole | 0.02%
Component | x (mm) | y (mm) | z (mrad)
Arc quadrupole | 100 | 100 | 100
IR Quadrupole | 50 | 50 | 50
FF Quadrupole | 30 | 30 | 30
Sextupole | 100 | 100 | 100
COD correction

## Slide 14: Dispersion correction (FF=30mm)
decreased from
30mm to 2.9mm
Factor 10 improvement
decreased from
77mm to 0.5mm
Factor 154 improvement

## Slide 15
1/5 quadrupole (~600 out of 3000 quadrupoles) strengths are changed to restore beta functions along the ring.
Beta-beating correction (FF=30mm)
decreased from
5.7% to 0.8%
decreased
from 6.8% to 0.5%

## Slide 16: Emittance tuning (FF=30mm)
Component | Field error
Dipole | 0.01%
Arc Quadrupole | 0.02%
Component | x ((mm) | y ((mm) | z ((mrad)
Arc quadrupole | 100 | 100 | 100
IR Quadrupole | 50 | 50 | 50
FF Quadrupole | 30 | 30 | 30
Sextupole | 100 | 100 | 100
Out of 1000 seeds, 831 converged
ex = 1.2170.005 nm ey = 0.043 0.002 pm
ey/ex = (0.0035 0.0002)%

## Slide 17
DA and MA (FF=30mm)
satisfy 10170.014
>500 seeds
Tracking by Bin Wang

## Slide 18: Correction results (FF=50mm)
Component | Field error
Dipole | 0.01%
Arc Quadrupole | 0.02%
Component | x (mm) | y (mm) | z (mrad)
Arc quadrupole | 100 | 100 | 100
IR Quadrupole | 50 | 50 | 50
FF Quadrupole | 50 | 50 | 50
Sextupole | 100 | 100 | 100
COD correction

## Slide 19: Correction results (FF=50mm)
Observable | Before correction | After correction
Hori. disp. | 30.0 mm | 2.9 mm
Vert. disp. | 77.0 mm | 0.5 mm
Hori. Beta-beating | 5.7% | 0.8%
Vert. Beta-beating | 6.8% | 0.5%
Observable | Before correction | After correction
Hori. disp. | 32.3 mm | 4.9 mm
Vert. disp. | 133.7 mm | 1.0 mm
Hori. Beta-beating | 5.5% | 1.2%
Vert. Beta-beating | 10.7% | 0.9%
Component | x (mm) | y (mm) | z (mrad)
Arc quadrupole | 100 | 100 | 100
IR Quadrupole | 50 | 50 | 50
FF Quadrupole | 30 | 30 | 30
Sextupole | 100 | 100 | 100
Component | x (mm) | y (mm) | z (mrad)
Arc quadrupole | 100 | 100 | 100
IR Quadrupole | 50 | 50 | 50
FF Quadrupole | 50 | 50 | 50
Sextupole | 100 | 100 | 100

## Slide 20: Emittance tuning (FF=50mm)
Component | Field error
Dipole | 0.01%
Arc Quadrupole | 0.02%
Out of 500 seeds, 300 converged
ex = 1.2180.009 nm ey = 0.059 0.002 pm
ey/ex = = (0.0048 0.0002) %
Component | x ((mm) | y ((mm) | z ((mrad)
Arc quadrupole | 100 | 100 | 100
IR Quadrupole | 50 | 50 | 50
FF Quadrupole | 50 | 50 | 50
Sextupole | 100 | 100 | 100

## Slide 21
DA and MA (FF=50mm)
25 seeds
Tracking by Bin Wang
9180.012
More seeds need to be studied

## Slide 22: Summary
CEPC lattice is sensitive to the imperfections. Therefore, the optics correction is very challenging.
CEPC optics correction procedure was demonstrated to be effective.
With the abovementioned imperfections, both DA and MA after correction are acceptable for the on-axis injection.

## Slide 23: To do list
Study whether the tolerance of the imperfections can be relaxed.
Optimize the correction strategy to achieve finer tuning of optics.
Include more types of imperfections.
Study off-momentum correction.

## Slide 24: Thanks for your attention

## Slide 25: Case3: preliminary result (25 seeds)