## Slide 1: Development and optimization of FF superconducting magnets (Super ct-factory)
KseniIa RIabchenko
Budker Institute of Nuclear Physics Siberian Branch of Russian Academy of Science
2019

## Slide 2
OUTLINE
Super CT factory
Quad configuration
Field quality
Pole geometry
Shielding collar
Coils tolerance
Pole tolerance
Conclusion

## Slide 3
SUPER CT FACTORY IN NOVOSIBIRSK
Super Charm-Tau (CT) Factory is a double ring e+e- collider to be operated in the centre-of-mass energy range from 2 to 6 GeV, with a peak luminosity of about 1035 cm-2s-1 (Crab Waist collision) and with longitudinally polarized electrons at the IP.
This high luminosity will allow access to data samples, which are 3 orders of magnitude greater than those previously collected in any other experiments. This will provide the opportunity of a systematic study of all states of quarks of the first two generations.

## Slide 4
FF CONFIGURATION
IP
IP
QD0
QF1
Beam trajectories in FF
One of the most essential element of the Super CT FF is a dual aperture superconducting quadrupole to squeeze the beams at the IP with the following parameters:
IP
Cryostat with FF magnets
Cryostat with FF magnets
Artist view of the FF arrangement
3.3 m
Aperture radius, mm | 23
Gradient, T/m | 100
Gradient integral, T | 22
Current, kA turn | 21,5
Crossing angle, mrad | 30
Effective length, m | 0,22

## Slide 5
TASKS OF THE STUDY
We decided to produce a full scale prototype of the quad and the main tasks of the study include:
3D simulation of the quad field
Production tolerance study
Optimization of the field components
Transverse dimensions and parameters of QD0s for SCTF and FCC-ee are rather similar…

## Slide 6
Yoke
Poles
Coils
Quadrupole configuration
300,1mm
79,8 mm
151,8
133,8
17,4
54 mm
The slide shows a draft version of the vacuum chamber

## Slide 7
Field quality
X
Y
r
ϕ
Relative multipole coefficient:
All calculations were performed by the Opera program. Formula to determine the quality of the magnet. The field integrals are taken at the radius :

## Slide 8
End pole chamfer
45°
L
L
Z
chamfer
Pole/ nose piece
X
Chart: L, mm
| 0 | 3 | 5 | 7.8280000000000003
B6 | -5.8847 | -5.1611 | -3.7833 | -1.4732
B10 | -0.86188 | -0.87548 | -0.90124 | -0.94454
I = 21500 A
In order to reduce B6 harmonics, it is necessary to make end pole chamfer. After carrying out calculations with different chamfer sizes, the following dependency was obtained:
B10 harmonic varies slightly with increasing chamfer sizes, B6 harmonic can be reduced by a maximum chamfer size to 1.5 units
As you can see from the graphs, chamfers are not enough, so we continued the optimization process

## Slide 9
Pole profile
Chart: R, mm
| 22.748000000000001 | 23.5 | 26 | 29
B6 | -5.8847 | -5.0882 | -2.6057 | -0.12329
B10 | -0.86188 | -0.91885 | -0.97592 | -1.0283
I = 21500 A
If it is necessary to further reduce the harmonics, we need to modify the pole profile. For example, to reduce B6 harmonic, you can change the radius of the hyperbola of the pole.
For our case, it can be seen, that when the radius is increased by 3 mm, the magnitude of B6 harmonics decreases by 3 units

## Slide 10
Pole geometry
Based on the previously presented results, the following combination of pole geometry was chosen: the hyperbola radius was 26.6 mm and the chamfer was 5 mm.

## Slide 11
Steel for yoke
Chart: B, kGs
| 0 | 1.7 | 4 | 7.0549999999999997 | 8.3849999999999998 | 9.7089999999999996 | 11.009 | 12.269 | 13.475 | 14.615 | 15.68 | 16.655000000000001 | 17.559000000000001 | 18.367000000000001 | 19.087 | 19.718 | 20.734000000000002 | 21.452000000000002 | 22.094000000000001 | 22.318999999999999 | 22.452000000000002 | 22.542999999999999 | 22.742000000000001 | 22.888999999999999 | 23.18 | 23.631 | 24.076000000000001 | 24.701000000000001 | 26.143999999999998 | 28.547000000000001
Permendur | 1500 | 1700 | 2500 | 3528.4 | 3535.77 | 3452.77 | 3301.99 | 3103.59 | 2874.74 | 2629.57 | 2379.29 | 2132.42 | 1895.21 | 1671.94 | 1465.3 | 1276.71 | 954.86 | 702.71 | 434.14 | 311.94 | 223.2 | 159.4 | 81.36 | 58.24 | 35.4 | 21.64 | 15.68 | 11.44 | 7.27 | 4.76
Steel M 100-1200 A | 1591 | 2055.01 | 2431.1 | 2743.1 | 2989.77 | 3168.56 | 3273.53 | 3293.38 | 3210.29 | 3002.79 | 2657.03 | 2187.09 | 1649.54 | 1193.6 | 270.56 | 143.24 | 63.98 | 13.98 | 3.98
Chart: Number of integral harmonic
| 6 | 10
Permendur | 0.043192 | -0.99015
Steel M 1200-100 A | 1.8718 | -1.0153
Pole Permendur Yoke Steel M 1200-100 A | 0.073026 | -0.98955
All initial calculations were performed for a quadrupole consisting entirely of permendur. Choosing the best pole geometry, we carried out for several types of steel.
First - the calculations for the permendur quadrupole, second, the case when we replaced the permendur on the ordinary electro technical steel, and the case when the yoke is made of ordinary steel, and the poles are made of permendur.
In general, the permendur poles are enough to improve the quality of the field. So, we decided to choose this types of steel for the model.

## Slide 12: Shielding collar
There was an idea, that for shielding the action of one coil to another, it is necessary to make an iron collar. It was expected that the longer the collar, the coils would interact less.
L1
I = 21500 A
L1 – iron screen length
Chart: L1, mm
| -2 | 0 | 4 | 8 | 12 | 14 | 16 | 20 | 24 | 30 | 50
A3 | -1.3335 | -0.64702 | 0.56794 | 1.0119 | 0.76561 | 0.44681 | 0.21545 | -0.062972 | -0.20308 | -0.27968 | -0.26484
B6 | 1.6842 | 1.9309 | 2.5202 | 2.4958 | 2.4324 | 2.2256 | 2.1188 | 2.0335 | 1.9898 | 1.5982 | 1.5857
B10 | -1.1118 | -1.1126 | -1.1229 | -1.1442 | -1.0512 | -1.0538 | -1.0533 | -1.0528 | -1.0528 | -1.1587 | -1.162
A3 | L1 = 2.5 mm | L1 = 4 mm | L1 = 20 mm
I = 21500 A | 0.29 | -4.42 | -0.08
I = 10750 A | 0.56 | -5.14 | 0.05
According to calculations, we see that there is a small shield at which the A3 harmonic vanishes. Therefore, it would be better to make a small collar, but with a smaller current value, the magnitude of this harmonic changes by 5 units. In this case, there will be a need for additional harmonic correction.

## Slide 13
Single aperture vs twin-aperture
Calculations for a single and twin aperture quadrupole with a full shielding collar of 50 mm and without it were made. On this slide, you can see cross section of magnetic field in the middle of a quadrupole.
B max = 2,5 T
B min = 5 x T

## Slide 14
w/wo shielding collar
B max = 3,9 T
B max = 3,9 T
B min = 6,6 x T
B min = 2,9 x T

## Slide 15
Field quality comparison
Chart: Without collar
| 6 | 10 | 3
single aperture | 2.6328 | -0.94745 | 5.4892e-12
twin aperture | 2.6447 | -0.9556 | -0.774
Chart: With collar
| 6 | 10 | 3
single aperture | 1.9722 | -1.0429 | -3.9553e-11
twin aperture | 1.9552 | -1.0476 | -0.19565
I = 21500 A
I = 21500 A
There are practically no differences in harmonics between single and twin aperture lenses with a collar.

## Slide 16: external field with collar i
At the point of interaction is a system of solenoids. For example, an external solenoid creates a field 2 tesla. The screening solenoid (L=2,4 m) zeros the fields in the quadrupole region. There is also another solenoid – compensating (B=3 T, L=0,3 m ). Because the compensating solenoid is at close range to the quadrupole, this solenoid creates a field acting on the lens.
Solenoids edge fields in the quadrupole area:
Bs<0.01 T, Bx<0.002 T
It is necessary to introduce additional corrections in the screening area.

## Slide 17: external field with collar ii
For this reason, we made a model task: how does the external field of all solenoids affect the integral harmonics.
Compensating solenoid
Screening solenoid
Quadrupole lense
Chart: Number of integral harmonic
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
quadr+compens+screening+inner | 27.0255 | -0.64577 | 1.0028 | 0.17161
quadr+compens+screening | -4.4548 | -2.6102 | 0.44738 | 0.11718
quadr+compens | 32.452 | -2.1635 | 1.3335 | 0.087092
quadr | -0.19565 | -3.088 | 1.9552 | -1.0476
The results for the system of solenoids show that a sextupole component arises. However, this is not scary, since we can suppress these harmonics.

## Slide 18: Coils tolerance i
- distance between the conductors
Now consider the effect of coils shift on the integral harmonics. Firstly, we change the width of the conductors on one side, which, respectively, leads to a change in the distance between them. The current was not changing, but the current density was.
Chart: hone, mm
| 0 | 0.5 | 1 | 1.5 | 2 | 2.5
A3 | -0.15095 | -12.1979 | -24.7726 | -37.8626 | -51.4554 | -65.4453
A5 | 0.011013 | 4.7811 | 9.7383 | 14.8708 | 20.1658 | 25.5596
B4 | -0.019418 | 8.0999 | 16.5568 | 25.3378 | 34.4288 | 43.7092
B6 | 1.9343 | -0.65366 | -3.3375 | -6.1078 | -8.9548 | -11.8193
The harmonic A3 changes with an increase in the distance between the conductors to about 65 units. The harmonics B4 and A5 increase with increasing distance between the conductors. B6 harmonic changes to the level of -10 units.

## Slide 19: Coils tolerance Ii
Many variant of coil displacements have been studied. From the results, it can be seen that after manufacturing a quadrupole lens, it is possible to easily get rid of unwanted harmonics by this method

## Slide 20
Pole tolerance i
g – packing factor
I = 21500 A
Chart: Number of integral harmonic
| 6 | 10 | 3 | 4 | 5
g = 0 | 1.9552 | -1.0476 | -0.19565 | -3.088 | 0.021564
g = 0.9 | 4.2472 | -1.0858 | 15.7036 | 3.8491 | -0.027338
The effect of nonlinearities at the poles on the harmonics was investigated. We simulated the presence of micro cracks in one of the poles, in other words, made it laminated with a packing factor equal to 0.9.
The graph shows that in this case, the harmonic A3 from the zero level increases to 16 units. A5 from the zero level to 4. The harmonics B6 and B4 varies slightly, but B10 does not change at all

## Slide 21
Pole tolerance ii
I = 21500 A
∆L - the amount by which the pole shifts
Chart: Number of integral harmonic
| 6 | 10 | 3 | 4 | 5
dL = 0 | 1.9552 | -1.0476 | -0.19565 | -3.088 | 0.021564
dL = 0.1 mm | 1.9324 | -1.0591 | 3.0576 | -1.3101 | -2.8122
The case when the pole is rotated by a certain amount has also been considered.
By calculations it can be seen that such a shift leads to an increase in the A3 harmonic by 3 units, a change in A5 in the negative direction by 1 unit.

## Slide 22
dual aperture superconducting quadrupole
Modified Panofsky quadrupole was proposed originally by Pavel Vobly.
ADVANTAGES – transversely very compact and can be placed close to the IP to intercept the beta growth; no influence to the adjacent quad; 100 T/m can be achieved in d=26 mm; the field quality at r = 10 mm is ~
DISADVANTAGES – difficult to add correction.

## Slide 23
conclusion
3D field simulation has been done.
Geometrical parameters were chosen.
Sources of possible errors and methods to correct unwanted harmonics were found.

## Slide 24: Thanks for your attention!!!
For any questions please contact us by mails:
kseny121195@mail.ru
e.b.levichev@inp.nsk.su
a.a.starostenko@inp.nsk.su

## Slide 25: Development and optimization of FF superconducting magnets (Super ct-factory)
KseniIa RIabchenko
Budker Institute of Nuclear Physics Siberian Branch of Russian Academy of Science
2019

## Slide 26
Pole geometry
Based on the previously presented results, the following combination of pole geometry was chosen: the hyperbola radius was 26.6 mm and the chamfer was 5 mm.

## Slide 27
Steel for yoke (I=10750 A)
Chart: B, kGs
| 0 | 1.7 | 4 | 7.0549999999999997 | 8.3849999999999998 | 9.7089999999999996 | 11.009 | 12.269 | 13.475 | 14.615 | 15.68 | 16.655000000000001 | 17.559000000000001 | 18.367000000000001 | 19.087 | 19.718 | 20.734000000000002 | 21.452000000000002 | 22.094000000000001 | 22.318999999999999 | 22.452000000000002 | 22.542999999999999 | 22.742000000000001 | 22.888999999999999 | 23.18 | 23.631 | 24.076000000000001 | 24.701000000000001 | 26.143999999999998 | 28.547000000000001
Permendur | 1500 | 1700 | 2500 | 3528.4 | 3535.77 | 3452.77 | 3301.99 | 3103.59 | 2874.74 | 2629.57 | 2379.29 | 2132.42 | 1895.21 | 1671.94 | 1465.3 | 1276.71 | 954.86 | 702.71 | 434.14 | 311.94 | 223.2 | 159.4 | 81.36 | 58.24 | 35.4 | 21.64 | 15.68 | 11.44 | 7.27 | 4.76
Steel M 100-1200 A | 1591 | 2055.01 | 2431.1 | 2743.1 | 2989.77 | 3168.56 | 3273.53 | 3293.38 | 3210.29 | 3002.79 | 2657.03 | 2187.09 | 1649.54 | 1193.6 | 270.56 | 143.24 | 63.98 | 13.98 | 3.98
Chart: I = 10750 A
| 6 | 10
Permendur | -2.434 | -0.94425
Steel M 1200-100 A | -2.4169 | -0.94449
Pole Permendur Yoke Steel M 1200-100 A | -2.4322 | -0.94426

## Slide 28: Coils tolerance I
- distance between points A to B
Chart: h4, mm
| 0 | 0.25 | 0.5 | 0.75 | 1 | 1.25
B3 | 0.051452 | -30.3139 | -45.3347 | -60.2768 | -75.2277 | -90.1484
B4 | -0.019418 | 17.9894 | 27.1536 | 36.4019 | 45.7836 | 55.258
B5 | 0.019963 | -8.8373 | -13.4747 | -18.2373 | -23.1406 | -28.1624
B6 | 1.9343 | 5.7134 | 7.7545 | 9.892 | 12.1269 | 14.4521
The effect of changing the thickness of the upper conductors and the distance between points A to B on the integral harmonics.

## Slide 29: Coils tolerance ii
- thickness of the one lateral conductor
Chart: hone, mm
| 0 | 0.25 | 0.5 | 1
A3 | -0.15095 | -20.8972 | -43.3423 | -90.9548
A5 | 0.011013 | 9.0504 | 18.2564 | 36.6062
B4 | -0.019418 | 15.245 | 31.2219 | 63.9642
B6 | 1.9343 | -3.3293 | -8.5985 | -18.7395
The effect offset down the one lateral conductor on the integral harmonics.

## Slide 30: Coils tolerance Iv
- distance between the conductors
Chart: h2, mm
| 0 | 0.5 | 1 | 1.5 | 2 | 2.5
B4 | -0.019418 | 16.3206 | 33.382 | 50.98 | 69.3547 | 88.3725
B6 | 1.9343 | -3.2322 | -8.6378 | -14.2119 | -19.9632 | -25.8616
The effect of changing the thickness of symmetrical side conductors and the distance between them on the integral harmonics.

## Slide 31: Coils tolerance v
- distance between the conductors
Chart: h3, mm
| 0 | 0.5 | 1 | 1.5 | 2 | 2.5
B3 | 0.051452 | 24.588 | 37.661 | 51.2355 | 65.2976 | 79.8332
B4 | -0.019418 | -16.5642 | -25.3291 | -34.402 | -43.7675 | -53.41
B5 | 0.019963 | 9.7102 | 14.8305 | 20.1117 | 25.5401 | 31.1019
B6 | 1.9343 | -3.3192 | -6.0825 | -8.9214 | -11.8253 | -14.7837
The effect of changing the thickness of the upper conductors and the distance between them on the integral harmonics.

## Slide 32
Coils tolerance Vi
- height at which the upper conductors fall
Chart: h5, mm
| 0 | 0.25 | 0.5 | 1
A3 | -0.15095 | -0.013286 | 0.1443 | 0.46514
B3 | -3.4076e-11 | -2.3068 | -4.93 | -11.249
B4 | -1.245 | 0.83526 | 1.8404 | 4.3595
B6 | 1.9343 | 1.8511 | 1.7533 | 1.5227
The effect of changing the height of the position of the upper conductors on the integral harmonics.

## Slide 33
Coils tolerance Vii
- distance between the conductors
Chart: h6, mm
| 0 | 0.5 | 1 | 1.5 | 2 | 2.5
B4 | -0.019418 | -15.8788 | -32.8326 | -50.4871 | -68.8189 | -87.8036
B6 | 1.9343 | -3.3979 | -8.7862 | -14.3634 | -20.1109 | -26.0092
The effect of changing the thickness of symmetrical upper conductors and the distance between them on the integral harmonics.

## Slide 34
Pole tolerance
I = 21500 A
Chart: Number of integral harmonic
| 6 | 10 | 3
permendure | 1.9552 | -1.0476 | -0.19565
permendure 10% | 0.36626 | -1.0391 | -0.23769
The effect of steel quality change by 10% on the integral harmonics.

## Slide 35: Calculation of some parameters
B, T | 2
V (coil), m^3 | 7593,6
G, T/m | 100
E, Gev | 1÷2,5
The quadrupole lens parameters such as magnetic field energy and normalized quadrupole strength were evaluated:
N
N
S
S
y
x
B