## Slide 1: DMM & TMM: the Double and Triple Micro-Mesh gaseous structures for ultra-low ion-backflow applications
Zhiyong Zhang
For the USTC MPGD group
State Key Laboratory of Particle Detection and Electronics, China
University of Science and Technology of China
CEPC 2019, Beijing
Nov.18, 2019

## Slide 2: Outline
  Motivation
Double Micro-Mesh gaseous structure
  Design and Fabrication
  Performance Characterization
  Optimization for further IBF suppression
  Triple Micro-Mesh gaseous structure
    Design and performance study
  Summary

## Slide 3: Motivation : GPD
  Gaseous Photon Detectors (GPD) with MPGD
    large area, high spatial and timing resolution, resistant to magnetic field, IBF suppression, low cost …
  Challenges
    High gain: to be sensitive to single photons
    Very low IBF
UV light：CsI，~mC/cm2
Visible light：Bi-alkali, ~μC/cm2 ！
Gas-PMT
PIC-SEC
A. Lyashenko et al. , NIM A 598(2009) 116-120
F-R-MHSP+GEM+MHSP
IBF: 0.03%
Complex structure

## Slide 4: Motivation: TPC
CEPC
  Application of TPC in high-rate environments: ALICE upgrade, ILD, CEPC …
    Very low IBF is the key: to minimize drift field distortion caused by ion space charge
    Continuous readout to keep up with high event rate
ALICE
Quadruple GEM, IBF < 1%
GEM+MM, Gain×IBF<~5
IBF <~ 0.1% required
MPGD is the only solution so far. The IBF still need to be further reduced.

## Slide 5
DMM Design
“Piggyback”
~0.2 mm
~0.1 mm
PA
SA
Drift region
DMM: Double Micro-Mesh gaseous structure
Hole-type → mesh-type : to strongly reduce IBF
Double mesh: cascading avalanche for high gain
Stacked two meshes
Gap between the stacked meshes: 200-300um, serving as pre-amplification (PA)
Gap between the bottom mesh and anode: 50-100um as secondary amplification (SA)
Allows to achieve very high gain, and yet significantly reduce ion back-flow.
~3-5 mm

## Slide 6: DMM Fabrication
  DMM is fabricated with the thermal bonding technique that has been developed at USTC.
  Micromegas fabrication process with thermal bonding technique
  A 2.5cm×2.5cm DMM prototype
More details:
Thermal bonding method for fabricating Micromegas detectors and its applications (arXiv:1910.03170）
A Thermal-Bonding Method for Fabrication of Micromegas and its applications, MPGD2019, 5-10 May 2019, La Rochelle, France.
Φ1mm spacer
10mm spacer pitch
150mm×150mm
Transferred to PCB by pre-heating
Thermal bonding
Cutting mesh
Assembling

## Slide 7: Gas Gain and Energy Resolution with 55Fe
PA+SA 19.1%
PA+SA
PA alone
Gain: PA, SA and combined
Resolution: PA and PA+SA combined
A typical 55Fe energy spectrum
Combined gain can reach up to 7×104 for 5.9 keV X-rays.
Combined resolution remains almost constant and is close to PA-alone resolution, suggesting a close-to-full collection of primary electrons for the high-voltage configurations we used.
PA+SA
SA alone
PA alone

## Slide 8: Previous results and validation
Gain measured with X-ray energy spectrum (Qfull-energy peak/QPrimary) is consistent with IAnode/IPrimary .
No ion space charge effect is confirmed in the DMM test.
  Up to 3×106 gain for single electrons
  down to 0.05% IBF
More details:
A high-gain, low ion-backflow double micro-mesh gaseous structure for single electron detection， NIM-A , 889 (2018) 78–82.
Study on the double micro-mesh gaseous structure (DMM) as a photon detector, https://doi.org/10.1016/j.nima.2019.03.033.
https://indico.cern.ch/event/757322/contributions/3387079/attachments/1840422/3017748/DMM-MPGD2019.pdf
Also in backup slides

## Slide 9: Can we further lower the IBF?
Obviously, the IBF is depend on the geometry of the detector structure, in which the alignment, density, distance etc. of two meshes can be optimized.
  Two meshes are perfectly aligned
  Two meshes are maximally mis-aligned
Colas P, Giomataris I, Lepeltier V. Ion backflow in the Micromegas TPC for the future linear collider, Nuclear Instruments and Methods in Physics Research Section A, 2004, 535(1-2): 226-230.
It suggests to increase the size of the ion cloud (σ) and decrease the mesh pitch (I)
To enlarge PA gap and mesh density in DMM

## Slide 10: Optimization for Low IBF
  It’s impractical to make any precise alignment of the two meshes. So setting the two meshes with a crossing angle is a practical way to ensure their mis-alignment.

## Slide 11: Optimization for Extremely Low IBF
500 vs. 650 LPI (same opening rate)
PA gap: from 160 to 240 μm
Larger gap increase the transverse diffusion of avalanche
Higher mesh density decrease the mesh pitch
Both of these increase the σ/l value, optimizing the IBF as a consequent.

## Slide 12: Optimization Outcome For DMM
To push IBF down to an extremely low level:
low PA electric field
large PA gap
high mesh density
crossing mesh setting
A IBF ratio down to ~0.025%, which has been improved with a factor of 2 compared with that before optimization.

## Slide 13: Optimization Outcome for DMM
Define IBF ratio ×gain as ε:
ε = 5
This result fulfill the requirement of ε < 5 in the R&D of CEPC TPC， even operated in higher gain of >10000 is possible to improve the S/N.

## Slide 14: Can the IBF be lower?
For the case of DMM, when we set PA at 550V and switch off SA, the Idrift/Iprimary was measured at ~1.3
Drift cathode (0V)
Pre-mesh (+HV)
Sec-mesh (+HV)
Anode (same to Sec-mesh)
So, adding another mesh on the DMM to suppress the SA ions is a easy option.
Let’s go to TMM
It means that the PA only contributes ~0.3 for the ε factor, the SA dominates the total IBF

## Slide 15
TMM Design
TMM: Triple Micro-Mesh gaseous structure
One more mesh on the DMM
More stable gain, lower IBF from second avalanche…
Stacked three meshes
Gap between the 1st and 2nd meshes: 200-300um, serving as pre-amplification (PA)
Gap between the 2nd and 3rd meshes : 200-300um as secondary amplification (SA)
Gap between the bottom mesh and anode: 50-100um as secondary amplification (TA)
~0.2 mm
~0.1 mm
PA
TA
Drift region
~3-5 mm
SA
~0.2 mm
“Piggyback +”

## Slide 16: Gain and energy resolution
Gas gain reaches up to for 5.9 keV X-rays
Energy resolution at ~21% (FWHM) indicates a high collection efficiency of the primary electrons

## Slide 17: IBF measurement for TMM
    The back-flow ions (at ε = ~0.3) is mainly from PA, concluding that the IBF can not be further reduced by adding more meshes, the TMM reaches the lowest IBF level for the mesh-type structure.
ε = ~0.3
~0.003% IBF

## Slide 18: To optimize
PA and TA voltages are fixed at 650V and 530V, this plot shows the combined gain changes with the variation of SA voltages
PA
TA
Drift region
SA
    Combined gain = PA gain × SA trans × SA gain × TA trans × TA gain

## Slide 19: Towards large area
It is a crucial issue for the DMM (TMM) is to make a large area for real experiments
Bulk etching method does not work well in the DMM due to the large thickness of 100um (SA) + 200um(PA) regions, but it will not be a problem for the thermal bonding method
Bulk etching
UV light exposure
Spacer setting
Mesh bonding
Spacer setting
Mesh bonding
A 150mm ×150mm DMM prototype is fabricated and under testing…
Thermal bonding

## Slide 20: Summary
Developed the DMM &TMM featuring high gain and low IBF
Demonstrated the performance of DMM &TMM with small-size prototypes:
  Gain: 7×104 for 5.9 keV X-rays and 3×106 for single electrons.
  IBF ratio: down to ~ 0.03% for DMM, ~ 0.003% for TMM
  Verified the feasibility of fabricating large area detectors
Potential applications
  Gaseous photon detectors
  High-rate TPC readout
  Many others…

## Slide 21: Summary
Developed the DMM &TMM featuring high gain and low IBF
Demonstrated the performance of DMM &TMM with small-size prototypes:
  Gain: 7×104 for 5.9 keV X-rays and 3×106 for single electrons.
  IBF ratio: down to ~ 0.03% for DMM, ~ 0.003% for TMM
  Verified the feasibility of fabricating large area detectors
Potential applications
  Gaseous photon detectors
  High-rate TPC readout
  Many others…
Thank you!

## Slide 22: Back-up

## Slide 23: Electron Transparency
  Transparencies for electrons passing through PA and SA meshes are extracted by measuring PA, SA and total (PA and SA combined, DMM) gas gains
    Combined gain = PA gain × SA trans × SA gain
SA trans ~ 15% @ ESA/EPA ~ 1
PA relative transparency
SA transparency
EPA/Edrift is set to 200 to maximize transparency most of the time.

## Slide 24: Ion Back-Flow (IBF) Measurement
Drift cathode (-HV)
Pre-mesh (-HV)
Sec-mesh (-HV)
Drift cathode (0V)
Pre-mesh (+HV)
Sec-mesh (+HV)
Anode (+HV)
Anode (0V)
IBF ratio = (IDrift - IPrimary)/IAnode
Keithley (6482) Picoammeter with ~10-fA resolution in a range of ±20 nA
IAnode
IDrift, IPrimary(no avalanche)

## Slide 25
Single GEM
  Our IBF measurements are reliable in terms of ion space-charge effect (impact is negligible).
Ion Space-Charge Effect
Conditions for our IBF measurement
M Ball et al 2014 JINST 9 C04025

## Slide 26: Validation of IBF Measurement
IBF ratios measured with 55Fe and X-ray tube are consistent
Gain measured with X-ray energy spectrum (Qfull-energy peak/QPrimary) consistent with IAnode/IPrimay
Qfull-energy peak/QPrimary= IAnode/IPrimay
IAnode stays proportional to X-ray intensity in a rather wide range, suggesting no gas gain saturation in the IBF measurement.
no gas gain saturation

## Slide 27: Performance Characterization
  DMM with Ar (93%) + CO2 (7%)
    Electron transparency
    Energy resolution and gas gain
    Ion back-flow ratio
  DMM with Ne (80%) + CF4 (10%) + C2H6 (10%)
    Single photon electron response
0.24 mm
0.12 mm
PA
SA
Drift region
3 mm
Mesh specs
500 LPI, 27um thick, 40% opening rate

## Slide 28: Sec-amplification (SA)
Full energy peak due to the lateral angle photoelectrons and Auger electrons
The transparency should be similar to PA’s, since their have the same mesh type.
Avalanche (-HV)
Drift (-HV )
Anode (0V)
~240um
~120um
Gain VS avalanche voltages
up to 2ᵡ104