## Slide 1: MOST2 PLL_Ser Design Review
Xiaoting Li
IHEP
April 30, 2019

## Slide 2: Outline
Requirement
  32-bit-input data, output data rate: 160Mbps@trigger, 4Gbps@triggerless
  Data valid flag
  Low power consumption
PLL Design and simulation
  Design A (in pixel chip)
    2.56GHz, ~ -100dBc/Hz@1MHz offset（Divisor N is 64）
    1.28GHz（N is 32）
    160MHz/80MHz output clock for periphery @triggerless mode ---- CKOUT
  Design B (test block)
    2.24GHz（N is 56）
    140MHz CKOUT
Serializer Design and simulation
  5.12Gbps is hard to realize by using 180nm process
  4.48Gbps seems to work at worst case in the preliminary simulation
  3.84Gbps

## Slide 3: Requirement
Data rate
  SFR structure: DR=Fpll, 4Gbps requires a 4GHz clock
  Tree structure (2:1): DR=2Fpll, a 2GHz clock is enough
Data valid flag
  D31 ---- When D31 is high, data is valid
Low power consumption

## Slide 4: Top sch of PLL_Ser
Control bits (7)
  BSEL, ISEL0, ISEL1, NSEL, TMOD, DSEL, CKESEL
Reset signal for test module
  PSET (high  reset)
Input
  REF
Output
  DOUT/_DOUT
Test
  TVC, TCK
Power
  AVDD/AGND, DVDD/DGND
Inner interface
  D<0:31>, SCK, CKOUT

## Slide 5: Operating mode (Design A)
TMOD-NSEL | Operating Mode | CKOUT (Hz) | D<0:31> (bps) | SCK (Hz) | SerCK (Hz) | Serial DOUT (bps)
0-x | Trigger | ---- | 5M | 5M | 80M | 160M
1-0 | Triggerless, ×64 | 160M | 160M | 160M | 2.56G | 5.12G
1-1 | Triggerless, ×32 | 80M | 80M | 80M | 1.28G | 2.56G

## Slide 6: PLL Design A
420×450 μm2
NSEL: 02.56GHz, 11.28GHz
ISEL1/ISEL0: 00/01/10/11  25/50/75/100μA
BSEL： 03kΩ, 18kΩ
TMOD: 0Trigger, 1Triggerless

## Slide 7: VCO post-simulation
Test bench B
Test bench A
Test bench A
  VF-Curve
  Phase noise
Test bench B
  Max frequency
  Function
  Single-end output swing of VCO and CMLby2
  Duty cycle

## Slide 8: VCO post-sim @ SS 85℃
Tuning range @ SS 85
  280MHz ~ 2.96GHz
Current range @ SS 85
  3.57mA ~ 16.46mA
Phase noise
  ~ -100dBc/Hz@1MHz offset
Current @ 2.56GHz & FF -40
  16.09mA
Current range @ FF -40
  6.85mA ~ 26.26mA

## Slide 9: VCO post-sim: VF-Curve, Kvco and Loop specs
C1: 3pF, C2: 120pF, R2: 3kΩ/8kΩ
Control bits: NSEL-ISEL1-ISEL0-BSEL

## Slide 10: Open loop response bode plot
Different N
Different charging current
Different Kvco

## Slide 11: PLL simulation
Half-post simulation
TT 27℃, 1-0110:
  triggerless
  Fpll=2.56GHz
  Icp=100μA
  LBW=1.5~2.5MHz
  ΔF = 117.5MHz, ΔT = 17ps, ΔVC =55mV @4μs
FF -40℃, 0-1110:
  trigger
  Fpll=1.28GHz
  Icp=100μA
  LBW=3~5MHz
SS 85℃, 1-0000:
  triggerless
  Fpll=2.56GHz
  Icp=25μA
  LBW=0.5~0.8MHz
Pre-simulation (7 corners)
  ΔF < 20MHz
  ΔT < 3ps
  ΔVC < 7mV
  Ipll=25mA @ 2.56G & FF 85
  Ipll=19.5mA @ 2.56G & TT 27

## Slide 12: PLL Design B ---- Divby28
Why the divisor is 28?
  4Gbps purpose
  Max frequency of divider
  50% Duty cycle
N should be integral multiple of 8
  64/56/48/40/32?
  2.56G/2.24/1.92/1.6/1.28G
  56=2*28=2*2*7*2
Passed pre-simulations
Post-simulations are ongoing
Other blocks of PLL are remained

## Slide 13: 32:1 Serializer Design
Timing
  Stage timing
    Data sampling
  Unit timing
    Data sampling (Dx--CKP)
    MUX (_Dxm--CLK)
  1UI = 500ps @ 2Gbps
    Time margin is very small at high speed
    Delay of data and clock
Big-small eye in eye diagram
  50% DC of clock

## Slide 14: 2:1 unit pre-simulation @2.3GHz-4.6Gbps
Data sampling
MUX timing
↑SS85
↓FF-40
Serialized correctly

## Slide 15: Data sampling and self testing
When data is invalid, that is D31 is low
  Hold the previous data
SYNCK (Fpll/8) and CKESEL
  Placing CKESEL (clock edge selection) in the first stage of Serializer maybe better
DSEL, select the data source
  0  pixel array data
  1  PRBS data
PRBS initial value
  1111 1110 1111 1110 1111 1110 1111 1110 0000 0100 0000 0100 0000 0100 0000 0100…

## Slide 16: Summary
Total current is less than 85mA (estimate)
Done/almost done
  PLL
  PLL_test (post-simulations of divby28, and simulations of whole PLL)
Ongoing
  Serializer (more pre-simulations, layout, and post-sim)
  PRBS-Gen (layout and post-sim)
Unfinished
  CML Driver
  Layout of PLL+Ser
  Test block with PAD (layout)
Thank you!